## Slide 1: HL-LHC PLC and TC Decisions in 2014 and 2015
O. Brüning, Paolo Fessia, Markus Zerlauth on behalf of the HL-LHC TCC team
2nd HL-LHC TCC, February 11, 2016

## Slide 2: HL-LHC PLC / TC Main Topics in 2014
February: D1 length reduction, RLIUP follow-up (parameters),
specifications
April: Crab Cavity integration (SPS cryostat), Optics V1.1,
TAS aperture @ 27mm or 30mm
June: Layout IR1&5, parameter update,
Superconducting Link & surface space
August: Baseline parameters, triplet corrector specs
October: movable TAN roadmap, revised layout, Q5 in IR6,
cold-mass configuration for Q5, Sextupoles @ Q10,
‘ultimate’ HL-LHC parameters

## Slide 3: HL-LHC PLC / TC Main Topics in 2015
January: BBLR Roadmap, triplet interconnection length,
feedback from MQXF review and cold box in TX46
March: 80 bunch scheme, 11T baseline, TAXN,
Glossary update, new triplet magnet length
July: Vibration studies and LRBB wire compensation
June: Ion parameters and schedule; Double Decker CE,
Schedule
September: Collimation roadmap
November: Heat Load, ion beam parameters, BS temperature,
TAS

## Slide 4: HL-LHC PLC Main Decisions
February 2014:
-Added injection parameters to HL-LHC baseline parameters
-D1 length from 6.7m to 6.3m and field from 5.2T to 5.6T
April 2014:
-New Crab Cavity layout with SPS cryostat option
-Optics V1.1
-TAS aperture reduction from 30mm to 27mm and
 later in October increased again to 30mm
June 2014:
-Temperature for all magnets (Q1-Q6) @ 1.9K
-Parameter update (RF curvature, BCMS and 50ns
 later removed and replaced by 8b4e)

## Slide 5: HL-LHC PLC Main Decisions
October 2014:
-Maintain the add. Q5 in IR6 and the MS at Q10 as baseline
January 2015:
-Endorsement for BPMS @ Q1 [inside exp. Cavern tbc]
-Temperature for all magnets (Q1-Q6) @ 1.9K
 Q6 still to be confirmed!!!
-Parameter update (RF curvature, BCMS)
March 2015:
-New triplet length and gradient (MQXF review):
4.2m & 7.15m @ 132.6T/m
-Tungsten TAXN fixed aperture & TCLX, mini TAXN in IR8
-Staged CC installation in LS3 and LS4 following the C&S R
-80bunch PS scheme adopted as option

## Slide 6: HL-LHC PLC / TC Main Decisions
October 2015:
-SPS Crab Cavity test in LSS6
June 2015:
-Decision to move most equipment underground
 Double Decker solution and new schedule
-Required Ion parameters for ALICE upgrade and approval of
equal luminosity sharing scenario
-Approval of Q5 layout in IR6 but with request for follow-up
by Cold Powering WP.
August 2015:
-Removed 50ns and 8b4e approved as 25ns backup scheme
September 2015:
-CLIQ and heaters for triplet magnet protection

## Slide 7
Run 2
Run 3
Run 4
LS 2
LS 3
LS 4
LS 5
Run 5
LHC schedule approved by CERN management and LHC experiments spokespersons and technical coordinators (December 2013)
LS2 starting in 2018 (July) => 18 months + 3 months BC
LS3 LHC: starting in 2023 => 30 months + 3 months BC
Injectors: in 2024 => 13 months + 3 months BC
LHC schedule beyond LS1
Beam commissioning
Technical stop
Shutdown
Physics
Run 2
Run 3
Run 4
LS 2
LS 3
LS 4
LS 5
Run 5
(Extended) Year End Technical Stop: (E)YETS
EYETS
YETS
YETS
YETS
YETS
YETS
300 fb-1
Goal of 3’000 fb-1 by mid 2030ies
30 fb-1

## Slide 8: HL-LHC PLC Main Decisions
November 2015:
-New HL-LHC TCC committee structure and project office
December 2015:
-Q1 to D1 magnets @ 1.9K with BST @ 40-60K
-D2 up to Q6 magnets @ 1.9K with BST @ 4.5-20K
October 2015:
-2kA to 600A and length change for the D2 and Q4 correctors
-Change Q4 current from 16kA to 5kA
-Q4 gradient of 120 T/m and length of 3.67m
-Q4 aperture to remain at 90mm
-Q6 temperature from 1.9K to 4.5K  tbc!
-Approval and publication of magnet circuit table

## Slide 9: Outstanding Issues
Vacuum IR2 and IR8:
-Evaluate coating options for low SEY (a-C is baseline)
Mobile Cryo Plant in IR4:
-official approval missing
Q6 temperature confirmation:
-official approval missing
Finalizing Q1 BPM integration:
-finalize integration, valves positions  experiment approval
Beam-Beam:
-Validation of LRBB wire positions and alternative
compensation via electron beams
High lumi LHCb integration into HL-LHC

## Slide 10: Outstanding Issues
Collimation system:
  -Quench tests in the LHC
   adoption of bump method for IR1/5
   adoption of empty cryostat option for IR2
   adoption of 11T magnet DS collimators for IR7
   still requires official approval
Triplet and Matching Section Quadrupole magnets:
  -Decision on single versus double circuit solution
  -Determination of leak current tolerances from WP2 (R)
  -Option of 2-Quadrant power supplies for triplet magnets
  -IPQ protection still needs to be confirmed (CLIQ / QH)
  -Q5 in P6
  -Aperture (tolerances)
  -ATS new version & correction scheme validation

## Slide 11: Outstanding Issues
Crab Cavities:
-Radiation impact still needs to be finalized
Corrector magnets for D2 / Q4:
-Still need studying and confirmation
Triplet area radiation:
-ALARA and intervention scenarios and planning
Configuration Baseline changes and Decisions on Configuration, Quality and Resource Officer Page
D1 – D2 powering:
  -Powering D1-D2 magnets in series