## Slide 1: Topics from the 2016 Chamonix Workshop with relevance for the HL-LHC project
G. Arduini, O. Brüning, Y. Papaphilippou, L. Rossi,
S. Redaelli, G. Vandoni, J. Wenninger, M. Zerlauth
2nd HL-LHC TCC, February 11, 2016

## Slide 2: Chamonix Sessions
Monday: Session 1 - Lessons from 2015 Operations
(operations, efficiency, MPT, Coll, RF& ADT, circuits)
Session 2 - Key Challenges for Operation
(UFOs, ULO, BLMs, e-cloud, Z heating & instabilities, SPS, BI)
Tuesday: Session 3 - LHC Hardware Performance
(Fault tracking, availability, Cryo, QPS, circuits, PC)
Session 4 - LHC Hardware Performance
(LBDS, RF& ADT, BI, Tech Infra, R2E,  7 TeV)
Wednesday: Session 5 - 2016 and Run 2
(YETS recovery, Exp expect, b*, injectors, ion run, MDs, plans)
Session 6 - LIU
Thursday: Session 7 – HL-LHC
Session 8 – LS2
Friday: C-MAC closeout

## Slide 3: Chamonix 2016: Monday Sessions
2015 operation and challenges:
e growth: non-colliding bunches close to preservation /
colliding bunches show large scatter around ≈ 15%/h @ FT
2% beam loss during cycle (1%)  up to 10 MJ for HL-LHC
33% of time in Stable Beam after TS2 (need ≈ 40%)
Only ⅓ of fills terminated by operators (HL-LHC ++) (UFOs!)
Collimation good and robust
Quenches: D3 OK @ 6.5 TeV  7 TeV?
Quenches: IPQs as above
Quenches: slower than expected training to 7 TeV wrt SM18
 expect ca. 1000 training quenches to 7 TeV start of RunI
 expect now half of that: ca. 500, ⅓ already done!
 secondary quenches might be higher though
Different cryo heat load in the LHC sectors: 2 families
Instabilities: have all diagnostics that is necessary  WBFB?
Notes: Losses at top energy are up to 1%. More importantly, I think that this was a very relaxed loss scenario that can become worst when the machine is pushed.

## Slide 4: Chamonix 2016: Tuesday & Wednesday
Tuesday - Hardware Performance:
Fault Tracker Tool  Asset for HL-LHC!!!
 ca. 28fb-1 for 2016 and 183 fb-1 for HL-LHC with 2015 stats
 can help in identifying priority for upgrades!
# Cryo: can one aim for > 93-95% availability
# QPS  possibility of full redundancy (≈ 5MCHF)
Wednesday - 2016 Goals and Configurations:
Experiments would like to have ca. 30fb-1
b* between 40cm and 50cm with tighter coll and phase adjust
Heavy Ion physics request not decided
Operation experience with new TDIS design
HL-LHC related MD requests:
-Full RF detuning operation
-Collimation: halo control, Z, efficiency, quench limits..
-ATS commissioning (2 and single IR squeezed)
-x = 0.03 measured in MDs (0.04 with noise and bad lifetime)

## Slide 5: Chamonix 2016: Thursday Sessions
HL-LHC @ Chamonix:
E-cloud heat load ≈ constant for above nominal intensities
 HL-LHC is OK if LHC can be conditioned to nominal
Need to decide on in-situ triplet (IPQ) coating [aC or laser]
RF Coupler lifetime of ca. 15y  impact for HL-LHC?
200MHz sub harmonic RF system
 when and based on what should we take a decision?
 observation that LIU could meet HL-LHC parameters with
longer bunches [presentation by Brennan]
SPS Crab Cavity tests: tight schedule but OK  SM18 ready!!!
Quench tests in LHC  Collimation Baseline configuration:
11T for P7, empty cryostat coll. For P2; bumps for P1/P5
Still pending some material/coating choice  need ECRs!
Vibration studies  interesting summary  feet reinforcement
Pb ion parameters now ‘only’ 30-40% short of ALICE needs!
Crystal collimation feasible for Pb operation?
Notes: I would recall that the solution for reducing the collimator impedance is still pending some material/coating choice validation

## Slide 6: Chamonix 2016: Friday C-MAC
C-MAC closeout points:
Congrats to all teams
30fb-1 requires more time in Stable Beams
 review number and length of TS
Estimate sources for e growth (injection and FT)
Look into possibility of WBFB for HL-LHC
Develop further the doublet beams for scrubbing
Study options and strategy for cryo availability > 98%
Magnet training campaign should not come before end 2016
Perform a risk assessment of a training campaign based on
experience with one or two sectors
Difference between LIU and HL-LHC parameters!
Risk analysis for aging RF components
Prepare procedures and criteria for how decisions will / should
be taken for the various options (e.g. RF, coating etc.)