## Slide 1: Relative Biological Efficiency of Antiprotons The AD-4 ACE Experiment Michael H. Holzscheiter University of New Mexico, Albuquerque
Introduction and historical background
Phase I – Biological Effective Dose Ratio (BEDR) Summary of results
Phase II – Relative Biological Efficiency (RBE) Experimental Methods Biology meets Physics – Problems and Issues Data Analysis and Error Discussions Final Results
Summary Missing items? Future tasks? Lessons learned?

## Slide 2: Historical Background
Heavy Charged Particles proposed for cancer treatment by Robert Wilson in 1946 (R R Wilson; Radiology 47 (1946) pp. 487 – 491)
“Higher-energy machines are now under construction, however, and the ions from them will in general be energetic enough to have a range in tissue comparable to body dimensions. It must have occurred to many people that the particles themselves now become of considerable therapeutic interest.”
“The object of this paper is to acquaint medical and biological workers with some of the physical properties and possibilities of such rays.”
Wilson already includes all essential elements: Straggling in target, ionization density, relative biological effectiveness, and the benefits and dangers of using heavier particles.
Initial work at Berkeley laid foundation for cancer treatment with heavy ions (C, Ne, Ar), but only proton treatment survived the funding cuts by NSF and NIH.
Luckily two post docs involved in the work at Berkeley (G. Kraft and H. Tsujii) took the knowledge home to Europe and Japan allowing the development of carbon ion therapy.

## Slide 3
Historical Background II
More exotic particles were proposed early on:
Pion Therapy was established at Los Alamos, SIN, and TRIUMF. Enhancements in therapeutical efficiency was expected due to annihilation of pions (Star formation). Pion Therapy eventually faded away due to poor spatial conformity of high dose region.
S.B. Curtis and M.R. Raju; Rad. Res. 34 (1968) 239-255
LANL: 227 patients 1974 – 81 SIN: 126 patients 1982 - 84
TRIUMF: 1982 - 85 randomized trials of pions versus photons
Antiproton Therapy was first proposed in 1984 by L. Gray and T. Kalogeropoulos: High concentration of dose around annihilation vertex predicted. (Rad. Res. 97 (1984) 246-252).
A. Sullivan, CERN: Measured relative energy deposition antiproton to proton: ONLY 30 MeV of 1.9 GeV deposited in target – BUT THAT’s FACTOR OF TWO

## Slide 4
Letter of Intent I-225 submitted August 2002
Proposal PS-324 submitted October 2002 and accepted February 2003.
MINUTES OF THE 162nd MEETING OF THE RESEARCH BOARD:
6. REPORTS AND MATTERS ARISING FROM THE SPSC MEETING OF 14 JANUARY 2003:
K. Königsmann reported on the recent meeting of the SPSC. He first discussed proposal
P324, to study the biological effectiveness of antiprotons for cancer treatment [12]. The
experiment involves exposing cells to the antiproton beam from the AD, and measuring
their survival fraction as a function of the position in the target. ……….
The Research Board approved the experiment for 9 shifts…….The experiment is to be
known as AD-4.
The birth of AD-4 ACE
AD-4 ran at 46.7 MeV for 17 individual shifts between June 2003 and November 2004. No absolute dosimetry of antiproton beam Measured relative biological effect Peak-to-Plateau compared to protons (BEDR)
We have produced the first measurements of the biological consequences of antiproton irradiation. These data substantiate theoretical predictions of the biological effects of antiproton annihilation within the Bragg peak, and suggest antiprotons warrant further investigation. “Antiprotons are 4x times more powerful in killing cancer cells.”

## Slide 5
INGREDIENTS:
V-79 Chinese Hamster cells embedded in gelatin
Antiproton beam from AD (46.7 MeV)
METHOD:
Irradiate cells for prescribed fluencies to give dose values where survival in the peak is between 0 and 90 %
Slice samples, dissolve gel, incubate cells, and look for number of colonies
ANALYSIS:
Study survival vs. dose in peak and plateau and compare to protons
(and carbon ions)
AD-4 ACE Phase I

## Slide 6
AD-4 ACE Phase I - Results
From: M.H. Holzscheiter et al. / Radiotherapy and Oncology 81 (2006) 233–242

## Slide 7
From: M.H. Holzscheiter et al. / Radiotherapy and Oncology 81 (2006) 233–242
AD-4 ACE Phase I - Results

## Slide 8
AD-4 ACE Phase II
Goals:
Build clinically relevant Spread Out Bragg Peak (SOBP) Penetration in Target ≈ 10 cm/Width of SOBP ≈ 1 cm.
Include absolute Dosimetry in order to measure Relative Biological Efficiency (RBE) which then can be used for dose planning excercises.
Requirements to AD:
Increase beam energy to 500 MeV/c (126 MeV kinetic)
Resulting in fewer but longer shifts due to more difficult switch-over of accelerator

## Slide 9
AD-4 ACE Phase II – Experimental Set-Up
Minor, but essential, changes:
Mimotera for shot-by-shot beam monitoring
Calibrated Ion Chamber for Dosimetry
EBT-2 Film on Tank for Beam Profile
Automated 7-Step Degrader System

## Slide 10: Relative Biological Effect
SF0.1
3.31 Gy
SF0.1
5.17 Gy
RBE0.1 1.56
= ratio of DOSE of reference radiation to dose of test radiation producing same BIOLOGICAL EFFECT

## Slide 11
Measuring RBE requires Dose and Biological Effect
Biological Effect:
Embed cells in gelatin matrix inside 6 mm diameter tube
Irradiate with different fluences of antiprotons (various doses)
Extract gelatin from tube and take 2 mm slices at several positions
Disolve slices and seed number of cells determined by predicted survival in growth medium
Incubate for 5 – 6 days
Stain cells and count number of colonies  extract survival fraction
Monte Carlo Assisted Dosimetry:
Determine number of antiprotons entering experimental set-up
Measure beam spot and position at entrance to target tank
Estimate beam divergence (0 mrad/source distance 200 cm)
Build model of experimental set-up in FLUKA
Transport 5 million primaries through FLUKA
Rerun using +/- sigma for parameters with know errors
Study systematic errors due to arbitrary assumptions

## Slide 12: Biological Effect - The tube approach
Beam
Irradiate V79 CELLS – Chinese hamster lung fibroblasts
Use different dose levels to cover 100% to 0.1% survival
Seed number of cells for expected survival of 100 cells

## Slide 13: The tube approach – not a trivial task

## Slide 14: Monte Carlo Assisted Dosimetry
Correction for change in experimental set-up after 2008
x-Axis for 2008 needed to be shifted by 4 mm

## Slide 15: Building the Spread-Out Bragg Peak (SOBP)

## Slide 16: SOBP Comparison between Years

## Slide 17: RBE Analysis
Correct survival fraction for Plating Efficiency (obtained from unirradiated tubes and/or from unrestricted fits)
Fit data to ln(SF) = -ax-bx2, obtain a, b, and sigma(a), sigma(b)
84 mm 2012
Extract Dose for 10% survival D10%

## Slide 18: RBE Analysis - Errors
Use s(a) and s(b) from fit to establish error band and s(D10%)
ln(SF) = -ax-bx2  ln(SF) = -(a±k*s(a))x – (b±k*s(b))x2
k is chosen so that ≈ 68 % of data points are in between the two curves
84 mm 2012

## Slide 19: RBE Analysis
Repeat procedure for all years (2008, 2010, and 2012)
RBE = D10%,x-rays/D10%, pbars
Plot Average of RBE’s for each slice
Combine statistical errors in quadrature (as long as variance of values is less than 2 sigma)
Chart: RBE Average 2008 - 2012
| 10.0 | 30.0 | 50.0 | 70.0 | 80.0 | 84.0 | 86.0 | 88.0 | 90.0 | 92.0 | 94.0 | 96.0 | 98.0 | 100.0
RBE | 1.2611 | 1.2505 | 1.1649 | 1.1815 | 1.1682 | 1.1646 | 1.1922 | 1.2532 | 1.3258 | 1.2653 | 1.382 | 1.4672 | 1.6215
 | 2.4839

## Slide 20
Chart: RBE Average 2008 - 2012
| 10.0 | 30.0 | 50.0 | 70.0 | 80.0 | 84.0 | 86.0 | 88.0 | 90.0 | 92.0 | 94.0 | 96.0 | 98.0 | 100.0
RBE | 1.2611 | 1.2505 | 1.1649 | 1.1815 | 1.1682 | 1.1646 | 1.1922 | 1.2532 | 1.3258 | 1.2653 | 1.382 | 1.4672 | 1.6215
 | 2.4839

## Slide 21
Discussion
Error bars contain only statistical variations (counting of survival)
Systematic errors affecting the result for each set are probably “covered” by averaging all sets. These are:
Error in Plating efficiency (11% - 15%)
Error in Dose calculation (<10%) Definition of beam spot size and position and beam divergence
(Dose calculations with all parameters changed by respective sigma’s and variations added in quadrature)
Both would shift the individual RBE vs. Depth curves up and down Alternative: normalize RBE in plateau? Fit in plateau carries largest errors
Dose error affecting Peak and Plateau region differently: Final uncertainty of FLUKA dose
2014 Benchmark Experiment

## Slide 22
Benchmark Experiment 2014 - Preliminary
Chart: Comparison FLUKA vs. Measurement for Tube B
| 0.610075 | 0.83415 | 2.056459999999996 | 2.28078 | 3.50151 | 3.724045 | 4.94233 | 5.164189999999985 | 5.888174999999991 | 6.114999999999991 | 6.337529999999997 | 6.55963 | 6.78403499999999 | 7.00723 | 7.229315 | 7.452385 | 7.672884999999987 | 7.893879999999997 | 8.1188 | 8.343185000000001 | 8.56868 | 8.79434 | 9.016115 | 9.236470000000001 | 9.457810000000002 | 9.680115000000001 | 9.90341 | 10.12679
Measurement | 3.3702 | 3.3287 | 3.319 | 3.3698 | 3.4779 | 3.3883 | 3.4145 | 3.3996 | 3.5013 | 3.593 | 3.6131 | 3.6493 | 3.7782 | 3.9379 | 4.1505 | 4.4069 | 4.8134 | 5.7267 | 7.9438 | 10.831 | 10.9414 | 4.8897 | 2.0892 | 1.4968 | 1.0309 | 0.81119 | 0.6386 | 0.60891
FLUKA Calculation | 3.2094 | 3.2131 | 3.2434 | 3.2511 | 3.3045 | 3.3277 | 3.4035 | 3.422 | 3.5052 | 3.5596 | 3.6189 | 3.7041 | 3.8058 | 3.9481 | 4.1478 | 4.4342 | 4.8924 | 5.7521 | 7.9942 | 12.2687 | 12.7346 | 4.8367 | 2.3288 | 1.5826 | 1.208 | 0.96503 | 0.79424 | 0.68677
Over-estimation of dose in Peak would result in increase of RBE values.
Analysis including correction factors for pressure and temperature in progress
14 %

## Slide 23
Summary and Discussions
Primary Goal:
RBE of antiprotons vs. depth up to the distal edge of the Bragg Peak.
Steep increase of RBE confined to the SOBP region.
Lessons learnt?
Biology experiments are hard!!
Need best possible diagnostic for beam! Mimotera only installed in 2010, multiple monitors better
Clinical beam would have been much better, but unrealistic! Flat field of 5 x 5 cm to eliminate divergence and scatter
Compress experiment to 1 year to avoid changes over time (Set-up changes, alignment, MC assisted dosimetry - but that would have inhibited the “learning curve”).
Leave experiment mounted at all times Survey of experiment impossible after installation of AeGIS

## Slide 24
No further real progress achievable with beam at CERN. Original FAIR/FLAIR facility should have been running by now offering higher intensity and continuous extraction.
Theoretical predictions in general confirmed, replacing theoretical “guesses” with experimental data.
Principle of real-time imaging confirmed.
Thank you AD Team AD users and CERN
We close the chapter but not the book