## Slide 1: The Principles of the CLIQ System
E. Ravaioli
Conceptual Design Review of the Magnet Circuits for the HL-LHC
21 March 2016

## Slide 2
CLIQ – Coupling-Loss Induced Quench
3/21/2016
Current change
Magnetic field change
Coupling losses (Heat)
QUENCH
Temperature rise

## Slide 3
CLIQ applied to a 14 m LHC main dipole

## Slide 4
Main CLIQ heating mechanism:
inter-filament coupling loss
Cu
SC
More effective heat deposition with respect to conventional technology based on thermal diffusion
Faster and more homogeneous quench initiation
Lower hot-spot temperature

## Slide 5
Main advantages and disadvantages
Advantages
More effective heat generation directly in the superconductor
Robust electrical design, easier implementation and repair
Faster quench initiation
  More homogeneous temperature distribution
  Lower hot-spot temperature
Lower failure risk
Less dependent on magnet, cable, strand parameters
Easy repair solution for a magnet with damaged quench heaters
Possible to avoid the installation of quench heaters
Disadvantages
Additional current lead(s) connected to the magnet (pulse current for <100 ms)
Energy deposited very homogeneously in the coil (inefficient at low current)
CLIQ connected directly to the main circuit
  Voltage to ground distribution, in particular if several magnets
  AC currents introduced
  Need to install parallel elements
  Integration with an energy-extraction system is possible but it needs to be carefully studied
Additional mechanical stresses due to the introduced current need to be analyzed

## Slide 6
CLIQ units
  CLIQ technology tested successfully on magnets of different size (from small-scale test magnets to full-scale accelerator magnets), inductance (from a few mH to a few H), type of superconductor (Nb-Ti, Nb3Sn), cable/strand parameters.
More detail tomorrow in Knud’s talk

## Slide 7
CLIQ terminals and leads
Aug 2015: full-size 15 m LHC main dipole
2014: H02b
Courtesy of Dan Cheng
  Need to carry only pulsed currents (<100-200 ms)
  Minimize their resistance (superconducting cable is a nice solution)
  Secure connection (Lorentz forces will act on them)

## Slide 8
CLIQ configuration
1
2
3
4
1
2
3
4

## Slide 9
CLIQ configuration
1
2
3
4
1
2
3
4

## Slide 10
Scaling of CLIQ performance
  CLIQ effectiveness
  → Coil geometry
  → Position of CLIQ connections
  → Electrical order of the poles
  → Conductor parameters
  → etc…
At high current
Low energy needed to start the quench
High energy density, needs to be quick!
 POWER is the key parameter
At low current
High energy needed to start the quench
Low energy density, velocity not critical
 ENERGY is the key parameter
(Number of CLIQ units)^2
(Charging voltage)^2
(magnetic length)^-2 (fixed by design)
Number of CLIQ units
(Charging voltage)^2
Capacitance of each unit
Magnetic length
# of CLIQ units
Capacitance

## Slide 11
CLIQ – Summary
  Faster energy deposition | More robust system
  Needs studies for integration in the magnet system
  CLIQ’s main ingredients
      Inter-filament coupling loss (Conductor)
      Units (Charging voltage, Capacitance)
      Terminals and leads (Resistance)
      Configuration (Effectiveness)
  CLIQ technology tested successfully on magnets with very different characteristics (MQXC2, HQ02b, MQY, MB,…)
  Simulation studies ongoing for the protection of future magnets (MQXF, 11 T, D1, D2, Q4, FCC magnets,…)