## Slide 1: Diagnostics and analysis: “The point of view of the MP3”
Arjan Verweij, TE-MPE
with input from other MPE collegues
Circuit review – CERN- 21-23 March 2016

## Slide 2
The MP3 (LHC Magnet Circuits, Powering and Performance Panel) is a panel of about 20 experts in the field of Magnets, Superconductors, Power converters, DFB, Cryogenics, Quench Detection (QD), Interlocks, ELQA, Electro-thermal modeling, Quench behaviour, Magnet testing, Data acquisition, Databases, … Besides looking at individual parts of the magnet circuits, the MP3 looks especially at interaction/dependency between various parts, affecting the performance of the circuits.

## Slide 3: General
The long-term advantages of “simple, uniform, transparent” circuits, powering, quench detection (QD), and protection should not be underestimated, and should be properly taken into account for any configuration choice.
Favor:
    Self-protected magnets, in stead of active protection
    Simple bridge comparison for QD, in stead of sensitive/complicated L(I)dI/dt compensation
    Separate D1 – D2 powering, similar to the other IPD circuits
    3 lead powering of the Q4, in stead of one main converter plus one trim
Avoid:
    Nested magnets
    Nested circuits
    Different protection systems, quench heater ratings, etc.
    Exceptions…
But, on the other hand, we are of course also very interested in working with new technology in the LHC, such as Nb3Sn, SC link, CLIQ, …

## Slide 4: General
The SC link, the current leads, long busbars, and the magnet should have individual QD, so as to set appropriate thresholds, filtering, and evaluation times.
    Busbar and magnet can be combined for the correctors.
    Short busbars can be combined with the magnet
    Splices/joints can be combined with the magnet or the busbar
A fast power abort in a circuit should not trip other circuits due to mutual coupling, especially important for the SC link and busbars (since not twisted and often in parallel over long lengths)
Each magnet circuit should have a complete documentation (approved by WPs, see talk Reiner), specifying electrical circuits, signal names, protection equipment, data flow, simulation data, prototype test data, etc.

## Slide 5: General
Quench detection (see also presentation by Jens):
    Each voltage tap should be fully redundant with separate connection/soldering onto the conductor/coil, so as to have two redundant QD signals with 1oo2 voting.
    Sampling frequency of all voltages should be at least 5 kHz.
    Optimize the signal-to-noise for the QD signals.
    QD should be flux-jump insensitive.
    One should foresee current-dependent QD thresholds.
    One controller per circuit

## Slide 6: 11-T dipole: General
The 11-T dipole has to comply to the ELQA testing at 2.1 kV (see talk Felix). The 11-T dipole should not impose a higher testing voltage on the main dipole circuit.
Each quench of the 11-T dipole in the LHC requires 10 hrs recovery (example: 3 quenches per aperture  24 quenches per circuit  10 days)
As the RB circuit, the 11-T dipole will be commissioned to Inom+100 A.
The 11-T dipoles should not quench, neither trip the QD, during an exp. decay from nominal with t=100 s.

## Slide 7: Circuit voltage taps for QD
D1
    DV between poles (1 x 2 signals)
    DV between half poles (2 x 2 signals) or dI/dt for symmetric quench detection (1 x 2 signals)
    V over the 2 cold busbars (2 x 2 signals)
    V over the resistive part of the current lead (2 x 2 signals)
    V over the HTS part of the current lead (2 x 2 signals)
    V over the SC link (2 x 2 signals)
D2
    DV between apertures (1 x 2 signals)
    DV between poles (2 x 2 signals)
    V over the 2 cold busbars (2 x 2 signals)
    V over the resistive part of the current lead (2 x 2 signals)
    V over the HTS part of the current lead (2 x 2 signals)
    V over the SC link (2 x 2 signals)

## Slide 8: Circuit voltage taps for QD
  Q4 (“3 leads” configuration with two main converters)
    DV between half apertures (2 x 2 signals)
    dI/dt for symmetric quench detection (1 x 2 signals)
    V over the 3 cold busbars (3 x 2 signals)
    V over the resistive part of the current lead (3 x 2 signals)
    V over the HTS part of the current lead (3 x 2 signals)
    V over the SC link (3 x 2 signals)
  Correctors
    Preferably DV between two halves of the corrector (including the busbar), to avoid inductive compensation.
    CCT corrector possibly DV between layers + compensation
    V over the resistive part of the current lead (2 x 2 signals)
    V over the HTS part of the current lead (2 x 2 signals)
    V over the SC link (2 x 2 signals)
    To be checked which correctors need symmetric QD.

## Slide 9: 11-T dipole: Voltage taps for QD
D1, A1
D1, A2
D2, A2
D2, A1
U_D1A1 – U_D2A1 and U_D1A2 – U_D2A2 : Normal and symmetric quenches
U_D1A1 – U_D1A2 and U_D2A1 – U_D2A2 : Redundancy
All signals doubled (board A & B), so [4 x 2] detection signals in total.
The protection on the D11 has to work taking into account the noise and transients in the circuit: the standard “100 mV, 10 ms” needs to be confirmed.
Trim
PC
Obviously, the noise of the trim converter should not trigger the QD. Especially the 0 V transition could cause additional noise and possibly QD trips.
Interaction between converter, trim converter, EE, and QD should be studied!!!

## Slide 10: 11-T dipole: Voltage taps
D1, A1
Upper
D1, A1
Lower
D2, A1
Taps for local diagnostics
Voltage taps for QD
UD1,A1 (board A & B)
UD2,A1
(board A & B)
No need for QD or monitoring of individual splices/joints, but possibility of local diagnostics in case of a problem.
A few more iterations are needed.

## Slide 11: Triplet: Voltage taps for QD
  Same strategy as 11-T dipole: no QD / monitoring of individual splices
  Triplet Q1 and Q3
    DV between 2 poles of each quadrupole (4 x 2 signals)
    DV between Q1a and Q1b and between Q3a and Q3b (2 x 2 signals)
  Triplet Q2
    DV between 2 poles of each quadrupole (2 x 2 signals)
    DV between P1 and P2 and between P3 and P4 of each quadrupole (4 x 2 signals)
      V over the 5 cold busbars (5 x 2 signals)
      V over the resistive part of the current lead (5 x 2 signals)
      V over the HTS part of the current lead (5 x 2 signals)
      V over the SC link (5 x 2 signals)

## Slide 12: Other protection equipment
Quench heaters:
Quench heater power supplies should preferably be the same as for the LHC (+-450 V, t≈80 ms)
Measurement of both the current in the quench heater and the voltage over the quench heater. Sampling frequency at least the same as LHC.
Quench heaters should be connected in such a way so as to have minimum mutual interference with the coil, so as to limit the measured voltage of the quench heater during the fast decay of the magnet current.
CLIQ:
Measurement of the current decay of CLIQ with at least 5 kHz.
Measurement of the voltage over the CLIQ capacitors.
DCCT’s (for QD):
f>5 kHz
Currents in parallel diode paths

## Slide 13: Post Mortem
Time synchronisation between ALL signals (converter, QD of the SC link, QD of the leads, QD of the bus, QD of the magnet, quench heaters, CLIQ, DCCT for QD, beam) should be better than 0.2 ms.
A PM file should be created for each QD trigger.
The data in the PM files should be correct, without spikes and timing errors, so that automatic analysis and verification can be used on these dependable systems.
Reception acceptance tests (incl. the string test in SM18) should have the same protection and measurement configuration as foreseen for the LHC: same QD boards, same DCCT, same quench heaters + supplies, same CLIQ, same control systems, etc.

## Slide 14: Typical HWC test sequence
Powering tests only start as soon as the Individual System Tests have been successfully performed. A typical HWC test sequence consists of a number of tests with increasing current levels. The correct functioning of the various systems (converters, QPS, leads, busbars, joints, magnets, EE, switches, diodes) is checked before going to higher currents. Each type of circuit has its “own” tailored test sequence.

## Slide 15: Test sequence
11-T dipole
Should follow the standard test sequence for the main dipole circuit. Due to the additional trim converter we might need to modify or add one or more tests.
Triplet
A new test sequence will be defined, based on the actual test sequence of the triplets (Q1,Q2a/b,Q3 with 3 nested power converters), but adapted to the different circuit configuration.
D1-D2
A new test sequence will be defined, based on the actual test sequence of the D1-D4 magnets, but adapted in case of combined powering.
Correctors
Should preferably follow the standard test sequence for the specific type of circuit (600 A, 600 A with EE, 80-120 A). A new procedure will be made for the triplet orbit correctors.
Test sequences can always be adapted if needed!!

## Slide 16: Questions?