## Slide 1: Quadrupoles trims for 2 GeV operation – Tunes @ extraction
E. Benedetto
LIU-PSB meeting 19/01/2016

## Slide 2: Input from A. Newborough
LIU-PSB meeting 5/11/2015
Magnet / Circuit | 2.0 GeV [Margin 5.6 kA + 5%] Integrated Field / Gradient | 2.0 GeV MPS or TRIM Current [Margin 5.6kA + 5%]
Bending Outer | 1.824 Tm [1.893 Tm] | 5350 A [5572 A]
Bending Inner | 1.824 Tm [1.893 Tm] | 5280 A [5487 A]
QF | 6.758 T/m [6.716 <> 7.060 T/m] | Bending Outer -446 A [-718 <> -469 A]
QD | -6.841 T/m [-6.799 <> -7.15 T/m] | Bending Inner -290 A [-540 <> -284 A]
A. Newborough, 13/11/15

## Slide 3: Tunes @ 2 GeV extraction
Chart: 
| 4.1760000000000002 | 4.1539999999999999 | 4.1959999999999997 | 4.133 | 4.2
Qy | 4.17 | 4.134 | 4.091 | 4.213 | 4.2
 | 4 | 4.5
 | QF gradient (T/m) | QD gradient (T/m) | Qx | Qy
“nominal” for dimensioning | 6.758 | -6.841 | 4.18 | 4.17
Margin (5.6kA+5%) | 6.716 | -6.799 | 4.15 | 4.13
QF nominal + QD margin | 6.758 | -6.799 | 4.20 | 4.09
QF margin + QD nominal | 6.716 | -6.841 | 4.13 | 4.21
WP = (4.20, 4.20) | 6.800 | -6.879 | 4.20 | 4.20
WP = (4.19, 4.19) | 6.783 | -6.865 | 4.19 | 4.19
Zero Trim (max tune) | 7.060 | -7.150 | 4.33 | 4.45
Qy
Qx
Going to higher tunes is always possible:
  smaller current in the Trims
There is good margin provided that we keep a similar working point as of today.

## Slide 4: A small post-it…
Need to update the Q editor to take into account new MPS: inner/outer coils will be powered independently