LHCb Calorimeter Upgrade for LS3
Baseline, activities and issues
Theatre of Dreams: LHCb beyond the Phase I Upgrade
The LHCb calorimeter upgrade group
F. Machefert
Thursday April 7th, 2016

---
Why would we like to improve the calorimeter after LS3 ? (I)
Guy
- We already produced very nice results with electrons, photons, p0
  - The present detector is working
    well
- Some of the new high profile channels rely on the calorimeter reconstruction
  - Lepton universality tests
  - Charm physics, etc...

---
Why would we like to improve the calorimeter after LS3 ? (II)
Guy
→ See next talk by Francesco

---
Why would we like to improve the calorimeter after LS3 ? (III)
Guy
→ See next talk by Francesco
- The constraints from the physics groups are often different
    and sometimes contradictory...

---
LS2 and LS3 cavern activities : baseline
- The plan for the LS2 is
  - Keep the PMT after gain reduction and perform a 40MHz readout
  - Requires a completely new readout electronics
    - New analog chip (ICECAL ASIC)
    - New digital board (IGLOO2, GBT-X, DC-DC …)
  - To adapt to the new slow control many
    other activities in parallel
    - New control boards
    - New HV/Calibration/Monitoring
      systems are being designed
  - Dismantling of the SPD/PS and
    lead converter
    - This is a major task
    - The time is limited
    - This is done in parallel with
      - Electronics installation / commissioning

---
LS2 and LS3 cavern activities : baseline
The other big activity planned for the future is the replacement of the modules in the innermost region of the ECAL (LS3)
  - At present the plan is to replace the innermost region of the inner part of the calorimeter
    - “The performances should remain satisfactory up to 2.5Mrad” (~ cte term ~<3%)
      - → 20fb-1 or ~2023
        according to the TDR
  - We have the 32 spare modules
  - 3 months should be enough to perform the operation
  - This requires “only” the dismantling of the columns of modules above the central region
    - Other intervention would require the dismantling of a large fraction of the calorimeter → long task

---
Replacement of the central cells
Working area to remove modules or beam plug
Don't touch this
500 kg beam plug to removed (crane to be used)
Keep

---
The module replacement during the LS3: Radiations
Matthias
- The reason for the replacement is dose and radiation tolerance
  - Simulations with a finer granularity (5x5x5 cm3) around the pipe
  - Simulations optimistic wrt Measurements → x2 safety factor
  - Dose is mainly localized in the left-right regions of the beam pipe
    - Dose profile is going down rapidly in x
- However, the 3% constant term will be reached before the LS3 in the central region
  - Situation getting worst after the upgrade: SPD/PS removal and neutron shielding
- Large degradation during Run 4 (before LS4 ~ RunI + RunII + 50fb-1)
48kGy during Run II

---
Effect of the neutron shielding
Matthias
- The effect of the neutron shielding is still to be understood
  - First simulations show an impact of x ~1.5 on the dose
  - This depends on the geometry adopted
Ratio of the dose expected with new geometry compared to the current geometry

---
Expected dose after 50 fb-1 in the present instrumented region
- Profile at the shower max along x after upgrade (50fb-1)
  - 2 corrections included : simulation (x2), shielding+PS/SPD (x2)
Matthias
Expect ~30Mrad corrected:
 X2 → simulations
X2 → shielding-PS/SPD

---
Expected dose after 50 fb-1 along the z direction
Profil along z at different x positions after the upgrade (50fb-1)
The curves corresponding to the worst case, for the instrumented region.
Previous estimations were 2.5Mrad for 20fb-1.
The new estimation includes new safety factors 2 (shielding + PS/SPD effect)
Dose decreases rapidly, however, clearly, the detector performances will be degraded (cte term) in the central region

---
This raises a few questions
- If the dose is larger than expected the question is
  - Can we perform the LS3 planned replacement earlier ?
    - During the LS2 ?
  - This is not planned: this activity adds up to an already tight schedule
- The neutron shielding has not a negligible impact
- If the modules are replaced during the LS2
  - The problem will appear again during the Runs 3 / 4
- How can we solve the problem on the long term ?
  1. Can we imagine another design for the beam plugs ?
    - This would not help much (Gloria, Matthias)
  1. The LS3 lasts almost 3 years on the last LHC schedule
    - There are projects for replacing some of the ECAL modules by a more performing and more radiation tolerant technology during the LS3 → this would potentially solve the problem

---
Some ideas for a new design
- Wish list
  - Improve energy, position resolutions in spite of pile-up/radiations
    - reduction of transversal extension of the showers (Molière Rad)
    - reduce the size of the cells accordingly (inc. granularity)
  - Could benefit from time measurement → see Roger/Maarten's talks
  - It does not seem necessary to replace the full detector (cost)
    - The area the most affected by
      - Radiation, pile-up and that
        mostly contributes to the physics should be considered
    - Inner, extended outwards, and to the horizontal band ?
    - The addition of new frontiers should be avoided
- The new geometry should benefit from the modular present design
  - New modules of the size (of a fraction) of a module
  - Easier integration with the modules kept
- Full projectivity is not feasible → would require many different modules
  - Can we integrate some projectivity in the horizontal plane (mag. bending plane) ?
    - Tilt the modules in the horizontal plane (problem of leakage)
    - Would improve significantly the position resolution ?
- Can we implement some longitudinal stacks readout ?

---
First attempts for a new design
- What kind of technology to use ? → See talk by Jim
  - Dream-type detector, W-Si, W-shashlik, DECAL, etc...
  - Time measurement → see TORCH session yesterday
- Comments:
  - Should be affordable
  - Time constraint → an already quite mature technology
- Simulation activities
  - 2 parallel designs are looked at at simulation level
    - W-shashlik (Vladimir Romanovski)
    - W-Si type modules (Francesco Dettori in a collaboration with the CLIC group at CERN)
  - Granularity reduced to ~2cm as a first attempt
    - better position resolution
    - fight against pile-up effect
  - Time measurement
    - Such a time measurement could be introduced in the simulation when the technology/geometry are clarified

---
What resolution could we expect from a better technology ?
Assuming 4 alternative scenarios
  1. Replace innermost region
  2. Replace full inner region
  3. Replace the full detector
  4. Replace the horizontal band (pile-up)
with the a technology characterized by
  factor x2 improvement on position
  factor x4 improvement on pile-up reduction
Pile-up

---
What resolution could we expect from a better technology ?
- Calculations have to be taken with care
  - Based on full MC simulation of the baseline upgraded calorimeter
    - Use the MC photons info (not the reconstructed one)
    - Add modelisations of the position/energy/pile-up effect
    - Extract performances for improved calorimeter
- We don't get much
  by improving modules in
  the inner region
- The constant term of the
  resolution is probably
  more important than the
  stochastic term
- Could we reduce the cost
  by replacing only the
  horizontal band ?

---
Conclusion
- There are a few technologies which are mature for the LS3
  - Scintillator-W based ECAL
  - CALICE-type ECAL
  - etc…
  - ...and the time measurement should be seriously considered
- Many activities to prepare LS2
  - Working on the LS3 in parallel is a challenge...
  - Hope to get some simulation results within a few weeks
    - Determine the performances with a new geometry
    - Determine the effect on specific physics channel (g, e, p0, …)
    - This will require a new reconstruction

---
BACKUP

---
Effect of the neutron shielding
Matthias
- The effect of the neutron shielding is still to be understood
  - First simulations show an impact of x ~1.5 on the dose
  - This depends on the geometry adopted
Ratio “with/without shielding”

---
Dose at the end of the Run I + II : ~ 3Mrad
Matthias
Profile at the shower max along x after Run I + II
48 kGy (corrected, worst case, 6fb-1) becomes 20kGy (corrected, 6fb-1) for the instrumented region

---
Some ideas for a new design (II)
- What kind of technology to use ? → See talk by Jim
  - Dream-type detector
  - W-Si
  - W-shashlik
  - DECAL
  - Time measurement → see TORCH session yesterday
- Comments:
  - Should be affordable
  - Time constraint → an already quite mature technology
- Proposal:
  - first try with W-shashlik type modules at simulation level
  - Time measurement could help
    - Such a time measurement could be introduced in the simulation when the technology/geometry are clarified

---
W/CeF3 : some tests for CMS
- Design tested at CERN and at Frascati
  - Optimistic conditions
    - not rad hard plastic fibres
    - Independent fibre light coll.
    - Selection of central events
- Less than 10% achievable (?)
- The decay time of the radiation
  tolerant sinctillator/scintillating
  fibres is by far larger than 25 ns
  - Completely new electronics
    design

---
W/Scint. Shashlik
- Based on R&D made for CMS
- Dimensions
  - 25X0 in 20 cm
  - RM ~ 20 mm
  - Cell size for the new simulations
    - ~20mm
- Very simple mechanics
  - No drilling of the scint / fibre insert
  - Simply de polished chamfers to favour
    scintillation light escape towards WLS
- Uniform light collection
Non-uniformities→shower containement

---
CALICE – type (CLIC)
- SiW ECAL:
  - 1x1cm2 lateral segmentation
  - 1 lint., ~24 X0
- In test beam
  - 30 layers (24X0) in 3
    stacks of 10 layers
    with different
    absorber thickness
  - 2 readout
    boards per
    layer
a~17-20%
b~1.9-2.6%
Not only a prototype → large overlap with the HGCAL project (CMS)