## Slide 1
Large Computer Centres
Tony Cass Leader, Fabric Infrastructure & Operations Group Information Technology Department
14th January 2009
and medium

## Slide 2: Characteristics
Power and Power
Compute Power
  Single large system
    Boring
  Multiple small systems
    CERN, Google, Microsoft…
    Multiple issues: Exciting
Electrical Power
  Cooling & €€€

## Slide 3: Challenges
Box Management
What’s Going On?
Power & Cooling

## Slide 4: Challenges
Box Management
What’s Going On?
Power & Cooling

## Slide 5: Challenges
Box Management
  Installation & Configuration
  Monitoring
  Workflow
What’s Going On?
Power & Cooling

## Slide 6: ELFms Vision
Node
Configuration
Management
Node
Management
Leaf
Lemon
Performance & Exception Monitoring
Logistical
Management
Toolkit developed by CERN in collaboration with many HEP sites and as part of the European DataGrid Project.
See http://cern.ch/ELFms

## Slide 7: Quattor
Node Configuration Manager NCM
CompA
CompB
CompC
ServiceA
ServiceB
ServiceC
RPMs / PKGs
SW Package Manager
SPMA
Managed Nodes
SW server(s)
HTTP
SW
Repository
RPMs
Install server
HTTP / PXE
System installer
Install Manager
base OS
XML configuration profiles
Configuration server
HTTP
CDB
SQL backend
SQL
CLI
GUI
scripts
XML backend
SOAP
Used by 18 organisations besides CERN; including two distributed implementations with 5 and 18 sites.

## Slide 8: Configuration Hierarchy
CERN
CC
name_srv1: 192.168.5.55
time_srv1: ip-time-1
lxbatch
cluster_name: lxbatch
master: lxmaster01
pkg_add (lsf5.1)
lxplus
cluster_name: lxplus
pkg_add (lsf5.1)
disk_srv
lxplus001
eth0/ip: 192.168.0.246
pkg_add (lsf5.1_debug)
lxplus020
eth0/ip: 192.168.0.225
lxplus029

## Slide 9: Scalable s/w distribution…
DNS-load balanced HTTP
M
M’
Backend
(“Master”)
Frontend
L1 proxies
L2 proxies
(“Head”
nodes)
Server cluster
H
H
H
…
Rack 1
Rack 2…
… Rack N
Installation images,
RPMs,
configuration profiles

## Slide 10: … in practice!

## Slide 11: Challenges
Box Management
  Installation & Configuration
  Monitoring
  Workflow
What’s Going On?
Power & Cooling

## Slide 12: Lemon
Correlation
Engines
User Workstations
Web browser
Lemon
CLI
User
Monitoring
Repository
TCP/UDP
SOAP
SOAP
Repository
backend
SQL
Nodes
Monitoring Agent
Sensor
Sensor
Sensor
RRDTool / PHP
apache
HTTP

## Slide 13: What is monitored
All the usual system parameters and more
  system load, file system usage, network traffic, daemon count, software version…
  SMART monitoring for disks
  Oracle monitoring
    number of logons, cursors, logical and physical I/O, user commits, index usage, parse statistics, …
  AFS client monitoring
  …
“non-node” sensors allowing integration of
  high level mass-storage and batch system details
    Queue lengths, file lifetime on disk, …
  hardware reliability data
  information from the building management system
    Power demand, UPS status, temperature, …
      and full feedback is possible (although not implemented): e.g. system shutdown on power failure
See power discussion later

## Slide 14: Monitoring displays

## Slide 15: Dynamic cluster definition
As Lemon monitoring is integrated with quattor, monitoring of clusters set up for special uses happens almost automatically.
  This has been invaluable over the past year as we have been stress testing our infrastructure in preparation for LHC operations.
Lemon clusters can also be defined “on the fly”
  e.g. a cluster of “nodes running jobs for the ATLAS experiment”
    note that the set of nodes in this cluster changes over time.

## Slide 16: Challenges
Box Management
  Installation & Configuration
  Monitoring
  Workflow
What’s Going On?
Power & Cooling

## Slide 17: LHC Era Automated Fabric
LEAF is a collection of workflows for high level node hardware and state management, on top of Quattor and LEMON:
HMS (Hardware Management System):
  Track systems through all physical steps in lifecycle eg. installation, moves, vendor calls, retirement
  Automatically requests installs, retires etc. to technicians
  GUI to locate equipment physically
  HMS implementation is CERN specific, but concepts and design should be generic
SMS (State Management System):
  Automated handling (and tracking of) high-level configuration steps
    Reconfigure and reboot all LXPLUS nodes for new kernel and/or physical move
    Drain and reconfig nodes for diagnosis / repair operations
  Issues all necessary (re)configuration commands via Quattor
  extensible framework – plug-ins for site-specific operations possible

## Slide 18: LEAF workflow example
5. Take out of production
  Close queues and drain jobs
  Disable alarms
Operations
HMS
1. Import
11. Set to production
SMS
2. Set to standby
7. Request move
technicians
6. Shutdown work order
Node
4. Refresh
13. Refresh
NW DB
8. Update
9. Update
Quattor
CDB
3. Update
12. Update
10. Install work order
14. Put into production

## Slide 19: Integration in Action
Simple
  Operator alarms masked according to system state
Complex
  Disk and RAID failures detected on disk storage nodes lead automatically to a reconfiguration of the mass storage system:
SMS
Mass Storage System
Disk Server
LEMON
Lemon Agent
RAID degraded
Alarm
Alarm Monitor
Alarm Analysis
set Standby
Draining: no new connections allowed; existing data transfers continue.
set Draining

## Slide 20: Challenges
Box Management
  Installation & Configuration
  Monitoring
  Workflow
What’s Going On?
Power & Cooling

## Slide 21: A Complex Overall Service
System managers understand systems (we hope!).
  But do they understand the service?
  Do the users?

## Slide 22: User Status Views @ CERN

## Slide 23: SLS Architecture

## Slide 24: SLS Service Hierarchy

## Slide 25: SLS Service Hierarchy

## Slide 26: Challenges
Box Management
  Installation & Configuration
  Monitoring
  Workflow
What’s Going On?
Power & Cooling

## Slide 27: Power & Cooling
Megawatts in need
  Continuity
    Redundancy where?
  Megawatts out
    Air vs Water
  Green Computing
    Run high…
    … but not too high
Containers and Clouds
You can’t control what you don’t measure

## Slide 28
Thank You!
Thanks also to
Olof Bärring, Chuck Boeheim, German Cancio Melia, James Casey, James Gillies, Giuseppe Lo Presti, Gavin McCance, Sebastien Ponce, Les Robertson and Wolfgang von Rüden