## Slide 1: 2014 Issues & Strategy execution
Piotr Skowroński

## Slide 2: The issues
Losses in TL2
Not clean recombination
Emittance growth
Closure
Dispersion control
Optics control on model level
Non-linear dispersion and chromaticity
BPI's in TL1 giving different reading for 1.5 GHz and 3 GHz
BPI's droop
BPI non-linearity
Inconsistent quad scans
Faulty BPMs
Phase sag

## Slide 3: Sources of the issues 1/2
Losses in TL2
  1. Too big emittance
  2. Insufficient control of the optics, predominantly of dispersion
  3. Insufficient orbit and Twiss closure in the recombination
Not clean recombination
  1. Insufficient orbit and Twiss closure in the recombination
  2. Stability: drifts in the machine make the systematic setup difficult, if not impossible, and move quickly the beam from sweet point
Emittance growth
  1. Insufficient orbit and Twiss closure in the recombination
  2. Insufficient control of the optics, predominantly of dispersion
  3. Non-linear dispersion
  4. Large chroma causes very fast decoherence in case of imperfect steering
Closure
  1. DL issue with BPIs: TL1 1.5GHz response
  2. CR issue with BPIs: droop leading to readout drift
  3. Not enough space for orbit correction at DL ejection

## Slide 4: Sources of the issues 2/2
Dispersion control
  1. Large dispersion beating from very small errors in k1, orbit, beam energy
  2. Missing dispersion correction knobs
  3. Missing dispersion correction application
Optics control on model level
  1. Model not accurate enough (optics errors) in Frascati chicane, TL2, TL2'
  2. The nominal optics is not optimal with higher order and stability respects

## Slide 5: Action List Before Beam
  Extract the 1.5/3GHz results (Piotr)
  BPI checks with BI (Steffen) ?
  Check attenuators for phase monitors to assure max S/N for best feed-back operation: (Frank)
  Preparation of TL2 optics with smoother non-linear dispersion (Piotr)
  Strategy conception for closure of transverse optics and tooling (can we do better than brute force quad-scan - rematch loop)

## Slide 6: Action List Action requiring beam
  Tuning of feedbacks (Tobias + Lukas)
  Response matrix with screens as beam position monitors - (Piotr)
  k1 measurements with Corrector-Quad-BPM and Corrector-Quad-Screen - (Piotr)
  Response matrix measurements with quadrupoles changed as much as possible to assure transmission (Piotr + Jack, done in TL1)
  BPI non-linearity measurements
  Verify if DL BPI's have the same issue ?

## Slide 7: Action List Not for now
  1. Stability requirements (Lukas)
  2. Analysis for new feedbacks
  3. TL1 optics with R56 opposite to TL2 to assure R56=0 from linac to TBL

## Slide 8: Tooling List 1/3
Phase space painting + analysis tools (Piotr - partially ready(?))
  Other related studies :
    Aperture meter
    BPI non-linearity correction for optics measurements (Davide)
Tool for energy spread optimization in CTS segmented dump - (Davide)
Tool for BPR475 flattening using MKS02 phase program (Davide -)

## Slide 9: Tooling List 1/3
Orbit tools:
  Dispersion Target Steering is the biggest priority (Davide) (ready, to be tested)
    implement as much as possible with simulation backend connected to MAD-X (ready and partially tested)
  Tool for re-fix orbit around spectro 4
  Tool for re-fix orbit around spectro 10
  Tool for re-fix orbit around Frascati chicane
  Orbit maching of DL with 3Ghz beam
  Dispersion Target Steering for all the main lines (horizontal and vertical).

## Slide 10: Tooling List 2/3
Tool that optimizes orbit on center of sextupoles using fact that kick is quadratic in one of its planes (!-------!)
Dispersion monitor tool
Quad scan program in simulation mode (camera images generated with sigmas from MADX quad scans simulation) to verify that the program works fine
    (!Reidar - tool works on linux consoles!)
Response matrix comparison when measuring for steering: app Davide - extraction from MADX (Piotr)
Energy stabilization and flattening feedback with MKS15: use 2 BPMs upstream of the F.Chicane to check stability of the beam: (Tobias to be agreed with Davide)

## Slide 11: Tooling List 3/3
BPI droop subtraction for closed orbit measurement (Tobias)
Overnight random corrections to improve transmission in desperate cases like TL2 (!-------!)
Tune measurement and tuning in CR revival (Tobias)
Feedbacks stall on beam parameters change (Tobias)
  Gun Timing
  Beam to spectro 4
  Intensity change
Tool for quadscan measurement overnight continuously (with static initial conditions first).
Not for now:
  Knobs for dispersion correction

## Slide 12: Commissioning strategy Linac - not an issue
Feedbacks - they should stall whenever beam parameters or destination change (time window, intensity, beam to spectro 4) because they do more harm than good when trying to adapt
  Loading
  Injector - implement sanity checks, for example sending beam to spectro 4 makes it run away
  TWT - low priority because the phase stability was not an issue; should use only average over the pulse and not try to adapt to pulse shape with switches

## Slide 13: Commissioning strategy Linac - not an issue
Steering
  DFS to be tried in the linac - should be straight forward
  DTS (Dispersion Target Steering) will be tried everywhere else
  Change of orbit in the Linac after a bend is on or any other reason
    Define strategy to recover after common cases
      after BHB.1040 on -> use corrector 0920
      after spectro 4 on - >
      after injector change ->
    Apply automatic tool from Davide to re-steer the end of linac to the reference orbit
RF setting up
  Tool to adjust phases to flatten BPRs implemented by Davide; apply ones at the startup should be sufficient
Optimization of energy spread in spectrometer, using also the algorithm from steering

## Slide 14: Commissioning strategy Delay Loop
  Verify that BPI's don't have the same problem as TL1
  Dispersion Target Steering
  Dispersion Correction
  Scan RF bump height to find optimum for closure
  Measure and correct beta beating (Twiss closure)
  Orbit closure in 2 steps
    3 GHz with magnetic (using TL1 pickups)
      Test it with 3GHz beam splitting
    Refine with 1.5GHz using CR BPMs (and not watching TL1)

## Slide 15: Commissioning strategy TL1
Implement optics with reverse R56 of TL2 PFF optics to assure R56 = 0 from phase monitor to phase monitor?
Also for nominal optics R56 is not null from linac to CLEX due to uncorrected doglegs contributions at CR extraction, vertical and TL2 prime
Steering
Dispersion Correction

## Slide 16: Commissioning strategy CR
  Give a try to the new optics for 1-2 days
    Check immediately if sextupole correction works or not
    If yes profit easier tune measurements and corrections
  Orbit
  Closed orbit
  DTS
  We could try tune measurement with some dirty off momentum cleaning
    For example try to scrape somewhere in CT
  Could try to use extraction kicker for better tune measurement
    I doubt it is feasible

## Slide 17: Commissioning strategy CR
  How to measure beta beating? It is a lengthy procedure
    Automated overnight? (Tobias)
    Automatic range adjustment?
  Correct the Twiss beating
  Optics correction of CR - procedure (from 29/09/2014):
    inject beam. Keep it N turns.
    extract the beam and measure Twiss parameters.
    repeat for different N up to 20... 30...
    to see what to do next after those results.

## Slide 18: Commissioning strategy TL2 and CLEX
  Get the straight beam through for nominal and PFF optics
  Dispersion Target Steering, hopefully after alignment it will be easier
  Steering
  Dispersion correction
  Optics measurements with phase space painting (regular RM we should get as steering by-product)

## Slide 19: Status
Many items were successfully implemented and were the key for the last results
Lack of time or available beam time did not let to complete the rest
The missing points for drive beam
  Stability
  Emittance
  Transmission from CR to the ends in CLEX
  Optics control

## Slide 20: The last year
The final report(s) need to be delivered in 2016/2017
This time there is no chance we catch the result in the following year: all the data points must be measured this year
To be efficient:
  Assign the responsible person who follows each topic
  Make a list of needed measurements
  Priorities
  Group the measurements by the required machine setup, thoroughly execute the list not to leave anything for later
  Check preparation for the most important experiments
    Presentation on the EV or OP meeting with the procedure (quick and dirty)
      Gives chance to think what is really needed and if it is prepared
      get feedback how it could be improved
      or if a better way to measure exists
    Reviews every couple of months

## Slide 21: Notes
TBM conditioning
  Over nights factor 8
  Higher rep-rate during days?
Beta beating from amplitude: kicking the beam with extraction kicker (when the decoheres and settles on the closed solution) global fit A_n*sin(mu0*t+fi_n)*exp(-d*t)
  A_n amplitude at BPM ~sqrt(beta)
  mu0 tune (global variable)
  t turn
  Fi_n phase advance from the kick
  d damping