Overview
H6 CTB2004 TB results
Andrei Kiryunin, Pavol Strizenec
  - Data – MC comparison, rel. 15.0.0, G4 9.2.p00, QGSP_BERT, 200 GeV charged pions
  - TopoClusters + LocalHadronCalibration used out of the box, with current ATLAS defaults
  - Disclaimer – it's a fresh analysis, not everything finalized yet
  - Still open – proper EM scale tuning (EMEC and FCAL use a scale obtained frome cone analysis)
  - Full blue symbols – data, open red – MC
  - Point D is EMEC/HEC region, point H – FCAL region, energy on EM scale + some moments
P. Strizenec
Foz do Arelho 2009, Hadronic calibration workshop

---
EM scale
difference data-MC higher in leading cluster than in sum
scale not recovered fully
crack as well

---
Andrei Kiryunin, Pavol Strizenec
  - Conclusions:
    - energy spectra and moments quite nice described outside crack, we see a “standard feature” of QGSP_BERT – slightly denser shower, which starts earlier in calo (for full set of eta-dependence of moments see backup slides in agenda)
    - some recovery of missing energy in crack after weighting for charged pions, but some problems with electrons (again see backup)
    - the detailed behaviour of all cluster moments not fully understood, but most features well reproduced by MC, specially the lateral size and
    - OOC and DM corrections needs to be redone for TB setup – clearly the ATLAS one are not appropriate here (different leakage, DM, .....)