## Slide 1: GEM Firmware Developer Notes
J. Gilmore, T. Lenzi
December 2015

## Slide 2: OH Fiber Communication Structure
Built around 2 Rx + 2 Tx fiber links (2 SFPs) to GLIB
  Note: currently all GTX links use elastic buffers
  One Tx for [Track data + slow control] and one Tx for Trigger/S-bit data
    Track Data Tx: 19 BX packet structure, one packet per VFAT2 chip (details below)
      Data transmission begins as soon as it’s available from VFAT (see diagrams on next page)
      Each packet contains a 32-bit BXN, so it gets repeated up to 24 times per event
        We have some ideas for improving this in the future… This area needs some planning for SLICE…
    Trigger Tx path really needs to be a non-elastic buffer for fixed trigger latency
      Currently this path is not used, need to install S-bit encoding logic: under development
  One Rx for [slow control + RxRecCLK] and one Rx for TTC commands
    TTC Rx path really needs to be a non-elastic buffer for fixed trigger latency
      Uses codes 100, 101, 110, 111 on T1 lines for L1A, BC0, Resync, CalPulse
Track Data Tx format
  Requires 19 BX to transmit a full packet: one packet per VFAT
    00BC + 16-bit-Hdr + (14x16-bit) TrkData + 32-bit-s.c.data + 16-bit CRC
  So far the “Hdr” header only uses 2 bits (14 bits free)
    Track-data-present flag and slow-control-data-present flag
Slow Control Rx format
  Requires 7 BX to receive a full packet from GLIB
    00BC + 16-bit-Hdr + 32-bit-Adr + 32-bit-s.c.data + 16-bit CRC
  So far the “Hdr” header only uses 2 bits (14 bits free)
    R/W type and slow-control-data-present flag

## Slide 3: OH VFAT2 Track Data Handling
The Track Data Concentrator loops continuously over all 24 VFAT2DATA registers
  FIFO_PUSH = SELECT_i AND VALID_i (possibly include AND HIT_i here too for zero-suppression)
    BXN & Data from the selected VFAT register (224 bits total) will write into Data Concentrator FIFO
    For zero-suppression, require adding VFAT DAV list in the event format to show which VFATs were all zeroes
  CLEAR_REG_i = SELECT_i AND VALID_i
  BXN comes from the L1A FIFO: the same BX is assigned for all VFATs in the event
194-bit shift register
Serial VFAT2 data
(just one VFAT)
VFAT2 format pattern detection = data valid
40 MHz
192-bit parallel VFAT2 data
VALID
DATA(192)
RAW_DATA_IN
CRC_OK
HIT
VFAT2 CRC check result
OR of all 128 strips = non-zero VFAT2 data available
DATA(192) + VALID + CRC_OK + HIT
195-bit VFAT
Data Register
VALID
CLOCK
40 MHz
VFAT2DATA(195)
CLEAR_REG
CE
CLK
RST
VFAT2 Input Data Handler
*This box is repeated 24 times, once per VFAT*
Data Concentrator FIFO
FIFO_PUSH
CLOCK
40 MHz
WEN
WCLK
TRACK_DATA(224))
VFAT2DATA + BXN
GTX Tracking Tx
Formatter
160 MHz
CLK
REN
GTX_CLOCK
START_NEW_PACKET
RCLK
NEW_PACKET
One packet per VFAT,
16-bits per clock. So including the header it takes 4.75 BX to complete a packet.
VFAT2DATA_0
VFAT2DATA_23
VFAT2DATA_i
Data Concentrator
Selector MUX
…
…
SELECT(5)
Counts i [0 to 23]
continuous loop
VFAT2 Track Data Concentrator
CLEAR_REG(24))
Data packets to GLIB
Note: It takes 194 BX for the
track data to arrive in OH
SLOW_CONTROL_DATA
TRACK_DATA_PRESENT
NOT_EMPTY
ENABLE

## Slide 4: OH Trigger Control
Four sources of “L1” triggers in OH
  Select one source with software tools via IPbus
    Normal L1A from AMC13 (via GLIB fiber link)
    Internal OH logic generator
      Programmable patterns selected in software via IPbus registers
        This logic can also control automated CalPulse and other fast functions
    Loopback
      S-Bit “self-trigger” from one VFAT2 chip, selected via software/Ipbus
      8 S-Bits from each VFAT2 get ORed together, so there are 24 choices
      Note that S-Bits are not clocked into the FPGA
    External LEMO cable input
  For the last 3 cases, GLIB will never see the trigger
    Consider moving the trigger source switching onto the GLIB to resolve this
    This area needs some planning for SLICE…
When L1A is received, OH stores the BXN in the L1A FIFO
  Use the BX counter value at the time L1A is received
    Currently this 32-bit BXN gets sent in every VFAT2 data packet
      Probably gets repeated 24 times per event! This can be improved in the future…
      BXN gets reset by BC0, and this is all that limits the BX count to 0-3563 range
  For SLICE test, OH should also keep an event counter (not just BXN) to send with the data packets
    This area needs some planning for SLICE…

## Slide 5: OH Clocking System
OH FPGA has access to three clock sources
  50 MHz oscillator clock (on board)
    MMCM in FPGA reduces the oscillator clock to 40 MHz internally
  GTX RxRecCLK (internal)
    Right now, this is what gives OH the real 40.08 MHz LHC clock
    It should come from the “Track Data” SFP Rx path, as latency/elastic buffer do not matter here
  QPLL, which right now must lock to a clock signal driven by the FPGA
    QPLL 40 MHz output goes to logic fabric, while QPLL 160 goes to all GTX as MGTrefCLK
    In Slice test the QPLL will only lock to the clock provided via the copper HDMI connector
  External LEMO clock input
    Only used in testbeam and tests at TIF
OH FPGA provides a clock output to CDCE
  BUFGMUX in FPGA selects “CLK_MUX” signal output to CDCE
    Default CLK_MUX at power-up is the 40 MHz “on-board” source
    Clock-aligner circuit in firmware compares this with RxRecCLK
    When RxRecCLK is locked and aligned for 1 msec the MUX switches CLK_MUX to use the RxRecCLK for the CDCE and all FPGA logic
      Note: the selected CLK_MUX signal drives all FPGA logic as well as the CDCE
  Switching logic for the BUFGMUX has 3 modes
    Automatic switching, never switching, or manual/IPbus/ChipScope
    Currently there is no logic to “switch back” automatically if a lock is lost
      We may be able to add this feature, but right now it requires JTAG access to reset the link
CDCE provides a stable MGTrefCLK for all GTX tiles (similar to QPLL)
  Note that it always seems to hold a lock on CLK_MUX during the BUFGMUX switching

## Slide 6: OH Threshold & Latency Scans
For thresholds focus on S-bits vs #BX
For latency focus on Track Data events vs #L1 triggers
Software chooses VFAT to scan & run mode via IPbus
  Also selects min/max for range & number of values to scan
  Set the number of events per value
Firmware sets appropriate VFAT I2C registers in sequence and records the scan results
  Threshold scan shows how many S-bits are set per “N” BX at each value
    Testbeam results show noise may trigger ~2 MHz
  Latency scan reports how many non-zero track packets are observed for “N” events at each value

## Slide 7: Other OH Functions
OH uses the 40.08 MHz LHC clock & sends it to all VFATs (LVDS)
  Each GEB VFAT column shares one clock line, so 3 clock lines are controlled by the FPGA, with 8 VFATs on each line
    Apparently no real benefit for fine tuning the timing of these lines
    However, it IS a good idea to fine-tune the VFAT data input lines into the FPGA using IObuf delays… This area needs some planning for SLICE…
OH sends TTC fast signals over the T1 control lines (LVDS)
  This uses one control line per column, with 8 VFATs on each line
  Commands are encoded in a 3-bit sequence
    Codes 100, 101, 110, 111 are used for L1A, BC0, Resync, CalPulse
Note that VFAT Reset (TTL) also goes out on one line per column
OH uses a wishbone system to handle I2C functions
  6 I2C masters and 6 slaves, used to control 6 I2C sectors (4 VFATs per I2C sector)
  Wishbone also handles ADC scan master, ADC slave, counters slave, status register and control register
    Counters include error counts and packet counts, etc.
      Errors include NotInTable, Disparity and 00BC format check
    Status register reports PLL/clock lock status, etc.
    Control register includes T1 line switch select, VFAT loopback select, VFAT track data mask, VFAT reset, system clock select, etc.

## Slide 8: Other Considerations in OH Logic
All logic resets in the firmware are synchronous
PLLs are not reset, but the advanced modules have a local reset available
  We should consider carefully where resets may be needed
    Many options inside GTX and also in error counters, GTX RxRecClk, etc.
    Sometimes we want to reset the fiber links without a power cycle…
  This area needs some planning for SLICE…
Resync from TTC is not used by OH, only for VFATs
  Probably OH should use it to reset event & error counters, etc.
  GLIB ignores all TTC signals and just forwards them to OH
  This area needs some planning for SLICE…
BC0 only resets BX count on the OH, but not on GLIB
  GLIB should use it too
  On VFAT2 this resets the BC and EC for some reason
  This area needs some planning for SLICE…
Several other registers have “individual” resets via IPbus
  Some should probably OR with Resync, BC0, etc.
  This area needs some planning for SLICE…
VFAT Reset has no function
  Probably this is used for VFAT3 only

## Slide 9: GLIB GTX Track Data Handling
Track Data Rx packets from OH gets saved in FIFOs
  Recall: 19 BX to complete a full packet: one packet per VFAT
    00BC + 16-bit-Hdr + (14x16-bit) TrkData + 32-bit-s.c.data + 16-bit CRC
  The Slow Control FIFO takes in the 32-bit s.c. data (if valid is set)
  The Trk Rx FIFO takes in TrkData for valid data: 16 bits @160 MHz
    FIFO readout is 32-bits @160 MHz
Trk Rx FIFO data readout goes to two buffer systems
  One BIG FIFO for all VFAT TrkData that goes to AMC13
    This FIFO is actually a chain of several FIFOs
    This FIFO chain readout is handled by the Event Builder logic
      Event Builder formats event packets for transmission to AMC13
  A smaller FIFO for Spy Path data, with readout via IPbus registers
    This path requires a prescale as IPbus cannot handle all the data in CMS collisions
      Prescale ratio should be set in an IPbus register
OH_TRACK_DATA (16b)
Tracking Rx
FIFO
Data to chained FIFOs & Spy buffer (32b)
160 MHz
Only the 14x16-bit data goes in here for each VFAT, and only if the DataValid is set in the packet header. Slow Control data goes to a separate FIFO.
Data goes out twice as fast as it comes in. But there is one-clock of extra lag for writing to additional FIFOs for the wait to verify they are not full from the previous write
GTX Rx
(Track Data path from OH)
GLIB Track Data Receiver