## Slide 1: GEM Firmware Concerns & Development Plans
GEM Firmware Workshop
February 2016
Texas A&M University

## Slide 2: Topics for Consideration
All types of RESETs at OH and GLIB
  BC0
  Resync
  Fiber link-sync/GTX reset
    OH needs an automated clock & link recovery method…
  Hard reset
  note that VFAT2 reset signal has no function, and BC0 also resets the event counter in VFAT2
    CMS will send the BC0 on every LHC orbit, so we’ll see it all the time
GLIB-OH link monitoring and controls, error detection and mitigation ideas for VFAT-OH-GLIB
  Consider the types of errors we can detect
  Establish the criteria: when do we need resets?
voltage monitoring, temperature sensor & board ID register
  Just use FPGA and SCA resources for these?

## Slide 3: Topics (2)
Each VFAT takes up a single packet; each packet contains a 32-bit BXN, so it gets repeated up to 24 times per event!
OH-to-GLIB bandwidth optimization: do we need it?
  consider that we need to include an L1A event number anyway
  if we add zero suppression then we must include the non-zero "DAV" VFAT list as well… should add “VFAT alive” count too
  easiest to do it all by building a single event packet at OH that carries all (non-zero) VFATs
    Header has one entry each for L1A number, Orbit count, BX id and DAV list
  should save bandwidth, and still contains all the information we want
How does GLIB handle multiple GEMs?
  Control & tracking data & event building & error monitor
  Calibrations/scans
GBT controls at GLIB and OH
  GBT configuration & clocks
  GBT path for L1 trigger & resync, VTTx controls

## Slide 4: Topics (3)
The trigger source is selected on the OH right now
  Probably better to make this centrally located on the GLIB
  Allows to share GEM self-triggers from S-Bits on other chambers
Each GEB VFAT column shares one clock line, so 3 clock lines are controlled by the FPGA, with 8 VFATs on each line
  Apparently no real benefit for fine tuning the timing of these clock lines?
  However, probably good to tune FPGA receiver timing for data (tracking & S-bits) coming back from VFAT...
    Fine-tune the VFAT data received into the FPGA using IObuf delays
    The range seems to be limited to ~2.5ns of delay, need to check

## Slide 5: Topics (4)
OHv2b has 6 transmitters and 2 receivers
  2 transmit links to OTMB (s-bit clusters)
  2 transmit links to GLIB (s-bit clusters)
  1 transmit/receive pair for FPGA-GLIB for tracking data & control
  1 transmit/receive pair for GBT-GLIB for tracking data & control
    Assume GBT is not reliable for first 6 months of Slice test
  Can we consider to live with just 4 transmitters
How is this different from the current system?
What data/control fields are not verified by a CRC?
  OH probably needs a CRC for the EC/BC/VFATcount
Consider how SEU may impact handling of data & control
  Try to be resilient against one-time errors and single-bit errors
    Control signals received at OH
    Data packets received at GLIB
  Can GLIB know how many VFATs are attached to the GEM?
  Can GLIB use voting among the 24 VFAT packets?

## Slide 6: Topics (5)
Define conditions to set TTS states
  Warning
  Busy
  Lost sync
  Error
Make sure we get “HCAL type” of AMC13 for Slice
  The “CMS type” does not have all the features we need
We need to define GEM fast command encoding
  BC0, Resync, L1A, calib pulse, hard reset, soft reset?
  Follow CSC example or CMS?
Decide the GLIB arrangement we will use
  Each GLIB takes both trigger and tracking data
  Or: a single “trigger GLIB” and several “tracking GLIBs”
  How many GLIBs needed for Slice test?

## Slide 7: Topics (6)
S-Bit handling in OH and OTMB and GLIB
  Will keep all 1536 bits, even with VFAT2
    Map to every eighth bit, but always set size=7
OTMB integrated trigger with S-bits and A/CLCTs
  4 layer CLCT, 3 layer CLCT+1 GEM, 2 GEM and ALCT only
GLIB plans for S-Bits
  Buffer in GLIB & Include in DAQ data stream after an L1A match

## Slide 9: GEM Firmware: Unassigned Tasks
GLIB: GEM Co-pad (local?) trigger algorithm
  Need a link for GEM trigger primitives to Muon TF system
  Need to define the format/protocol as well
GLIB-AMC13 trigger data link?
  Use fabric B for local triggers and also path to TF?
GLIB needs improved trigger source selection plan
GBT-JTAG emulator logic development
  Follow the Cern GBT-FPGA project
Resyncs & reset planning for the OH & GLIB
  Fiber link resyncs & a variety of logic/counter resets
SEU handling
  Automatic scrubbing/correction loop logic
  Hard resets & triple voting

## Slide 10: Strawman Proposal… people & tasks
Alfredo: GLIB firmware
  Work on multiple-GBT Emulator cores for GLIB
Andrew: OH & OTMB firmware
  VFAT S-bit/pad clustering & encoding for CSC & GLIB links
Ryo: OH & GLIB firmware
  ZS logic for handing track data and S-bits