## Slide 1: ELENA – Electron Cooler
Jean Cenede
BI Day June 10th 2016
on behalf of Electron Cooler team
Map Presentation :
  Electrons Cooling generalities
  Electron Cooler at CERN
  ELENA E-Cooler
  E-Gun & Collector

## Slide 2: What‘s a Electron Cooling
BI Day March 10th 2016
Means to increase the phase space density of a stored ion beam.
Mono-energetic cold electron beam is merged with ion beam which is cooled through Coulomb interaction.
Electron beam is renewed and the velocity spread of the ion beam is reduced in all three planes.

## Slide 3: Concept overview of a E-cooler
e-Gun
e-Collector
Circulating Beam
Electron Beam
BI Day March 10th 2016
Circulating Beam Cooled
Solenoïd
Drift

## Slide 4: Electron Cooler system is composed of :
BI Day March 10th 2016
Low velocity Electrons Source :
The E-GUN
final current given by Child’s Law:
I = µ .V3/2
A set of Magnetic circuit :
Expansion Solenoïd, Drift, Toroids, Squeezes coils ….
(Used to transport the electrons Beam)
A Electron Anode Recuperator :
The COLLECTOR

## Slide 5: Cooling effects on Beam viewed by
E-cooling
Acceleration
BI Day March 10th 2016
Beam Ionization Profile Monitor
(LEIR Vertical datas acquisitions : A.Frassier)
Schottky Monitor
(Beam Revolution Frequences )

## Slide 6: CERN’s Electron Cooler : AD and LEIR
BI Day March 10th 2016

## Slide 7: Location
Soon in ELENA Ring
4th Section
BI Day March 10th 2016

## Slide 8: Concept overview of Vacuum Elements
Vacuum system
Gun & Collector
BI Day March 10th 2016
Gun
Collector
Vacuum
Chamber

## Slide 9
Concept overview of Magnets Elements
Magnets
Supporting system
Toroid

## Slide 10: Toroid Assembling details
3D Printing Simulations
Assembling Sequences

## Slide 11: ELENA E-COOLER Power Diagram
Beam Specifications :
I e- : 1/5mA
U e- : -55/-355 V
No High Voltage Cage
BI Day March 10th 2016
Momentum | 35 MeV/c | 13.7 MeV/c
Pbar-beam energy | 648 keV | 100 keV
E-beam energy | 355 eV | 55 eV
I e | 5 mA | 2 mA
Bgun | 1000 G | 
Bdrift | 100 G | 
Toroid bending radius | 0.25 m | 
Cathode radius | 8 mm | 
E-beam radius | 25 mm | 
Cooling drift length | 1.0 m | 

## Slide 12: Gun & Collector Design
Gun and collector design optimization performed with EGUN
BI Day March 10th 2016
(I = µ .V3/2 )

## Slide 13: Gun and Collector Specifications : (Inspired by : AD, LEIR E-COOLER & FERMILAB design )
Adapted to cathode design, electricals, thermals requirements
Differents electrodes with differents forms, positions & voltages
Modularity for eventuality modifications
XH-Vacuum : 10-12 mmb
Hight temperature Back-out : 200 to 300°
BI Day March 10th 2016

## Slide 14: Cathode Assembly Concept overview
Support Cathode
Cathode :
(Provider SAES Getters)
Pierce Electrode
BI Day March 10th 2016

## Slide 15: Gun Concept overview (on CDD: AD_NECGA%)
Gun Flange
(DN160CF + SHV + Fil. connector )
Cathode Assembly
Grid Electrode
Anode Electrode
Each Potential is separate by
ceramic Isolator
Sleeve & Elastique compress ring
(total : 135mm height)
BI Day March 10th 2016

## Slide 16: Gun to Collector Design
Gun and collector design optimization performed with COMSOL Multiphysics
(G. TRANQUILLE)
BI Day March 10th 2016

## Slide 17: Collector Concept overview (on CDD : AD_TER% dimensions Ø 314 x 455mm)
Collector (Anode)
Ceramic Isolator
Reppeler Electrode
Ceramic Isolator
Collector flange
(DN200CF)
BI Day March 10th 2016

## Slide 18: Bake Out Brazing Stress Simulation modification & validation (ANSYS by EN-MME)
BI Day March 10th 2016
Chart: Steps
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Temp. (°C) | 22 | 300 | 22 | 300 | 22 | 300 | 22 | 300 | 22 | 300 | 22

## Slide 19: Planning ELENA Electrons-COOLER
GUN & COLLECTOR :
Ready
E-COOLING Assembling in the midle of ring ELENA
Connecting E-COOLER to ELENA ring
2015
Today
2016
2017
BI Day March 10th 2016
I hope it will live
Happily !!!!

## Slide 20: ELENA E-cooler Gun configuration on a lovely Test bench for validation.

## Slide 21: Soon ELENA E-COOLER Gun Beam tests (Test bench bat 236: Started by R.Sautier)

## Slide 22
Thanking to Electron Cooler team :
Gerard Tranquille
Alexandre Frassier
Lars Soby
Lars Varming J.
Marc Timmins
Antti Juhani K.
Alejandro Carlon Z.
Benjamin Moles
BE BI
BE OP
EN MME

## Slide 23: That’s All For Now
BI Day March 10th 2016
Next step for E-COOL Team :
A new E-COOLER for AD-RING for LS2

## Slide 26: The magnet system
Magnetic system components
Main cooler solenoid
Gun solenoid
Collector solenoid
Expansion solenoid
Squeeze coil at collector
2 x Toroid section consisting of
9 racetrack coils each
Various corrector coils to
ensure good field quality
Orbit correctors
Solenoid compensators

## Slide 27
Fine tuning the field

## Slide 28: Beam Ionisation Profile Monitors
Bottom Electrode
MCP
Top Electrode
Readout
e-
Ion +
e-
Residual Gas
Vaccum Chamber