## Slide 1: IPM Simulations at Fermilab
3-4 March 2016
Randy Thurman-Keup

## Slide 2: Nova Era Main Injector / Recycler
Recycler accumulates protons from Booster synchrotron
  8 GeV
  ~5 x 1013 protons
Main Injector receives beam from Recycler
  8 GeV incoming
  Up to 120 GeV outgoing
    Nova neutrino experiment
  588 53-MHz rf buckets
    each bucket ~18 ns
    1 x 1011 protons per bucket
    Bunch length typically ~1-3 ns
  Few millimeters transverse sigma

## Slide 3: MATLAB Simulation
Simulation tracks particles through arbitrary E and B fields
Uses interpolation to obtain the fields at any point from previously calculated field distributions
Propagates using a relativistic formula
Invert

## Slide 4: Matlab Simulation
Once the acceleration is determined, a discrete evaluation of the differential equation of motion is used to step the particles
The magnetic and electric fields are handled separately
  Magnetic contribution to the motion is only applied to the components perpendicular to the B field
  Magnitude of the velocity perpendicular to the B field is forced to be preserved, since the B field does no work
    This in particular helps with the tight spirals along the field lines

## Slide 5: Source Fields
The electric and magnetic fields of the bunch are calculated before hand for various bunch parameters
  Evaluated with proper time delay to represent the moving beam
Electric field of Fermilab IPM determined from a 2-D Poisson calculation
  Would like to create a more detailed 3-D electric field distribution using CST
  Try to explain discoloration on beam chamber out from ends of IPM active region
Magnetic field of Fermilab IPM from 3-D magnet model

## Slide 6: Ionization Particle Distributions
Ionized particle distributions are random in emission angle with 1/E2 energy distribution
  Don’t think random emission is correct
Not sure how to deal with low KE regime
  Dominated by quantum effects?
  Does it matter?

## Slide 7: Gated-on Expected Signal
From figure 7 of Sauli #, the number of primary ion pairs produced in one centimeter of a gas species i at one atmosphere of pressure by one minimum ionizing particle can be roughly parameterized as
Expressing this in terms of the proton bunch parameters and partial pressures in the beampipe one arrives at
At the peak of a Main Injector bunch, the number of ionization electrons is ~10 per anode strip (no MCP gain)
#F. Sauli, “Principles of Operation of Multiwire Proportional and Drift Chambers”, CERN 77-09, 3/5/77.

## Slide 8: Gated-on IPM
Particles originating from single point
(resolution contribution)
Elapsed time ~ 1.7 ns
Anode Strip

## Slide 9: Gated-on IPM
Bunch offset refers to x
Particles originating from single point
(resolution contribution)

## Slide 10: Gated-off IPM
Magnet with vertical B field
Cathode
Field shaping electrodes
Electron Suppression Grid
Wire mesh gate
Microchannel Plate (MCP)
Anode strips
B Field ~ 1 kg
E Field ~ 0 kV/m
OFF
Electrons propagate into or out of the page

## Slide 11: Gated-off Fields
X Component of E field
Y Component of E field

## Slide 12: Gated-off Motion
Electron drift along beam direction
Single particle
Particle origination point

## Slide 13: Gated-off Behavior
Bunch Centers
Drift Velocity
1.2 cm / 150 ns = 8 cm/ms
Compared to
10 cm/ms analytically estimated
Y motion vs time

## Slide 14: Gated-off Ion Paths
Elapsed time is ~1.5 ms
Ok, since ions do not go past the gating grid

## Slide 15: Gated Grid Test

## Slide 16: Conclusions
Use of Matlab simulation with fields generated from other sources allowed an evaluation of the gating grid behavior for the new IPMs at Fermilab
Matlab historically not the best choice for tracking since it is/was an interpreted language
  Works well if problem can be formulated in matrix form
Details of initial momenta of ionization products very crude
  Decided that details were probably only relevant for low momentum transfers
  Low momentum transfers quickly overcome by clearing and magnetic fields

## Slide 17: Extras

## Slide 18: Fermilab
Source and Linac
Booster Synchrotron
Antiproton
Accumulator and
Debuncher
Recycler and
Main Injector
Tevatron
n to Nova

## Slide 19: Magnet Measurements
0.002 T
0.004 T
Old Shunt
New Shunt
IPM Active Region

## Slide 20: Magnet Measurements
B Field Line
Maximum Deviation

## Slide 21: Magnet Measurements
B Field Line
Deviation from top to bottom
Average value of 200 mm could be hall probe rotation; corresponds to ~0.1 degrees

## Slide 22: MI Orbit Perturbation
Measured magnet integrated field is
Maximum displacement around the ring for the measured field integral is
For the Main Injector and the maximum is 50 and the tune, , is 0.43

## Slide 23: IPM Concept
Magnet with vertical B field
Cathode
Field shaping electrodes
Electron Suppression Grid
Wire mesh gate
Microchannel Plate (MCP)
Anode strips
500 mm spacing
Beam
(into page)
Ions
Electrons
Ionization Happens

## Slide 24: Gated IPM Concept
Problem with MCP is short lifetime
  Plate is using up lifetime whenever beam is in the machine and the IPM voltage is on
  Voltage takes a while to raise and lower
Would like to be able to gate the charge to preserve the MCP
  Stop the electrons and ions from reaching the MCP
  Allow the electrons and ions an escape path from the IPM active region
    i.e. no Penning traps

## Slide 25: Gated IPM Concept
  The force on a charged particle is
  Assume that and
  Solve the differential equations and one gets the usual solution of circular motion in the plane, constant motion along and a drift along which in this case is , i.e. along the beam
  Putting in the values for the electric and magnetic fields gives us a drift velocity of ~10 cm/ms along the proton beam direction
    The electrons will have drifted beyond the MCP in ~1-2 ms

## Slide 26: Magnetic Field in Simulation
Measured
Model
0.0004 T
0.0005 T

## Slide 27: Gated-on IPM
Magnet with vertical B field
Cathode
Field shaping electrodes
Electron Suppression Grid
Wire mesh gate
Microchannel Plate (MCP)
Anode strips
B Field ~ 1 kg
E Field ~ 1 kV/m
ON
Electrons spiral down helically