## Slide 1: Trim Test in SM18
S. Yammine in collaboration with H. Thiesen
TE-EPC-MPC
08/04/2016

## Slide 2: Contents
01 Introduction
02 Failure Scenarios and Critical Tests
03 Test Configurations
04 Proposition

## Slide 3
01
Introduction

## Slide 4: Introduction
11 T dipole is series with the main dipoles
Trim circuit is in parallel with the 11T

## Slide 5
02
Most Critical Failure Scenarios

## Slide 6: Failure Scenarios
Trim PC Failure – Failure 1
  Actions : Trim Crowbar + RB Crowbar + Stop PCs
  Worst Case Scenario : IMains = 6 kA - ITrim = -250
  Remark : The dipole is a current source (current inertia)
VDiode = Rtotal Itrim
Rtotal < 20 mΩ → Diode not triggered
Rtotal > 20 mΩ → Diode triggered
Diode triggered : what is impact on the system (diode voltage, cryogenics, quench) ?

## Slide 7: Failure Scenarios
FPA – Failure 2
  Actions : Trim Crowbar + RB Crowbar + Stop PCs + EESs
  Worst Case Scenario : IMains = 12.85 kA - ITrim = 34 A
  Remark : V11T = 12 V
Itrim = V11T /Rtotal
Rtotal > 60 mΩ → No overcurrent
Rtotal < 60 mΩ → Overcurrent
Overcurrent : 800-1000 A for a circuit sized for 300 A

## Slide 8
03
Test Configurations

## Slide 9: Test Configurations
Proposition of Test Configurations
Configuration 2 (On Two Clusters)
Configuration 1 -
Control of the 2 PCs together highly complex

## Slide 10: Test Configurations
Configuration 1 Simulation
Unstable Control : Result of connecting two voltage sources
Impossible to control 2 currents using this configuration
Instability

## Slide 11: Test Configurations
Proposed solutions : Voltage control on one PC + Current Control on the other.
Current control is still unstable! It will be worse on the test bench.
Configuration 1 Simulation
Instability

## Slide 12: Test Configurations
Configuration 2 Simulation
Configuration 2 (On Two Clusters) -
Control of the 2 PCs together possible
No problems for configuration 2
Questions to answer : What is the complexity to implement this solution via warm cables in SM18?

## Slide 13: Test Configurations
Testing Possibilities
Tests | Configuration 1 | Configuration 2
Trim Operation Verification (without second PC) | Yes | Yes
11T TF | Yes | Yes
Trim Overcurrent Test | No | Yes
Partial Bypass Diode Constraint | Yes | Yes
Complete Bypass Diode Constraint | No | Yes
2 PCs Test | No | Yes
Configuration 1
Configuration 2

## Slide 14
04
Proposition

## Slide 15: Proposition
Test Plan Study (April - September) :
  Test configuration alternatives
  Feasibility study
  Instrumentation required
  Test plan definition

## Slide 16: Thank you for your attention

## Slide 17: Test Configurations
Alternative Proposed Solutions :
Dummy Load : We need a high inductance (6kA). Possible ?
  We discussed putting a dummy load on the trim side : Alteration of the circuit property – The test will not be viable anymore.
  Putting a dummy load on the mains side is a possibility but we need a 6 kA inductance!
Voltage control + Current control : Control not possible.
Any other propositions are welcome