## Slide 1: LHCb: status and plans for the online system upgrade
Paolo Durante
paolo.durante@cern.ch
on behalf of the LHCb collaboration

## Slide 2: Outline
New readout system
  Slow & fast control
  Optical links
  Readout board
  Event building
  Data centre
Online mile-stones

## Slide 3: Run3 upgrade
Higher luminosity from LHC
Sub-detectors will upgrade
Removal of hardware trigger
  Inefficient at high luminosity
  New readout electronics
Filter farm will need to handle:
  Larger event size (~50KB to ~100KB)
  Larger event rate (~1MHz to ~40MHz)
New challenges for DAQ & High-Level Trigger
Detector
Hardware trigger
Data acquisition
High Level Trigger farm
CERN long term storage
Offline physics analysis
2020

## Slide 4: Run3 Online System
Dimensioning the system:
  ~10 000 optical links
    detector to surface (~350 m)
    up to 4.8 Gbps/link
  ~500 readout nodes (up to ~24 links/node)
  ~40 MHz event rate
  ~100 KB event size
High bisection bandwidth in event builder network
  ~32 Tb/s aggregate bandwidth
  Leverage emerging 100G technologies
Global configuration and control via ECS subsystem
Global synchronization via TFC subsystem
Detector front-end electronics
Event Builder network
Event Builders (PC + readout board)
Eventfilter Farm
~ 80 subfarms
UX85B
Point 8 surface
subfarm switch
TFC
x500
subfarm switch
Online storage
Clock & fast commands
throttle from PCIe40s
Clock & fast commands
6 x 100 Gbit/s
6 x 100 Gbit/s

## Slide 5: ECS (Experiment Control System)
  Controls and monitors all subsystems
    DAQ, TFC, HLT, farm…
  Continuity from current implementation
    JCOP / DIM / WinCCOA / SMI++ / Recipes
  Already able to drive current readout board prototype, from input to output
  Frontends rely on GBT-SCA hardware by EP-ESE
  Low-level components are being implemented
Test UI
HW Description UI
FPGA
Firmware
DIMServer
PCIe40
PCIe driver P
PCIe library P
GbtServ
PCIe
Host PC
Control PC
WinCC-OA
Operation UI

## Slide 6: TFC (Timing & Fast Control)
Current status
  Already integrated in firmware
  Uses same readout board hardware as the DAQ (PCIe40)
  Can send fast commands to frontends
    SciFi, UT, Muon ASICS already being tested
  Programmable internal throttle for bandwidth regulation
Ongoing work
  PON (Passive Optical Network) technology integration (with EP-ESE)
  Clock phase tests on readout board (with CPPM)
  Continue feedback and compliance testing with frontend experts

## Slide 7: Long-distance optics
Counting room on surface
  Power, cooling, space constraints in underground area
  ~350 meter distance
Based on EP-ESE technology
  Rad-hard Versatile Link on frontends
  Initially qualified for ~100m
Fiber infrastructure by EN-EL
  Pilot installation at end 2014
Loopback tests in 2015
  ~9 months, ~700 meters
  Avago MiniPOD transceivers
  Bit Error Rate < 10-18
  Full system equivalent: < 5 errors/day
  LHCC milestone
Continued tests in 2016
  Versatile TX on frontend prototype
  MiniPOD RX on readout board prototype
MiniPOD™
VTRx

## Slide 8: Readout boards / Event builders
Detector front-end electronics
Event Builder network
Event Builders (PC + readout board)
Eventfilter Farm
~ 80 subfarms
UX85B
Point 8 surface
subfarm switch
TFC
x500
subfarm switch
Online storage
Clock & fast commands
throttle from PCIe40s
Clock & fast commands
6 x 100 Gbit/s
6 x 100 Gbit/s

## Slide 9: Readout board hardware (PCIe40)
PCI Express add-in card
  Altera Arria10 FPGA
  100Gbps DMA engine to event-builder memory
High-density optical IO
  Up to 48 transceivers (Avago MiniPODs)
  Reuse same HW for timing distribution system
Decouple FPGA from network
  Maximum flexibility in network technology
Exploit commercial technologies
  PCI Express Gen3 interconnect
  COTS servers designed for GPU acceleration
2nd generation readout board
  Developed at CPP Marseille
Pre-production launched
  Ready end of Q2
Market survey completed
  Tender in H2 2016

## Slide 10: Readout board firmware
Common architecture for all subdetectors
Joint effort of LAPP, CERN, CPPM
Highly configurable through frontend-specific parameters
Handles ECS, TFC & DAQ, subdetector-specific logic
Event ID
TFC Processing
Error Recovering
Data Processing
MEP building
BCID Alignment
Raw Data Decoding
Computer Network
CCPC
resets
ECS - BAR0
x6
xM
xM
Low Level Interface
Low Level Interface
If GBT mode
If Widebus mode
Throttle
SOL 40
xM
xM
xM
TFC decoder
TFC data
ODIN 40
FE(s) data
xM
xN
xM
xN
x1
N+M = 24

## Slide 11: Readout unit dataflow
A single Readout unit must sustain ~400Gbps IO bandwidth
Optimize memory bandwidth
  Design for zero-copy operations and RDMA over the network
  Organize dataflow according to topology and IO resources
  Exploit full network bandwidth
PCIe40
DAQ
network
FILTER
network
CPU
CPU
Memory
Memory
PCIe40
DAQ
network
FILTER
network
CPU
CPU
Memory
Memory

## Slide 12: Event-building software (DAQPIPE)
Recreate distributed event-building dataflow of LHCb Run3
Modular architecture, “drivers” for each network technology under evaluation
Leverage existing HPC sites to assess scalability
Close collaboration with the industry through CERN OpenLab
Already achieving ~86Gbps with Infiniband EDR
  Meets our target
  Reduced scale setup
Off-site tests for Infiniband EDR and Intel Omni-Path currently ongoing…
Event-builder core
Ethernet
driver
InfiniBand
driver
Omni-Path
driver
Readout module
Dataflow
manager
Builder
unit
Data
generator

## Slide 13: 128node InfiniBand scalability (CINECA)
Performance limited
by non-exclusive
utilization of cluster

## Slide 14: Future data centre at Point 8
 | Turnkey commercial solution (Requires minimal support from CERN engineering groups) | Leverage existing infrastructure at Point 8
Building | Buy pre-fabricated containers from a commercial supplier | Accommodate the farm in an existing building (SX8 hall)
Cooling | Cooling solution depends on the vendor (e. g. free air cooling) | Passive rear-door heat exchangers using primary water from existing cooling towers Compatible with DCLC for hot spots Test setup at the pit to evaluate performance with on site “warm” cooling water
A review to decide the most cost-effective solution will take place in April.

## Slide 15: Online mile-stones
Q1 2016: long-distance fibres validation (successful)
Q2 2016: event-building with 32-port switch (successful)
  Thanks to the Bologna, CNAF and Ferrara teams
   would be good to repeat this in a lab-setup (better tuning etc…)
Q2 2016: event-builder scalability to 600 nodes
  Achieved with 128 nodes, larger scale test still this year need to get a slot from external HPC sites (France, US…)
Q2 2017: data-centre solution defined
Q4 2017: full DAQ network test
Q3 2018: network technology decision
Q3 2019: ready for commissioning

## Slide 16: Thank you for your time

## Slide 17: Setup
Review of TDR suggested a test installation at P8 to ensure the viability of the long distance read-out
Installed 3 Trunk cables with 144 fibers each from different providers at P8
  1 x 144 Fibers from Fibernet, pre-connectorized
  1 x 144 Fibers from CERN, pre-connectorized
  1 x 144 Fibers from CERN, spliced
All 432 Fibers have been tested and have expected Attenuation
Currently Measuring the spliced fibers
  Worst case scenario due to additional attenuation of splice point
Testing on loop with 2 x 350m
  Higher attenuation than in final setup
  AMC40 transmitter has more optical power though
  Longer fiber just about compensates for the stronger transmitter
17
AMC40
Patch Panel
SX8
(Gas Building)
Patch Panel
UX8
Bunker
BER tester
~ 350 m

## Slide 18: Result so far
Setup has been running for over 9 months now
1018 bits tested so far
0 Errors
BER < 10-18 with 95% confidence
18
CL = Confidence Level
N = Number of bits tested
E = Errors
BERs = Specific Error Rate
Confidence | 63% | 74% | 95%
Aggregated BER | < 3.1 x 10-18 | < 4 x 10-18 | < 9 x 10-18
Error rate for 12k fibers | < 16 / day | < 20 / day | < 45 / day

## Slide 19: Timing distribution at LHCb
VELO
L1 FE
TTCrx
VELO
L0 FE
TTCrx
VELO
L0 FE
TTCrx
ODIN
Readout Supervisor
ODIN
Readout Supervisor
Local trigger
L0
ODIN
Readout Supervisor
THOR
TFC Switch
MUNIN
Throttle Switch
TTCtx
Optical transmitter
TTC system
RF2TTC
LHC clock
MEP Req. (GbE)
L0 (LVDS)
Trigger
splitter
VELO
L0 FE
TTCrx
VELO
L0 FE
TTCrx
VELO
TELL1
TTCrx
TTCoc
Optical splitter
VELO
L1 FE
TTCrx
VELO
L0 FE
TTCrx
VELO
L0 FE
TTCrx
VELO
L0 FE
TTCrx
ECAL
L0 FE
TTCrx
ECAL
TELL1
TTCrx
HUGIN
Throttle OR
MEP Req. (GbE)
FREJA
TTC monitoring
HUGIN
Throttle OR
BPIM
TTCtx
Optical transmitter
TTCtx
Optical transmitter
TTCtx
Optical transmitter
TTCtx
Optical transmitter
TTCoc
Optical splitter
TTCoc
Optical splitter
TTCoc
Optical splitter
LHC orbit
TTCoc(BST)
BST
MEP Requests
Unidirectional
1:32 max split ratio
Low bandwidth
Obsolete components
Very low payload for Bunch synchronous data

## Slide 20: Upgrade proposal 1:TTC over GBT
Courtesy: Federico Alessio (CERN)
From TFC point of view, we ensure constant:
LATENCY: Alignment with BXID
FINE PHASE: Alignment with best sampling point
Some resynchronization mechanisms envisaged:
Within TFC boards
With GBT
  No impact on FE itself
Loopback mechanism:
re-transmit TFC word back
allows for latency measurement + monitoring of TFC commands and synchronization

## Slide 21: Upgrade proposal 2:TTC over PON
OLT
ONU1
ONU2
ONU3
FTTH
FTTC
FTTB
1
1
1
2
3
3
1490nm
2
2
2
1
1
1
3
3
3
1
1
1
2
2
2
3
3
3
1310nm
2
2
2
1
1
1
3
3
3
1
2
B
1
1
3
1
2
B
1
1
3
1
2
B
1
1
3
1
2
B
1
1
3
B
3
B
B
Courtesy S. Baron et al. (CERN)
https://indico.cern.ch/event/400951/
Major topology of growing Access Network Market known as:
  Fiber To The X (FTTx) (http://en.wikipedia.org/wiki/Fiber_to_the_x)
Point-to-MultiPoint (P2M)
One single fibre in charge of both downstream and upstream transmissions (using wavelength multiplexing technique)

## Slide 22: TTC-PON
Standard: XG-PON1
Fixed latency downstream
Line rate
  Down: 9.6 Gb/s
  Up: 2.4 Gb/s
Wavelength:
  Down: 1577nm
  Up: 1270nm
Bidirectional
Range: 1-1000m
Split ratio: 1:128
Error detection
OLT: Optical Line Terminal
ONU: Optical Network Unit

## Slide 23: AMC40 readout board
Philosophy: one common board for DAQ and timing/control
1st generation readout board
  Developed at CPP Marseille
Mezzanine for ATCA crate
Altera Stratix V FPGA
≤36 bidirectional optical links
  Avago MiniPODs
  GBT / GWT / 10GbE protocols
Produced and made available to the collaboration (MiniDAQ1)
Firmware designed for migration to 2nd generation readout board

## Slide 24: PCIe40 status
Current status
  Low-Level Interface available
    Slow control through PCIe
    100Gbps DMA
    On-board communication (I2C, SPI)
    Filtered PLL clock
    CvP (programming via PCIe)
    Temperature and current monitoring
  New custom heat-sink design
  Procurement ongoing after tender
Next plans
  x24 GBT integration
  PON tests for timing distribution
  Optical links characterization
    Eye aperture
    BER
  Cooling characterization
    f( firmware, airflow, heat-sink )
  Monitoring via IPMI

## Slide 25: PCIe Gen3 DMA performance
1 interface (optimized)
2 interfaces (unoptimized)
Chart: Time (s)

## Slide 26: Firmware status
AMC40
Readout over GBT / WideBus
Fixed-size frontend protocol
6 optical links
Front-end configuration via GBT-SCA
Data monitoring inside FPGA
UDP output protocol over 10GBASE-R
Embedded FE data generator
Data verification outside FPGA
Configurable data rate throttle
Variable-size FE protocol
PCIe40
… all of the previous, plus:
HW-specific low level interface
PCI Express Gen3 DMA interface & driver
Increase number of optical links
Integrate LLI & DMA into firmware
Implement remaining frontend protocols

## Slide 27: Event-building software performance
DAQPIPE now supports following APIs:
Libfabric
MPI
TCP
Implemented automatic benchmarking and reporting
(with web-based interface)
On-the-fly monitoring (htopml)
Benchmarks of
Intel Omni-Path
Infiniband EDR
currently in progress!
Already observing 86 Gb/s on EDR