## Slide 1
CLIC News

## Slide 2
CLIC accelerating structure
Outside
Inside
6 mm diameter beam aperture
11.994 GHz X-band
100 MV/m
Input power ≈50 MW
Pulse length ≈200 ns
Repetition rate 50 Hz
Micron–precision disk
25 cm
HOM damping
waveguide

## Slide 3
Breakdown rate
CLIC accelerating structure specifications include:
a gradient 100 MV/m,
a pulse length 180 ns,
and breakdown rate, BDR, 3x10-7/pulse/m.
BDR is the fraction of pulses which have a vacuum arc. Breakdown currents and lost acceleration result in lost luminosity on that pulse.
The three quantities are related to each other:

## Slide 4
CPI 50MW 1.5us klystron
Scandinova Modulator
Rep Rate 50Hz
Beam test capabilities
Xbox-1
Xbox-2
Xbox-3
Previous tests:
2013 TD24R05 (CTF2)
2013 TD26CC-N1 (CTF2)
2014-15 T24 (Dogleg)
Ongoing test:
Aug2015- TD26CC-N1 (Dogleg)
CPI 50MW 1.5us klystron
Scandinova Modulator
Rep Rate 50Hz
4x Toshiba 6MW 5us klystron
4x Scandinova Modulators
Rep Rate 400Hz
Previous tests:
2014-15 CLIC Crab Cavity
Ongoing test:
Sep2015- T24OPEN
Medium power tests (Xbox-3A):
2015 3D-printed Ti waveguide
2015 X-band RF valve
OPERATIONAL
OPERATIONAL
COMMISSIONING February 2016
Testing Capability at CERN
Major increase in testing capacity!

## Slide 5
X-band test stands at KEK and SLAC
Nextef at KEK
ASTA at SLAC
Tsinghua University and SINAP have both ordered 50 MW X-band klystrons.

## Slide 6
Performance summary at CLIC specifications

## Slide 7
Conditioning
Accelerating structures do not run right away at full specification – pulse length and gradient need to be gradually increased while pulsing. Typical behaviour looks like this:
4 million pulses per day at 50 Hz
Pulse length steps
BDR falls during flat E run

## Slide 8
Scaled gradient vs cumulative number of PULSES
Scaled gradient vs cumulative number of BREAKDOWNS
Comparing conditioning
Pulses
Breakdowns
Comparison of the conditioning of high gradient accelerating structures
Alberto Degiovanni, Walter Wuensch, and Jorge Giner Navarro
Phys. Rev. Accel. Beams 19, 032001 (2016) - Published 4 March 2016

## Slide 9
Longer term operation
7 months @ 50 Hz
30 days @ 1 kHz
pulsed dc
rf

## Slide 10
Long term evolution of BDR
rf
pulsed dc
Pulses

## Slide 11
Gradient Perspectives
un-damped
damped (mostly)

## Slide 12
New baseline structure: major objective
R = 0.5mm
R = 2.5mm
Width=11mm ->10.1mm
Opening=8mm->7.8mm
Analysing results and re-optimizing CLIC, we have a new baseline structure.
We expect to get to 120 MV/m unloaded, closing the gap we expect from beam loading.
Mechanical design done. To be built and tested.

## Slide 13
Symmetry plane structures
Structures in parts along symmetry planes have significant potential advantages - cost, joining, heat and chemical treatment, materials. Does require 3-D micron precision milling which is now possible.
Early tries with quadrants yielded unsatisfactory results, but don’t believe this was end of story. We’re back!
vs.

## Slide 14
Structure in halves – testing in XBox-2
CERN design and high-gradient testing, SLAC fabrication.
Hard copper version under preparation.

## Slide 15
https://indico.cern.ch/event/358352/session/7/contribution/40
Applications of X-band acceleration
Linear collider - TeV
XFEL – 1 to 10 GeV
Compact Compton source
few 10s MeV
Thompson/Compton
source – few 100s MeV
CLIC
Tsinghua, China
Australian Light Source
Smart*Light, NL
50MW

## Slide 16
XbFEL H2020 design study to be resubmitted in 2017.
XBox3-B to Australian light source, Monash University proposal.
X-band deflector and accelerating structure testing for X-band option for XFEL at SINAP.
X-band linearizer system with Fermi@Trieste and SwissFEL
Selected collaborations on applications of X-band and high-gradient

## Slide 17
Trans-National Access for Xboxes in Aries (EUCARD3) proposal.
SMART*Light, Dutch proposal for compact Compton X-ray source.
Transverse deflector based on 50 MW klystron for SINBAD at DESY.
X-Band Thompson source energy upgrade at Tsinghua University.
Medical linac structures – TERA/KT and Lancaster/Cockcroft.
Selected collaborations on applications of X-band and high-gradient - continued
We gain experience with help and resources of other projects! For example XFEL-type accelerating structures are similar in gradient and iris aperture to CLIC 380 GeV structures.

## Slide 18
HG2016
https://indico.hep.anl.gov/indico/conferenceDisplay.py?ovw=True&confId=963