## Slide 2: Cryogenic Safety Rules and Guidelines at CERN
Simon Marsh HSE-SEE-XP

## Slide 3: GSI-M-4 Cryogenic Equipment
In accordance with its intergovernmental status, CERN establishes and updates Safety Rules to implement its Safety Policy
Prior to 2015, pressurised cryogenic equipment was covered by the General Safety Instruction for pressure equipment
In the June 2015 refresh of the mechanical safety rules General Safety Instruction GSI-M-4 was released, as a response to the specific needs of cryogenic equipment at CERN
Available on the CERN Safety Rules website: www.cern.ch/safety-rules

## Slide 4: GSI-M-4 Cryogenic Equipment
Defines the minimum safety requirements related to the life cycle of cryogenic equipment
  Cradle to grave approach
Pressurised and non-pressurised equipment used at a temperature equal to or lower than 123.15 K
Valid for all new equipment and equipment brought onto the CERN site from elsewhere
  Cryogenic equipment already present on the CERN site when GSI-M-4 came into force requires implementing its provisions by June 2017
Defines and requires an equipment “Safety File”
Aligned, as far as possible, to existing standards

## Slide 5: GSI-M-4 Cryogenic Equipment
Design, manufacture and procurement
  Primarily based on European Directives for pressure equipment and transportable pressure equipment
  Use of harmonised European standards
    Use of other technical standards is subject to approval by HSE Unit
  CE marking
  Declaration of conformity
  Factory acceptance tests, where applicable
  Instruction manual

## Slide 6: GSI-M-4 Cryogenic Equipment
Installation, acceptance, commissioning and use
  Protection by safety devices against overpressure
  Risk assessment for oxygen deficiency hazards
    Compensatory measures in place before use
  Checks and proof tests
    By HSE Unit if maximum allowable pressure PS > 0.5 bar
    By owning organic unit for others
  Allocation of a CERN identification number
  Operating procedures in compliance with the instruction manual and with emergency procedures
  Use by authorised, competent and trained persons only
  Operated within its normal operating parameters and within its next inspection/requalification date

## Slide 7: GSI-M-4 Cryogenic Equipment
Periodic inspections
  External visual inspection
  Requalification for transportable pressurised cryogenic equipment
  Functional test of safety valves
    Test-bench verification of set pressure and leak tightness
    3 or 5 year interval depending on fluid, external fouling, flammability, type of equipment that is being protected, type of relief valve.
Maintenance
Recommissioning
  Part of Management of Change
Decommissioning / dismantling

## Slide 8: Major Safety Implications
Specialists from the HSE Unit can decide to specifically define equipment and installations as being ‘liable to have major safety implications’
  This decision cannot be made by the Departments themselves
May include cryogenic equipment
  Not compliant with the applicable European directives, or
  of a highly complex design, or
  using reduced safety factors, or
  requiring special conditions of use, or
  using unconventional materials or manufacturing technologies, or
  presenting a high-level hazard for people, the environment or other installations in the event of failure.
Requires HSE Unit approval for each stage of the lifecycle and specific safety checks
HSE Unit can define additional safety requirements in collaboration with the owning organic unit
Requires formal Safety Clearance from the HSE Unit prior to operation

## Slide 9: Safety Guidelines
Safety Guideline SG-M-4-0-1 Cryogenic Equipment issued in August 2016 to support GSI-M-4
Provides guidance on the following aspects:
  Cryogenic hazards
    Personal safety
      Asphyxiation
      Effect of cold temperatures
    Process safety and asset integrity
      Overpressure
      Brittle fracture
      Icing
      Oxygen enrichment
  Risk assessment
  Prevention / protection
  Equipment compliance
Available on the CERN Safety Rules website: www.cern.ch/safety-rules

## Slide 10: Safety Guidelines
Safety Guideline SG-M-4-0-2 Oxygen Deficiency Hazards to be published soon
Provides guidance on the following aspects:
  Risk assessment methodology and aspects to consider
  Control and mitigation measures
  Effects of exposure to oxygen deficient atmospheres
  Definition of evacuation time
Will be made available on the CERN Safety Rules website: www.cern.ch/safety-rules