## Slide 1: VMM3 L0 Data Acquisition Logic
Sorin Martoiu

## Slide 2
LAT. FIFO (64)
LAT. FIFO (64)
LAT. FIFO (64)
LAT. FIFO (64)
L0 CH FIFO (16)
Trigger
L0 SEL
L0 SEL
L0 SEL
L0 CH FIFO (16)
L0 CH FIFO (16)
L0 CH FIFO (16)
EV BUILD
L0 SEL
BCID FIFO (32)
FE
PD/ADC
FE
PD/ADC
FE
PD/ADC
FE
PD/ADC
64-deep raw data FIFO
  The effective latency accepted scales with the incoming hit rate
  For max hit rate 4MHz/channel* max latency is 12.8us
Online (25ns) data selection circuit for each channel
16-deep Selected Data FIFOs to allow time to serialize data to output
32-deep Trigger Timestamp FIFO stores the timestamp of each incoming trigger and is transmitted in the output format
Operation of the L0 Data Acquisition Logic. Overview

## Slide 3
LAT. FIFO (64)
LAT. FIFO (64)
LAT. FIFO (64)
LAT. FIFO (64)
L0 CH FIFO (16)
L0
L0 SEL
L0 SEL
L0 SEL
L0 CH FIFO (16)
L0 CH FIFO (16)
L0 CH FIFO (16)
EV BUILD
L0 SEL
BCID FIFO (32)
FE
PD/ADC
FE
PD/ADC
FE
PD/ADC
FE
PD/ADC
Selected Data
Dummy Data
Trigger Timestamp
Operation of the L0 Data Acquisition Logic
Data Selection
For each incoming trigger pulse (25ns) the data in the raw FIFO is selected based on the timestamp included in raw data
  A configurable acceptance window of 1..8 x 25ns can be used
  If two consecutive triggers have their windows overlap, data is copied to both triggers
In the Selected Data FIFO, dummy data is written for channels which does not have data in the trigger window. Dummy data is not readout.

## Slide 4
LAT. FIFO (64)
LAT. FIFO (64)
LAT. FIFO (64)
LAT. FIFO (64)
L0 CH FIFO (16)
Trigger
L0 SEL
L0 SEL
L0 SEL
L0 CH FIFO (16)
L0 CH FIFO (16)
L0 CH FIFO (16)
EV BUILD
L0 SEL
BCID FIFO (32)
FE
PD/ADC
FE
PD/ADC
FE
PD/ADC
FE
PD/ADC
Selected Data
Dummy Data
Trigger Timestamp
Operation of the L0 Data Acquisition Logic
Data Serialization
The Event Builder builds packets for each trigger and serializes the data to the output
Each packet contains:
  the Trigger Timestamp
  Hit Data for each channel which has a hit in the trigger window (dummy data is discarded)
  Hit Data includes differential timestamp relative to the Trigger Timestamps