Implementing the
GBT data transmission protocol
in FPGAs
Sophie	BARON	(CERN)
Jean-Pierre	CACHEMICHE	(CPPM)
Frédéric	MARIN	(CPPM)
Paulo	MOREIRA	(CERN)
Csaba	SOOS	(CERN)

---
Outline
Introduction
GBT ASIC presentation (reminder)
Typical architecture of use
GBT protocol implementation on FPGA
Test setup and results
Further work
Reference design availability
Conclusion

---
Introduction
- Aim of our study:
  - Interoperability between GBT chip and FPGAs must be guaranteed
  - Check the compatibility of FPGAs (Xilinx and Altera) with the GBT protocol
- Warning:
  - This presentation will give some results and numbers concerning the implementation of the GBT protocol on Altera and Xilinx FPGAs but be aware that they cannot be used in any case as a tool of comparison of the two vendors

---
GBT ASIC presentation
Motivations
  - Radiation hardened chip compatible with Super LHC luminosity
  - Reduce the number of optical fibres installed
  - Concentrate R&D effort
GBT ASIC characteristics
  - General purpose bidirectional optical serial link running at 4.8 Gbps, on which transit:
    - Data
    - Trigger, Timing and Control
    - Slow control
  - Custom transmission protocol
    - Able to correct up to 16 consecutive erroneous bits

---
Typical architecture
GBT protocol needs to be compatible with the FPGAs
and vice versa

---
Frame description
SLHC frame: 120 bits @ 40 MHz ≡ 4.8 Gbps
User field: 82 bits ≡ 3.28 Gbps
Reed-Solomon overhead
allowing to correct up to 16 consecutive erroneous bits
H: Header, 4 bits
SC: Slow Control 4 bits
GBT control 2 bits (80 Mb/s)
Slow control 2 bits (80 Mb/s)
D: Data (3.2 Gbps)
FEC: Forward Error Correction (32 bits)
Line efficiency: 68%
4
80
32
4

---
GBT protocol – Encoding scheme overview
The frame is shifted out MSB first, that is: FRM<119>, FRM<118>, … FRM<0> (The header shifts out first)
Interleaving
RS Encoding
Scrambling
H<3:0>
SC<3:0>
D<20:0>
D<79:63>
SCR<20:0>
SCR<83:63>
SCR<41:0>
FEC<15:0>
SCR<43:42>
SCR<83:44>
FEC<31:16>
H<3:0>
D<41:21>
D<62:42>
SCR<41:21>
SCR<62:42>
FRM<119:0>
FRM<119>
FRM<0>
4
60
H<3:0>
SC<3:0>
D<79:0>
FRM<119:0>
80
21
21
21
21
21
21
21
21
4
Scrambler
Scrambler
Scrambler
Scrambler
44
44
60
120
RS Encoder
RS Encoder
Interleaving

---
FPGA implementation
FPGA devices from Altera or Xilinx embed serial transceivers configurable for several standard telecommunication protocols (XAUI, Gigabit Ethernet, PCIe, ...)
- But:
  - Transceivers include neither scrambler nor Reed Solomon encoder nor interleaver
  - Their word aligner/comma detection module are not flexible/configurable enough to fit our needs
  - The width of the parallel interface of the ser/des can only take predefine values
- So the way to implement the GBT protocol on FPGA is:
  - To use the transceiver in the most basic way (ser/des function)
  - To implement custom function in logic cells
Hard block configured
by vendor specific
config file
Scrambler
Reed
Solomon
Encoder
Interleaver
MUX
&
Clock
domain
crossing
Serializer
84 bits
40 MHz
88 bits
40 MHz
120 bits
40 MHz
4 bits header
120 bits
40 MHz
40 bits
120 MHz
4.8 Gbps
Deserializer
Pattern
detect
&
Word
aligner
4.8 Gbps
Descrambler
Reed
Solomon
Decoder
Deinterleaver
DEMUX
&
Clock
domain
crossing
84 bits
40 MHz
88 bits
40 MHz
120 bits
40 MHz
4 bits header
120 bits
40 MHz
40 bits
120 MHz
120 MHz
40 bits

---
Pattern search for data alignment
- The pattern search and alignment functions are achieved with two entities:
  - A barrel shifter allowing to bit shift the incoming data
  - A state machine looking at the expected header position in the frame and giving the “locked” status
Word boundary
Header
...
...
Locked status
Deserializer
Demux
Barrel
shifter
Pattern
search
state
machine
40bits
4.8Gbps
40bits
40bits
120bits
120MHz
120MHz
120MHz
40MHz
Bit slip command
From Giulia
Papotti's thesis
Out
Of Lock
In Lock
23 consecutive correct headers
4 incorrect headers
within 64 successive frames
1
0
0
1
1
0
1
0
0
1
0
1
1
0

---
Resource usage
Implementing several channels leads to an important usage of logic cells resources
The Reed Solomon decoder takes most of the resources
Resource usage (in ALMs*) by entity for one
full channel implemented on Stratix II GX
ALM: Adaptative Logic Module (contains 2LUTs and 2 registers)

---
Optimization
- Resource sharing technique:
  - Use one decoding module for n channels by increasing its working frequency by n
  - Gain not as significant as expected because multiplexing and demultiplexing functions use many registers
De-
serializer
Pattern
detect
&
Word
aligner
4.8 Gbps
De-
scrambler
Reed
Solomon
Decoder
De-
interleaver
DEMUX
&
Clock
domain
crossing
84bits
40MHz
84bits
120MHz
120bits
120MHz
120bits
40MHz
40bits
120MHz
40bits
120MHz
DEMUX
MUX
De-
scrambler
De-
scrambler
De-
serializer
Pattern
detect
&
Word
aligner
4.8 Gbps
De-
interleaver
DEMUX
&
Clock
domain
crossing
120bits
40MHz
40bits
120MHz
40bits
120MHz
De-
serializer
Pattern
detect
&
Word
aligner
4.8 Gbps
De-
interleaver
DEMUX
&
Clock
domain
crossing
120bits
40MHz
40bits
120MHz
40bits
120MHz
84bits
40MHz
84bits
40MHz
84bits
40MHz
120bits
40MHz
120bits
40MHz
120bits
40MHz
84bits
40MHz
84bits
40MHz

---
Optimization results for 12 links
No optimization
Optimization: one decoder for 3 links
51% occupancy
ALMs of StratixIIGX90
40% occupancy
ALMs of StratixIIGX90

---
Tests
Tests of implementation have been done using two different platforms:
Xilinx Virtex 5 ML523 platforms
Altera StratixIIGX PCI express development board

---
Tests (2)
120MHz ref
PLL
PLL
Altera (SIIGX based)
Xilinx ML523 (V5FXT based)
Generator
Error counters
No error detected
during 2 hours of running
120MHz ref generated by an AGILENT JBERT N4903
Electrical (SMA) to optical mezzanine on Xilinx side
Optical transceivers SFP+ 1300nm types from MergeOptics
Generator and Error detection controlled and monitored through ChipScope.
Generated words: constants or flying bits
Scrambler
RS
Encoder
Interleaver
MUX
&
Clock
domain
crossing
Serializer
84bits
40MHz
88bits
40MHz
120bits
40MHz
120bits
40MHz
40bits
120MHz
4,8Gbps
Deserializer
Pattern
detect
&
Word
aligner
4,8Gbps
Descrambler
RS
Decoder
Deinterleaver
DEMUX
&
Clock
domain
crossing
84bits
40MHz
88bits
40MHz
120bits
40MHz
120bits
40MHz
40bits
120MHz
40bits
120MHz
Scrambler
RS
Encoder
Interleaver
MUX
&
Clock
domain
crossing
Serializer
84bits
40MHz
88bits
40MHz
120bits
40MHz
120bits
40MHz
40bits
120MHz
4,8Gbps
Deserializer
Pattern
detect
&
Word
aligner
4,8Gbps
Descrambler
RS
Decoder
Deinterleaver
DEMUX
&
Clock
domain
crossing
84bits
40MHz
88bits
40MHz
120bits
40MHz
120bits
40MHz
40bits
120MHz
40bits
120MHz

---
Measurements
Xilinx and Altera platforms both show excellent performances
Stratix II GX & SFP+ with GBT protocol
Virtex5 FXT & SFP+ with GBT protocol
Total Jitter @BER10-12 = 78 ps pkpk
Total Jitter@BER10-12 = 90 ps pkpk
Test conditions:
  - ML523 (Virtex 5 FXT) for Xilinx, Stratix II GX PCIe for Altera both powered by the power supply given in the kit
  - Reference clock generated by J-BERT 4903A from Agilent
  - Same SFP+ 1300nm optical transceiver from MergeOptics, 50 cm of optical fiber, for both platforms
  - Measurements made with Lecroy SDA100G sampling scope equipped with 10 GHz optical sampling head
Remark: the Stratix II GX performances are slightly lower because the reference clock could not be as ideally connected as for the Virtex 5 due to the plateform connectivity

---
Further work
- Continue to optimize the implementation:
  - One idea could be to pipeline Reed Solomon decoder to be able to multiplex more channels
Test the compatibility with real GBT device
Implement this protocol on the latest devices (StratixIV GX and Virtex 6)
Study implementation of constant phase/latency of embedded transceivers (see Ioannis Papakonstantinou slides)

---
Design availability
Reference designs implementing one or several full channels for both Xilinx and Altera devices exist
- Firmware starter kit will be offered to the interested people. It will contain:
  - Source code for both implementations (Altera & Xilinx)
  - Documentation
  - Basic support
  - You will just need to provide the hardware
- You just need to contact Sophie Baron (Sophie.Baron@cern.ch) giving
  - Your name
  - The description of your project

---
Summary
- First time the GBT protocol runs on real platforms
  - These platforms will be used to test the GBT ASIC
- GBT protocol runs on both major FPGAs vendors
  - Interoperation proven
Further resource usage optimization under investigation
Firmware starter kit will be available soon
References:
  - Giulia Papotti's thesis: https://espace.cern.ch/GBT-Project/GBTX/Publications/Forms/AllItems.aspx
  - Csaba Soos and Paulo Moreira slides @ TWEPP09
  - GBT project web site: http://cern.ch/proj-gbt

---
Thanks for your attention

---
Back up slides

---
Scrambler
- Aim of the scrambling:
  - Reduce the occurrence of long sequences of '0' (or '1') only;
  - Achieve a good DC-balance
- Scrambler characteristics:
  - Doesn't add any redundancy/overhead
  - Has a latency of 1 clock cycle
  - Generates a pseudo random signal
83
21 bits Scrambler
21 bits Scrambler
Input:
User field, 84 bits
Output:
84 bits (scrambled)
21 bits Scrambler
21 bits Scrambler
0

---
Reed Solomon encoder
- Aim of the Reed Solomon encoding:
  - Protect the data against transmission errors
- Reed Solomon encoder characteristics:
  - Composed of 2 RS encoder (15,11), symbol = 4 bits
  - Only combinatorial logic
  - Allows to correct up to 2 symbols (8 consecutive bits for example)
120 bits output:
88 bits input:
4 bits header
119
87
84
Image of the 2 inputs of 44 bits
83
44
60
RS encoder (15, 11)
+
+
44
84 bits scrambled
43
44
60
RS encoder (15, 11)
2 fields of 16 redundant bits
0
0

---
Interleaver
- Aim of the interleaving:
  - Improve the capacity of the code to correct long burst of errors
- Interleaver characteristics:
  - Interleaving made at a symbol level (4 bits)
  - Only “routing”, no clock cycle
  - Increases the code correction capability from 2 to 4 consecutive symbols
    (16 consecutive bits) without increasing overhead
119
119
Header always in the right place
Input:
120 bits from
the RS encoding
Output:
120 bits with interleaved symbols
0
0