## Slide 1: The UT Electronics Slice Test Plan & Preparation At Syracuse
Jianchun Wang
INFN Milano LHCb UT Workshop
May 17-19, 2016

## Slide 2: Motivation of Electronics Slice Test
The UT electronics slice test system is crucial in validating the whole readout scheme, testing and optimizing design of major components.
We want to test functionalities of individual components and measure their performance when signal and LV/HV powers are routed according to the baseline design of the UT readout system.
Individual studies include:
  Check the data integrity in the system, measure signal to noise ratio with baseline configuration.
  Study power connection, grounding & shielding schemes, measure signal coupling, noise pickup with different configurations.
  Check digital signal quality in the flex cables, pigtails, & optical fibers by measuring eye diagram and bit error rate.
  Test ECS protocol and determine: whether the single-ended I2C works with the expected voltage drop; whether it introduces large noise to the signal; & whether an alternative protocol is needed.

## Slide 3: Major Components of The Readout System
Regulators
MCB
SOL40
SALT ASICs
TELL40
Flex Cable
DCB
Hybrid Flex
PC
Si Sensor
MiniDAQAMC40
USB-to-I2C adapter
COMET
(with USB,
or GBTx DB)
Test board
(SALT8, SALT128)
Prototypes
SALT8a/b,
SALT128
Bare stave
CF sheet,
Prototype
CapArray,
Half-A sensor
VLDB
8xSALT8Prototype Hybrid
Prototype
Pigtail
Prototype

## Slide 4: Prototypes & Substitutes
Final |  | Substitutes & Prototypes |  | 
Sensor |  | CapArray | Half-A | 
SALT |  | SALT8a | SALT8b | SALT128
Hybrid |  | SALT8 Testboard | SALT128 Testboard | Hybrid_8x8
Stiffener |  |  |  | 
Wirebonds |  | 4-ASIC Ada | 8-ASIC Ada | 
Flex cable |  | Prototype_1 | Prototype_2 | Prototype_3
Pigtail |  | MegArray2ERF8 | MegAda | Prototype
Backplane |  |  |  | Prototype
MCB | ECS | VLDB | I2C Adapter | 
 | TFC |  |  | 
 |  |  | COMET with USB interface | COMET + GBTx DB
DCB |  |  |  | 
Opt. Fiber |  | Sample |  | 
TELL40 |  | MiniDAQ1 / AMC40 |  | MiniDAQ2 / PCIe40
SOL40 |  |  |  | 
Bare Stave |  | CF sheet | Prototype | 
LV Regulator |  | Prototype |  | 
Use components as close to the final design as possible for realistic tests.
Green color components are available, yellow components are to be produced.

## Slide 5: Components of Phase I Slice Test
Final |  | Substitutes & Prototypes |  | 
Sensor |  | CapArray | Half-A | 
SALT |  | SALT8a | SALT8b | SALT128
Hybrid |  | SALT8 Testboard | SALT128 Testboard | Hybrid_8x8
Stiffener |  |  |  | 
Wirebonds |  | 4-ASIC Ada | 8-ASIC Ada | 
Flex cable |  | Prototype_1 | Prototype_2 | Prototype_3
Pigtail |  | MegArray2ERF8 | MegAda | Prototype
Backplane |  |  |  | Prototype
MCB | ECS | VLDB | I2C Adapter | 
 | TFC |  |  | 
 |  |  | COMET with USB interface | COMET + GBTx DB
DCB |  |  |  | 
Opt. Fiber |  | Sample |  | 
TELL40 |  | MiniDAQ1 |  | MiniDAQ2
SOL40 |  |  |  | 
Bare Stave |  | CF sheet | Prototype | 
LV Regulator |  | Prototype |  | 
MegAda board is now available. We will start phase I slice test right after this workshop.

## Slide 6: Objectives of Phase I Slice Test
In phase I slice test we want to
  Validate signal integrity with a few differential lines.
  Investigate effects of I2C cross talk.
  Investigate effects of digital analog cross talk.
  Study general noise immunity.
Now we have all major components. Phase I test will start right after this workshop.
If components for phase II are available, some phase I tests may be done directly on the phase II setup.

## Slide 7: Components of Phase II Slice Test
Final |  | Substitutes & Prototypes |  | 
Sensor |  | CapArray | Half-A | 
SALT |  | SALT8a | SALT8b | SALT128
Hybrid |  | SALT8 Testboard | SALT128 Testboard | Hybrid_8x8
Stiffener |  |  |  | Prototype
Wirebonds |  | 4-ASIC-Ada | 8-ASIC Ada | 
Flex cable |  | Prototype_1 | Prototype_2 | Prototype_3
Pigtail |  | MegArray2ERF8 | MegAda | Prototype
Backplane |  |  |  | Prototype
MCB | ECS | VLDB | I2C Adapter | 
 | TFC |  |  | 
 |  |  | COMET with USB interface | COMET + GBTx DB
DCB |  |  |  | 
Opt. Fiber |  | Sample |  | 
TELL40 |  | MiniDAQ1 |  | MiniDAQ2
SOL40 |  |  |  | 
Bare Stave |  | CF sheet | Prototype | 
LV Regulator |  | Prototype |  | 
A prototype hybrid of 8 SALT8b ASICs to replace the SALT8 testboard.
A COMET board that has GBTx DB + a USB-I2C adapter to replace VLDB.
We may use prototype bare stave instead of a CF sheet.

## Slide 8: Goals of Phase II Slice Test
In phase II test we want to
  Reproduce tests in phase I with a more realistic setup.
  Validate the COMET board, especially since it has a fresh implementation of GBTx, & VTRx communication.
  Test HV distribution system.
  Generate a realistic voltage drop between the COMET & the FE hybrid to determine if the I2C communication works.
  Study signal interference between ASICs.
Majority of phase I & II tests need to be done before the electronics review on July 1st. There is ~ 1 month left for component production, system setup & test.

## Slide 9: Slice Test Phase 3+
We will update the slice test plan after phase II basing on how prototype components progress.
With SALT128 we want to study noise performance, power consumption, channel coupling, …
Prototype pigtail cable & back plane will be added to the system for signal quality & noise performance measurements etc.
Use more than one hybrid to measure inter-hybrid interference, and maybe also between 2 sides of stave.
…

## Slide 10: Phase I Slice Test Setup @ Syracuse
Flex Cable Assembly
GBT frame data
(TFC/ECS & event)
GBTx
SCA
AMC40
MiniDAQ
SALT8 TB
I2C signal to
config GBTx
½ A sensor
VLDB
E-link data
320 Mbps
I2C signal to
config SALT8
MegAda
LV
SALT8b
Bonding
Adapter
Available
now
CCPC
Linux PC

## Slide 11: Status of Other Major Components
Status of major components to be added in the phase II slice test and tests later are presented at this workshop
  COMET with GBTx daughter card (by Will Parker).
  Hybrid of 8 SALT8 & new flex cable (by Mauro Citterio)
  SALT128 (by Marek Idzik, Krzysztof Swientek, Tomasz Fiutowski)
  SALT128 test board (by Carlos Abellan Beteta)
  Pigtail cable (by Maria Del Pilar Peco Regales)
  Prototype bare stave (by Ray Mountain)
Other components:
  MegAda: It is available now. I will bring 1 or 2 back to Syracuse.
  MiniDAQ2: One system is purchased for UMD, available this summer.
  LV regulator: We have one prototype from Brian Hamilton.

## Slide 12: The DAQ System
The Linux PC
  PVSS control panels sends out configuration data to CCPC via an 1 Gbps Ethernet cable.
  A process running on PC reads event data in MEP from AMC40 via a 10 Gbps optical line, saves data in files for further analysis, or has real time analysis to avoid huge data files.
  Quartus loads firmware to AMC40 FPGA via a USB-to-jtag connection.
  Configures GBTx on VLDB via USB-to-I2C adapter.
CCPC on the MiniDAQ system
  Access register of FPGA on AMC40, write or read back register values of configuration.
AMC40 on the MiniDAQ system
  A special firmware is implemented to combine TFC/ECS & event data in 1 pair of optical fibers, to & from VLDB separately.
  The GBT frame to VLDB consists of GBTx config (IC), SALT8 config (EC), & TFC.
  The GBT frame from VLDB contains data from all input e-ports on VLDB & IC/EC read back.
  AMC40 generates MEP from VLDB GBT frame data and sends to PC via a 10 Gbps optical.
On VLDB
  GBTx is configured from the USB-to-I2C adapter, or from IC data.
  GBT-SCA communicates to GBTx of EC data & relay in I2C protocol with SALT8.
  E-ports operate at 320 Mbps, send TFC/CLK to SALT8, & receive event packets.

## Slide 13: PVSS Control Panels
TFC control panels by Federico Alessio
SALT8 test control panel started by Carlos Abellan
8-bit TFC for UT
Calib, Synch, Snapshot, BxVeto, NZS, HeaderOnly, FEReset, BXReset

## Slide 14: Measure System Performance
Besides of validating the readout chain, we also want to measure the system performance in analog domain and digital domain.
Static measurements of LV voltage drop & power consumption.
Noise of individual channels & common mode for high frequency effects. Some effects may also show up in the coupling of adjacent channels.
We can measure bit error rate (BER) of the digital signal to check the quality of overall communication.
We can also measure eye diagrams in individual components.

## Slide 15: Requirements of BER Measurement Method
  The bit error rate (BER) measurement program runs on the Linux PC. It has following requirements:
  The program analyzes the MEP data at real time to avoid saving huge files, as the data rate per ASIC is ~ 0.12 GByte/s. We need to run in hours to measure the very small BER value.
  The analysis algorithm has to be simple & fast, since events come in at 40 MHz rate. For a 3.2 GHz CPU, there is only 80 cycles per event.
  It needs an accurate determination on whether or not the data received at the end of readout chain is exactly what was sent out from the head.

## Slide 16: Bit Error Rate Measurement
In a first attempt we configure SALT8b to send out Synch package for every clock cycle, and check only Bxid[3:0].
The BER is expected to be very small. So from previous events we determine what Bxid[3:0] should be in the current event.
Bxid[3:0] signal may be affected by Bxid[11:8], Patt[11], Patt[8], & Patt[7:4].
Bxid[11:8] can have all different values, independent of Bxid[3:0] value. We can set Patt[11], Patt[8], & Patt[7:4] to different values in different runs.
Thus we can measure the true BER, check bits at a rate of 5.761011 bits per hour.
In a slice system without flex cable, with timing optimized, we measured the BER of the system to be 0.
Eport 0 (8-bit) |  | Eport 1 (8-bit) |  | Eport 2 (8-bit) | 
12-bit BXID |  |  | Synch pattern |  | 
Bxid[11:8] | Bxid[7:4] | Bxid[3:0] | Patt[11:8] | Patt[7:4] | Patt[3:0]

## Slide 17: Eye Diagram Setup
Tektronix DSA 70404C
Tektronix P7504 LVDS probe
A ERM8 connector with a modified micro-coax soldering tip
SALT8b Testboard modified for eye diagram test

## Slide 18: Eye Diagram @ SALT8b TB (I)
3.1 ns for
320 Mbps
Reflection due to impedance mismatch
Triggered by
master clock.
0 & 1 are
well separated.
Fast 01 & 10 transition.
Small jitter.
Relatively open eye diagram

## Slide 19: Eye Diagram At The End of Flex Cable
Plots taken by Nathan Jurik
Rev2 flex cable
Rev1 flex cable
Rev2 seems worse than rev1, maybe due to the impedance issue in the new Flex cable.

## Slide 20: Summary
We have staged slice test plans to validate the read out chain and optimize individual components.
The system setup depends strongly on the available components.
We plan to study the noise performance, bit error rate, eye diagrams to provide quantitative & qualitative measurements of the readout system.
Phase I test that was aiming for this workshop is behind plan. We hope phase I & phase II tests can be ready for the electronics review on July 1st at Syracuse.