## Slide 1: ECal Optimization for High Energy Photons
N. Nikiforou

## Slide 2: Possible Models
 | # Layers | Absorber Thickness [mm] | Si [mm] | Other (gaps, etc) [mm] | Absorber Thickness [X0] | Si+Other Thickness [mm] | Si+Other Thickness [X0] | Total Thickness [mm] | Total Thickness [X0] | Calorimeter Thickness [mm] | Calorimeter Depth [X0]
CLIC_o2_v04 (current) | 17 | 2.4 | 0.5 | 1.5 | 0.65 | 2 | 0.06 | 74.8 | 12.01 | 129.2 | 22.85
 | 8 | 4.8 | 0.5 | 1.5 | 1.30 | 2 | 0.06 | 54.4 | 10.84 |  | 
CLICdet_20_10 (original CLIC_ILD) | 20 | 2 | 0.5 | 1.5 | 0.54 | 2 | 0.06 | 80 | 11.96 | 140 | 23.35
 | 10 | 4 | 0.5 | 1.5 | 1.08 | 2 | 0.06 | 60 | 11.39 |  | 
CLICdet_30_10 (possible high granularity option) | 30 | 1.5 | 0.5 | 1.5 | 0.41 | 2 | 0.06 | 105 | 13.89 | 155 | 22.58
 | 10 | 3 | 0.5 | 1.5 | 0.81 | 2 | 0.06 | 50 | 8.68 |  | 
CLICdet_40 (possible high granularity option) | 40 | 1.9 | 0.5 | 1.5 | 0.51 | 2 | 0.06 | 156 | 22.85 | 156 | 22.85
 | 0 | 0 | 0 | 0 | 0.00 | 0 | 0.00 | 0 | 0.00 |  | 
Calculations from geometry xml file using excel
Note: we can “easily” accommodate an ECal thickness up to 159 mm (thickness of envelope) in our models without increasing detector size

## Slide 3: Full Simulation Study
Modified CLIC_o2_v04 Geometry in DD4hep/lcgeo
Simulated single photons with DDSim (100k events)
  Plus 10 GeV γ, 10 GeV μ and 50 GeV Κ0L for Calibration (x 10k events)
Each model calibrated fully
Reconstructing with DDMarlinPandora
Limit study in barrel () since I don’t trust ECalEndcap+ECalPlug reconstruction fully yet
Look at pfoEnergyPhotons but also ECalTotalCaloHitEnergy to make sure there are no issues with photon reconstruction (would need to recover photons otherwise)
Very preliminary! (only had Friday + weekend to do this)
  Not all 500 GeV photon events could be simulated and reconstructed in time (so not shown, only up to 200 GeV)

## Slide 4: 100 GeV Photons
Model/ Energy | Total γ PFO Energy |  | Total ECal Energy (no γ reco) | 
 | Mean [GeV] | Sigma [GeV] | Mean [GeV] | Sigma [GeV]
CLIC_o2_v04_100GeV | 101.33 | 2.25 | 99.55 | 2.33
CLICdet20_10_100GeV | 101.32 | 2.04 | 99.72 | 2.05
CLICdet30_10_100GeV | 101.67 | 1.74 | 99.49 | 1.82
CLICdet40_100GeV | 101.07 | 1.65 | 99.17 | 2.04
Notice that this has significant underflows! ~6-7% -> Implicitly “bad” events where photons are badly reconstructed are ignored
Underflows <0.1%

## Slide 5: PFO Photon Energy σ(Ε)/E vs E
Chart: Photon Energy [GeV]
| 25 | 50 | 100 | 200
CLIC_o2_v04 | 3.9717 | 2.9315 | 2.2261 | 1.7538
CLICdet20_10 | 3.6499 | 2.6917 | 2.0262 | 1.616
CLICdet_40 | 3.1466 | 2.239 | 1.6338 | 1.226
CLICdet_30_10 | 3.0537 | 2.2498 | 1.7193 | 1.4123

## Slide 6: Total ECal Energy σ(Ε)/E vs E
Chart: Photon Energy [GeV]
| 25 | 50 | 100 | 200
CLIC_o2_v04 | 4.0418 | 3.0302 | 2.3416 | 1.8616
CLICdet20_10 | 3.6709 | 2.719 | 2.0576 | 1.6295
CLICdet_40 | 3.282 | 2.5067 | 2.0579 | 1.8531
CLICdet_30_10 | 3.0864 | 2.324 | 1.8301 | 1.5519

## Slide 7: Conclusions?
A closer look is needed
If model has to be frozen, I would propose we go with 30 layers (20+10)
One can notice that the performance changes when more energetic showers penetrate more the back layers with coarser sampling