## Slide 1
Seongjoo Lee
(Dongguk & Yonsei Univ.)
ALICE ITS Upgrade : Pixel chip design
TowerJazz 0.18um CMOS Image Sensor Process
2016. APR. 10

## Slide 2
1. pALPIDE-2(2014)
2. pALPIDE-3(2015)
3. ALPIDE(2015 – 2016)
4. Conclusion & Future plan
Outline

## Slide 3
1. pALPIDE-2(2014)
1.1 4-b IDAC for the MLVDS and DTU block : Design
- Implementation of the MLVDS block(design by A. Lattuca, INFN Torino) on pALPIDE - 2
- Test chip of the PLL(design by G. Mazza, INFN Torino) and LVDS Driver(design by A. Lattuca, INFN Torino) block
=> Requirement of the current mirror : 4-b IDAC(able to control current source of each block)
MLVDS
DTU – LVDS Driver
DTU – PLL

## Slide 4
1. pALPIDE-2(2014)
1.2 MLVDS Driver : performance check
- Verification with 4-b IDAC.
=> Performance was satisfied with our goal.

## Slide 5
2. pALPIDE-3(2015)
2.1 4-b IDAC for the MLVDS and DTU block : Resistor implementation
- Checking sheet resistance, variation and mismatch of a resistor(Iout is depending on a resistor value) : meet target
- Optimization of power connection(Analog power or Digital power) for reduction of noise
Resistor(Current source)

## Slide 6
2. pALPIDE-3(2015)
2.2 Front-end : Power Supply Rejection Ratio(PSRR) simulation
Nominal setting | Qin | Ileak | Vreset | Ibias | Ithr | Vcasp | Vcasn | Idb
 | 0e- | 400fA | 1.4V | 20nA | 0.5nA | 0.6V | 0.4V | 10nA
VDD, VSS or PW
Variables : Power node, Vp, Freq. and shape
PSRR simulation - Filtering 100kHz to 1MHz noise on power( Vp : up to 50mV)
Checking mismatch & noise simulation

## Slide 7
3. ALPIDE(2015 – 2016)
3.1 Power-on Reset : Reduction of Single Event Upset(SEU) sensitivity
Critical nodes
< First gain stage >
VDD
Vramp
RESET
RESET
(PoR out)
Vref+
+
-
RESET
Vref+
DVSS
Iramp
C
+
-
Vref+
Vref-
DVDD
Vref+
Vref-
Vref- > Vref+
Vramp
RESET
MD
718nA
1.5µA
1nA
1u/10u
C_RST
SEU on a sensitive node
Reset : enabled
Original design by Yavuz Degerli (CEA/IRFU,Centre d'etude de Saclay Gif-sur-Yvette)
Filtering capacitor
(CAP1 & CAP2)
=> Addition of filtering capacitors & duplication the cell to reduce SEU sensitivity

## Slide 8
pALPIDE3 | 2 MUXs | 2 STDs | DPE
Static power (DC) | 3.1 nW | 17.7 nW | 13.1 mW
Average power (Static + Dynamic) | 2.4 mW | 9.8 mW | 13.2 mW
2 MUXs
2 STDs
DPE
- To optimize power consumption of 2 STDs,
=> Single-ended To Differential buffer(STD) : Stages and size ↓
=> MAIN Driver & P-E Driver : Input transistor size(Load cap) ↓
(Reduced driving capability of 2 STDs => Load capacitor↓)
- Common mode voltage(VCM)
1.1V => 0.9V (EDR recommendation)
pALPIDE3
ALPIDE
Original design by Alessandra Lattuca (Universita e INFN Torino)
3. ALPIDE(2015 – 2016)
3.2 DTU – LVDS Driver : Optimization of the power consumption
Performance : Better than pALPIDE3 results & Power : 26.9% decrease (@ Nominal corner)

## Slide 9
4.1 Conclusion
pALPIDE – 2
- 4-b IDAC : satisfying target
- MLVDS verification with 4-b IDAC : satisfying target
pALPIDE – 3 - Resistor implementation on 4-b IDAC : satisfying target
- PSRR simulation for the Front-End circuit : Filtering 100kHz to 1MHz & Vp = up to 50mV on Power
ALPIDE
- Power-on Reset : Reduction of Single Event Upset(SEU) sensitivity : addition of filtering capacitor &
duplication the cell
- Power optimization of the LVDS Driver : 27% decrease & better performance than pALPIDE - 3
4. Conclusion & Future plan

## Slide 10
4.2 Future plan
4. Conclusion & Future plan
- 2016
=> Course work
=> 4월 – 9월(?) : New project – CMOS Image Sensor(CIS)
=> 9월(?) – 12월 : CIS 측정 준비
- 2017
=> CIS 측정 및 측정 결과로 졸업 논문 작성, 졸업 시험, 영어 시험

## Slide 11
Backup slides

## Slide 12
To separate Full-analog(8-bit Current DAC & Voltage DAC), Current Mirror is changed.
Backup slides – 4-b IDAC(pALPIDE-3)

## Slide 13
pALPIDEfs_V2 Current Mirror for the MLVDS block
pALPIDEfs_V3 Current Mirror for the MLVDS block
Backup slides – 4-b IDAC(pALPIDE-3)

## Slide 14
Chart: Max(fast corner) value/Min(slow corner) value
| mr23t | rm1 | rm2 | rm3 | rm4 | rm5 | rmL | rnlpoly2t | rnlpoly3t | rnmpoly2t | rnmpoly3t | rnplus2t | rnplus3t | rnplus_sal2t | rnplus_sal3t | rnwell_AA2t | rnwell_AA3t | rnwell_STI2t | rnwell_STI3t | rphpoly2t | rphpoly3t | rplpoly2t | rplpoly3t | rpmpoly2t | rpmpoly3t | rpplus2t | rpplus3t | rpplus_sal2t | rpplus_sal3t
max/min | 1.3971 | 4.5625 | 4.5625 | 4.5625 | 4.5625 | 4.5625 | 2.5491 | 31.4994 | 31.502 | 1.61 | 1.6144 | 2.1572 | 2.1572 | 21.5171 | 21.5171 | 2.2974 | 2.2974 | 3.2323 | 3.2321 | 1.3018 | 1.3018 | 33.6527 | 33.6527 | 1.4128 | 1.4089 | 2.3826 | 2.3826 | 23.0181 | 23.0181
Chart: Max(fast) value/Min(slow) value=>rnmpoly2t
| 0.18 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 5 | 100
Max/Min | 2.249 | 1.743 | 1.654 | 1.628 | 1.615 | 1.607 | 1.603 | 1.596 | 1.58
Width[um]
Width = 2um
Length = 710um
NAME | Ω/□
mr23t | 2kΩ/□
rm1 | 80mΩ/□
rm2 | 80mΩ/□
rm3 | 80mΩ/□
rm4 | 80mΩ/□
rm5 | 80mΩ/□
rmL | 40mΩ/□
rnlpoly2t | 6Ω/□
rnlpoly3t | 6Ω/□
rnmpoly2t | 400Ω/□
rnmpoly3t | 400Ω/□
rnplus2t | 70Ω/□
rnplus3t | 70Ω/□
rnplus_sal2t | 7Ω/□
rnplus_sal3t | 7Ω/□
rnwell_AA2t | 450Ω/□
rnwell_AA3t | 450Ω/□
rnwell_STI2t | 1kΩ/□
rnwell_STI3t | 1kΩ/□
rphpoly2t | 1kΩ/□
rphpoly3t | 1kΩ/□
rplpoly2t | 5Ω/□
rplpoly3t | 5Ω/□
rpmpoly2t | 310Ω/□
rpmpoly3t | 310Ω/□
rpplus2t | 120Ω/□
rpplus3t | 120Ω/□
rpplus_sal2t | 5Ω/□
rpplus_sal3t | 5Ω/□
Backup slides – 4-b IDAC(pALPIDE-3)

## Slide 15
1
2
3
(MOS saturation current)
=> The vgs is dependent on variation of Power Supply.
Backup slides – 4-b IDAC(pALPIDE-3)

## Slide 16
Chart: IREF_P(Typical corner)
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5
1 | 0 | 0.22 | 0.44 | 0.66 | 0.88 | 1.09
2 | 0 | 0.03 | 0.07 | 0.1 | 0.14 | 0.17
3 | 0 | 0.34 | 0.67 | 1 | 1.33 | 1.66
△I[uA]
△V[V]
Chart: IREF_N(Typical corner)
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5
1 | 0 | 0.09 | 0.18 | 0.27 | 0.36 | 0.45
2 | 0 | 0.08 | 0.16 | 0.23 | 0.31 | 0.39
3 | 0 | 0.14 | 0.28 | 0.41 | 0.55 | 0.69
△I[uA]
△V[V]
Backup slides – 4-b IDAC(pALPIDE-3)

## Slide 17
Chart: IREF_P(DRIVER)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Slow | 0 | 0.3068 | 0.6123 | 0.9165 | 1.2194 | 1.521 | 1.82 | 2.132 | 2.431 | 2.73 | 3.029 | 3.328 | 3.627 | 3.926 | 4.225 | 4.524
Typical | 0 | 0.4095 | 0.8164 | 1.2233 | 1.625 | 2.028 | 2.444 | 2.847 | 3.25 | 3.653 | 4.056 | 4.459 | 4.862 | 5.265 | 5.668 | 6.058
Fast | 0 | 0.5811 | 1.1596 | 1.742 | 2.314 | 2.899 | 3.471 | 4.043 | 4.628 | 5.2 | 5.772 | 6.357 | 6.929 | 7.501 | 8.086 | 8.658
I[mA]
4-bit IDAC_CODE
 | Driver pmos |  | Driver nmos |  | Receiver pmos |  | Receiver nmos | 
 | σId | σId/Id | σId | σId/Id | σId | σId/Id | σId | σId/Id
FF | 0.26μA | 0.61% | 0.76μA | 0.88% | 0.27μA | 0.63% | 0.52μA | 1.20%
SS | 0.15μA | 0.65% | 0.42μA | 0.92% | 0.15μA | 0.67% | 0.29μA | 1.24%
TT | 0.19μA | 0.64% | 0.57μA | 0.93% | 0.2μA | 0.66% | 0.39μA | 1.28%
Chart: IREF_N(DRIVER)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Slow | 0 | 0.6253 | 1.2389 | 1.846 | 2.457 | 3.055 | 3.653 | 4.238 | 4.836 | 5.421 | 6.006 | 6.578 | 7.163 | 7.735 | 8.307 | 8.866
Typical | 0 | 0.832 | 1.651 | 2.457 | 3.276 | 4.069 | 4.875 | 5.668 | 6.461 | 7.254 | 8.047 | 8.827 | 9.607 | 10.387 | 11.167 | 11.934
Fast | 0 | 1.183 | 2.34 | 3.497 | 4.641 | 5.772 | 6.916 | 8.047 | 9.165 | 10.296 | 11.414 | 12.532 | 13.65 | 14.82 | 15.86 | 17.03
I[mA]
Backup slides – 4-b IDAC(pALPIDE-3)

## Slide 18
< Before >
< After >
Resistor
Width = +24um
108um
65um
89um
R = ρ(L/W)
ρ=400ohm/□
L=2um
W=709.695um
(max. height=120um)
Number of segments = 9(series)
< Resistor >
Backup slides – 4-b IDAC(pALPIDE-3)

## Slide 19
②
VOH - VOL = IS·2·RT
①
②
①
②
①
VDD
VSS
Voltage swing : VSS to VDD
Voltage swing : VOL to VOH
INPUT
OUTPUT
①
①
②
①
②
①
Backup slides – LVDS Driver(ALPIDE)

## Slide 20
pALPIDE3 | 2 MUXs | 2 STDs | DPE
Static power (DC) | 3.1 nW | 17.7 nW | 13.1 mW
Average power (Static + Dynamic) | 2.4 mW | 9.8 mW | 13.2 mW
2 MUXs
2 STDs
DPE
- To optimize power consumption of 2 STDs,
=> Single-ended To Differential buffer(STD) : Stages and size ↓
=> MAIN Driver & P-E Driver : Input transistor size(Load cap) ↓
(Reduced driving capability of 2 STDs => Load capacitor↓)
- Common mode voltage(VCM)
1.1V => 0.9V (EDR recommendation)
pALPIDE3
ALPIDE
Original design by Alessandra Lattuca (Universita e INFN Torino)
Backup slides – LVDS Driver(ALPIDE)

## Slide 21
2 STDs
MAIN & P-E
Input TR
RES
2 STDs
MAIN & P-E
Input TR
RES
pALPIDE3
ALPIDE
Resistor(VCM = 1.1V)
Resistor(VCM = 0.9V)
Reference voltage
Reference voltage
Backup slides – LVDS Driver(ALPIDE)

## Slide 22
PRBS = 1.2Gbps Driver CODE = 9 P-E Driver CODE = 9 | Slow |  | Nominal |  | Fast | 
 | pALPIDE3 | ALPIDE | pALPIDE3 | ALPIDE | pALPIDE3 | ALPIDE
Horizontal opening [ps] | 741.8 | 769.6 | 759.5 | 778.4 | 736.1 | 772.8
Vertical opening [mV] | 373.2 | 399.6 | 470.6 | 504.7 | 591.9 | 632.9
Jitter(p-p) [ps] | 134.8 | 107.6 | 107.7 | 73.5 | 97.1 | 57.4
Average power [mW] | 18.8 | 13.1 | 26.4 | 19.3 | 37.0 | 28.7
 | Slow | Nominal | Fast
Corner | SS | TT | FF
VDD | 1.62V | 1.8V | 1.98V
Temp. | 85℃ | 27℃ | -40℃
p-p jitter
Simulation : Better than pALPIDE3 results
Power : 26.9% decrease (@ Nominal corner)
VCM : 1.1V => 0.9V
Backup slides – LVDS Driver(ALPIDE)

## Slide 23
VDD
Vramp
RESET
RESET
(PoR out)
Vref+
+
-
RESET
Vref+
DVSS
Iramp
C
+
-
Vref+
Vref-
DVDD
Vref+
Vref-
Vref- > Vref+
Vramp
RESET
MD
718nA
1.5µA
1nA
1u/10u
C_RST
Principle
- The first gain stage discharges the capacitor C through the transistor MD at the beginning of every ramp.
- Vref+ and Vref- cross each other after some time, MD turns off and ramp of Vramp is initiated
- When Vramp becomes larger than Vref+, reset is disabled.
Original design by Yavuz Degerli (CEA/IRFU,Centre d'etude de Saclay Gif-sur-Yvette)
Backup slides – Power-on Reset(ALPIDE)

## Slide 24
Critical nodes
< First gain stage >
VDD
Vramp
RESET
RESET
(PoR out)
Vref+
+
-
RESET
Vref+
DVSS
Iramp
C
+
-
Vref+
Vref-
DVDD
Vref+
Vref-
Vref- > Vref+
Vramp
RESET
MD
718nA
1.5µA
1nA
1u/10u
C_RST
SEU on a sensitive node
Reset : enabled
Original design by Yavuz Degerli (CEA/IRFU,Centre d'etude de Saclay Gif-sur-Yvette)
Filtering capacitor
(CAP1 & CAP2)
Backup slides – Power-on Reset(ALPIDE)

## Slide 25
CAP2
CAP1
80um
120um
80um
120um
pALPIDE3 : PoR
ALPIDE : PoR
Reduction of SEU sensitivity (addition of capacitance on critical nodes)
Other nodes : No problem
Duplication of cell in ALPIDE with logic “OR” to further reduce probability of upset
Backup slides – Power-on Reset(ALPIDE)