## Slide 1: KISTI-GSDC site report
KoALICE National Workshop
@ ARPINA, Busan, South Korea
8 April – 10 April 2016
Sang-Un Ahn
on the behalf of KISTI-GSDC
Notes: Good Day Everyone.
I am Sang-Un Ahn,
and on behalf of the GSDC Tier1 Team,
I am going to talk about the status of KISTI Tier1
precisely the progress and the performance of our site
as a candidate of WLCG Tier1.

## Slide 2: CONTENTS
KISTI GSDC Overview
Tier-1 operations
Network
KoALICE Support
Conclusion
Notes: This is the outline of today’s talk.
Short introduction to the KISTI and GSDC,
Summary report on the operations of Tier1 and KIAF,
Current network configuration and future plan including OPN joining,
Milestones, and conclusion.

## Slide 3: KISTI gsdc Overview

## Slide 4: KISTI Location
South Korea
Busan
Daejeon
2h by car
Gwangju
Jeju Island
Daegu
KISTI
30 Government Research Institutes
11 Public Research Institutes
29 Non-profit Organizations
7 Universities
Daedeok R&D Innopolis
Rare Isotope Accelerator
(To be constructed)
Seoul
Incheon
Airport

## Slide 5: KISTI GSDC
Government funding research institute for IT founded in 1962
  600 people working for National Information Service(distribution & analysis), Supercomputing and Networking
  Operating Supercomputing and NREN Infrastructure
  Supercomputer: 307.4 TFlops at peak(14th ranked at Top500 in 2009; 201st now)
  NREN Infrastructure: KREONet2
    Domestic: Seoul ←(100G)→ Daejeon
    International: HK ←(100G)→ Chicago/Seattle(Member of GLORIAD)
KISTI (Korea Institute of Science and Technology Information)
History of GSDC
GSDC (Global Science experiment Data hub Center)
Government funding project to promote research experiment providing computing power and storage
  HEP: ALICE, CMS, Belle, RENO
  Others: LIGO, Bioinformatics
Running Data-Intensive Computing Facility
  13 staffs: sysadmin, experiment support, external-relation, administration
  Total 7,900 cores, 6,000 TB disk and 1,500 TB tape storage
GSDC Facility
2007
2009
2013
2012
2011
2010
2014
Formation of GSDC
ALICE T2 Test-bed
ALICE T1 Test-bed
ALICE T1 candidate
2015
ALICE T2 operation start
KISTI Analysis Facility
Full T1 for ALICE
Start CMS T3
10Gbps LHCOPN Established

## Slide 6: GSDC System Overview
1.5 PB
Torque/MAUI
4,500 slots
ALICE T1, Belle, RENO
HTCondor
2,500 slots
CMS T3, LIGO, KIAF
Public
Private
2.5 PB
3.5 PB
IBM TSM/GPFS
HITACHI USP/VSP
EMC Clariion/VNX
HITACHI HNAS
EMC ICILON
4 Spine switches
74 Leaf switches
500+ Servers in 22 racks
14 Storage racks
4 tape frames
40 RACKS!!!!

## Slide 7: System Management
Services are defined at Puppet (manifests, profiles)
  Stash is used for Puppet code management
Nodes are created/provisioned via Foreman with Puppet classes
  Any VMs are managed by the Red Hat solution
Centralized authN/authZ are provided via IPA (SSO to be implemented)
JIRA helps to track issues and to manage project
Confluence is a useful tool for documentation and sharing
Project
Issue tracking
Puppet code
management
(via Git)
Documentation & Space
Node definition
Provisioning
Manifests
Profiles
v3.7.4

## Slide 8: Tier-1 Operations
Notes: Operations.

## Slide 9
Physical Machine
Batch System: Torque/MAUI
Grid Middleware: EMI
PS, Proxy, SE, BDII
Computing Resources (3488 core)
Storage Resources (3.1PB)
EMC isilon
SAN
/gpfs[01..08]
CEs
SE
VOBOX
squid
xrootd
emi
siteBDII
perfSONAR
Xrootd RDR
Xrootd Servers
GPFS Servers
TSM Server
alien
apmon
apmon
cvmfs
xrootd
apmon
xrootd
apmon
xrootd
apmon
frm
emi
bdii
gpfs
tsm
tsm
Xrootd Servers
10G
64G
SAN
SAN
/data
/data
emi
qlexec
cvmfs
torque
WLCG Mesh
ALICE
emi
srm
gridftp
emi
cream
torque
Worker Nodes
Xrootd RDR
isolated
Virtual Machine
RAW Data Flow
Job Flow
ALICE::KISTI_GSDC::SE2
ALICE::KISTI_GSDC::TAPE
200TB
400TB
1.5PB
1.5PB

## Slide 10: Pledges
 | 2014 | 2015 | 2016
CPU(HS06) (Installed) | 25,000 (28,800) | 28,000 (28,800) | 31,000 (38,200)
Disk(TB) (Installed) | 1,000 (1,000) | 1,000 (1,000) | 1,500 (1,500)
Tape(TB) (Installed) | 1,500 (1,000) | 1,500 (1,500) | 1,500 (1,500)
2016 pledges are fulfilled
ALICE Only

## Slide 11: Jobs
KISTI, 3.19% = 2.6M jobs for the last 6 months
Sep 2015
Mar 2016
Maximum 3,402 concurrent jobs = 37 kH06
(84 nodes x 32 (logical) cores + 20 nodes x 40 (logical) cores)
~ 1300
Maximum 1,344 concurrent jobs (84 nodes x 16 cores)
> 5GB memory available per job
For HI Reco Run ~ Feb 2016
Stable and smooth running
Participating in HI Reco Run at the end of 2015
261M jobs done for the last 6 months
~ 2500
ALICE Only
~ 3300
Notes: Concerning jobs, we have eighteen hundred job slots for ALICE.
Current performance for high energy physics job processing is about sixteen k-HepSpec.
Including computing power of KISTI Tier2, our share for ALICE jobs is three point six percent.
The pledges for this year is twenty five k-HepSpec with two thousand cores.
And this will be fulfilled by the end of November.
There has been several issues on operations but overall site performance has been gradually getting better as you can see in the bottom plot.
I am not going into details on this plot.

## Slide 12: Storage
3 Yrs Use History
← May 2013
Run2 Data Taking
400TB Disk buffer for helping fast access to data archived
1,465 TB Used (Tape)
855.6 TB Used (Disk)
ALICE Only
1.465PB ALICE RAW Data Transferred
99% Storage Availability for the last 6 months
Tape
Disk
99% Storage Availability of R/W for last 6 months
Jun 2013
May 2015
Notes: Storage.
One petabyte of disk has been allocated for ALICE which fulfilled the pledges for two thousand thirteen,
And one petabyte of tape has been installed
together with a disk buffer of four hundred seventy five terabytes.
By the end of this year, disk pool for tape will be expanded up to six hundred
to have higher availability as well as better performance on throughput.
One of the milestones for Tier1, to be explained in the later, is to achieve more than 90% (ninety percent) of availability of storage for at least two months.
On the left plot, for more than six months, KISTI storage has shown higher availability than the requirement.

## Slide 13: Site Availability/Reliability
99.8% Reliable for the last 6 month (from Sep-2015 to Feb-2016 )
  Monthly Target for Reliability of ALICE test: 97%
  Less than 10 days of yearly downtime
On track for a stable and reliable site
  Participating in weekly WLCG operations meetings(1 times (Mon) per week): reporting operation-related issues
  24/7 monitoring & maintenance contract
  2 persons responsible for on-call
 | Sep | Oct | Nov | Dec | Jan | Feb
Reliability | 100 | 100 | 100 | 100 | 100 | 99
Availability | 100 | 100 | 100 | 95 | 100 | 99
< Monthly Availability/Reliability (%) >
ALICE Only
Notes: In this slide I summarized our site availability based on WLCG monthly report.
Monthly target for reliability is ninety seven percent.
The red line on the bottom plot represents the monthly target,
and you can see the history of KISTI Tier1 site availability and reliability,
of OPS and ALICE VO on every months since March two thousand twelve.
As you can see, it has shown gradual increase of overall availability.
In particular, for the last year, mostly we achieved the monthly target in spite of a few unscheduled downtime.

## Slide 14: Network
Notes: Operations.

## Slide 15: KISTI Domain Network for T1
2 Core Switches
Physical Firewall
Backbone Router

## Slide 16: KISTI-CERN Network (LHCOPN)
GSDC/KISTI
@Daejeon
KRLight
@Chicago
NetherLight
@Amsterdam
CERN
@Geneva
SKB(EAC+PC-1)
SKB(EAC+UNITY)
SURFnet
(CANARIE)
SURFnet (SURFnet)
SKB(Level3)
SKB(Level3)
Seattle
LA
New York
SK Broadband (~’16.8)
SURFnet
SURFnet (SURFnet)
KREONET
10Gbps Upgrade done by 31st April 2015

## Slide 17: Performance
CERN IT Gateway
Multi-stream: 500
Max peak: 1GB/s
10G enabled
KISTI-GSDC
CERN→KISTI (5 min)
CERN→KISTI
Average: 65 MB/s
> 9Gbps peak (~ 1GB/s) observed
  CERN IT provided a gateway, 500 parallel transfers
    xrd3cp crashed with Xrootd v3.3.4 (fixed @ v4 or later)
  Max 1GB/s peak @ alimonitor.cern.ch
  Confirmed full capacity
MRTG @ MX960
alimonitor.cern.ch

## Slide 18: KISTI-ASIA
Connected to JP, US, CN, TW(ASGC) and HK
  via Kreonet2
  JP connected through APAN
Not connected to TEIN @ HK
Asian Tier sites are well connected
Tsukuba
Wuhan

## Slide 19: Example: Current Status
KISTI(KR) ↔ COMSATS(PK)
30 hops
Tracepath
over 400ms latency
KISTI
Daejeon
Tokyo
Singapore
COMSATS
Islamabad
KREONET
TRANSPAC
PACIFICWAVE
APAN-JP
TEIN
LA
Seattle
HK
KISTI-CERN 250ms latency

## Slide 20: Asia Tier Center Forum
Motivation
Improving network environment among Asian Tier Centers
At first, for only ALICE sites: KISTI T1 <-> ALICE T2 in Asia
Note that T2s in Asia quite well connected via TEIN and APAN-JP
KISTI has its own backbone called KREONET, partner of GLORIAD
Natural to think of taking the shortest route from T2 to T1 or vice versa
Geographically close but technically far
Current situation: occasionally CERN or European site or US sites are effectively closer than KISTI T1 for ALICE T2 in Asia
Inefficient routing paths
  Best effort among possible paths instantaneously
  Long distance -> more hops

## Slide 21: Asia Tier Center Forum
Goal
The aim of this forum is to discuss on the possible solutions for the improvement of connectivity among Asian Tier sites and their status of domestic network environment and
To monitor periodically the state-of-art of the established network environment through this forum and to organize a body with a broader agenda embracing not only the network but also common issues that could be arisen among Asian Tier sites.
The target of this forum is mostly Asian Tier sites, however, the forum is open to every interested parties, in particular, distributed computing co-ordinations of LHC experiments and network experts on OPN/ONE.

## Slide 22: Asia Tier Center Forum
1st Asia Tier Center Forum @ KISTI, Daejeon, South Korea
22 - 24 September 2015
10 Site reports with domestic/campus network status
T1: ASGC (TW), KISTI (KR)
T2: Tsukuba (new T2 for ALICE, JP), Wuhan (CN), Bandung (ID), TIFR (CMS T2, IN), Kolkata (IN), COMSATS (PK), SUT (TH), Hiroshima (JP)
3 LHCONE related talks
LHCONE Status (by Edoardo Martelli, CERN)
US implementation (by William Johnston, ESnet)
Guidelines for site configuration (by Michael O’Connor, ESnet)
Joint session of TEIN & KREONET
Asia implementation (by Edoardo Martelli, CERN)
TEIN (by Patch Lee, TEIN*CC) and KREONET (by Buseung Cho, KISTI) preparation for LHCONE
Current activity on TEIN-GLORIAD connection
http://www.atcforum.org

## Slide 23: Asia Tier Center Forum
Agreed to implement LHCONE VRF in their networks,
to interconnect the VRFs in HK and to give transit each other their peering links to GÉANT(TEIN), STARLight(KISTI, ASGC), and Seattle(KISTI)
TEIN
KREONET (KISTI)
ASGC

## Slide 24: Result
KISTI(KR) ↔ PAKGRID (PK)
KISTI
Daejeon
Tokyo
Singapore
PAKGRID
(PK)
KREONET
TRANSPAC
PACIFICWAVE
APAN-JP
TEIN
LA
Seattle
HK
Before path (2015)
After path (2016)
Connection test (1Gbps)
Latency : -155.546 ms
Hop : -10
Tracepath test condition
Source: KISTI-GSDC (134.75.125.152)
Destination: Pakgrid (111.68.99.138)
After
287.264ms
Before
442.810ms
Tier centers in ASIA use optimal routing path through GSDC Tier 1 center.
Tier centers in ASIA use abnormal routing path. (example test: Parkgird)

## Slide 25: TEIN-GLORIAD-KR
10Gbps
SG
JP
Indonesia
TH
IN
Amsterdam
10Gbps
CERN
HK
Pakistan
Chicago
1 ~ 10Gbps
KISTI-CERN LHCOPN
GLORIAD-KR
TEIN
KISTI
GSDC
Seattle
10Gbps
100Gbps
10Gbps
10Gbps

## Slide 26: 2nd Asia Tier Center Forum
October 2016 @ SUT, Thailand
Thanks to Prof. Chinorat Kobdaj

## Slide 27: KoALICE Support

## Slide 28: MoU Summary
Purpose
  Collaborating to promote heavy-ion research and user community in Korea by using computing infrastructure and technology
 | 2014 | 2015 | 2016
CPU core (Physical) | 150 | 300 | 450
Storage (TB) | 200 | 200 | 200
Contact
Role | Name | Institute
KoALICE Representative | In-Kwon Yoo | PNU
KISTI Representative | Haeng Jin Jang | KISTI
ALICE Software Support | Jihye Song | PNU
ALICE Technical Support | Sang-Un Ahn | KISTI
Resource
  ALICE Tier-1 + KIAF
  Adjustable depending on funding and request from user community
Etc.
  Co-hosting KoALICE-KISTI Workshop
  Collaboration on establishing computing infrastructure and computing project in ALICE

## Slide 29: KIAF System
afmaster01.sdfarm.kr
(kiaf.sdfarm.kr)
kwn1001.sdfarm.kr
kwn1008.sdfarm.kr
8 nodes
SSH(Private Key)
PROOF on Demand enabled based on HTCondor
  Total 192 workers with 173TB storage
User authentication @ https://kiaf.sdfarm.kr:8443/auth
  Proxy valid for 1 hour (requires user certificate)
Submission Node
Central Manager
PROOF Master
XRootD Header
Execution Node
PROOF Salve
XRootD Server
ROOT
pod-submit …
condor_submit …
ALICE software deployed via CernVM-FS
Dataset management via XRootD
22TB
22TB
22TB

## Slide 30: How to use KIAF: brief summary
$ ssh -p4280 -i $HOME/.globus/userkey.pem kiaf.sdfarm.kr
SSH connection with private key after obtaining a proxy(1h) @ https://kiaf.sdfarm.kr/auth
Environment setup
$ source /pool/podenv
PoD start
$ pod-server start
$ pod-submit -r condor -n 10
$ pod-info -n
10
$ root -l
root[0] TProof *p = TProof::Open(“pod://”)
…
If you are familiar with HTCondor batch system,
$ condor_status
$ condor_q
$ condor_submit myjob.jds
…

## Slide 31: KIAF Activities
PNU | Inha | Konkuk | Total
4 | 4 | 2 | 10
User Accounts
2014 | 2015 | 2016 | Total
101 | 3,703 | 1,239 | 5,043
Job Accounting
(available since Sep 2014)
Data | Period | Run | Type | Pass | Datasets
Real | LHC13b | 195344-195483 | ESD | 3 | 13
Real | LHC13c | 195529-195677 | ESD | 2 | 15
Real | LHC10h | 137161-139510 | AOD | 2 | 155
Sim | LHC13d3 | 195389-195677 | ESD | - | 21
Sim | LHC11a10a_bis | 137161-139510 | AOD | - | 143
Sim | LHC11a10b_plus | 137161-139510 | AOD | - | 141
Sim | LHC13d3 | 195389-195633 | AOD | - | 16
Sim | LHC14g3a | 195389-195677 | AOD | - | 23
Sim | LHC14g3b | 195389-195677 | AOD | - | 20
Sim | LHC14g3c | 195831-195872 | AOD | - | 4
Registered Datasets
KIAF Tutorial (`15.07)
  9 participants (PNU 2, Inha 6, KU 1)
Sigma MC Production support (Dr. Borissov)
  JDL for HTCondor
  sim.C/rec.C for local cvmfs access
p-Pb analysis support (Inha Univ.)
2015. 07

## Slide 32: KIAF Upgrade Plan
Providing opportunistic resources from KISTI Tier-1 in case of bursting (Up to 7,200 HS06 ~ 600 slots)
  Achieving better overall resource usage utilization for ALICE
  HTCondor + EMI test (or other combination)
Upgrading Operating System to SL6
  New XRootD has to be tested with Dataset Manager for KIAF
  HTCondor, CVMFS, PROOF on Demand are ready
End of This Year (2016)

## Slide 33: GSDC School of Computing
Chart: 
| Physics | Med | Comp
열1 | 17 | 6 | 8
6 Lectures and Lab given by GSDC Staff and External Expert
  Grid Computing
  Networking
  Linux Administration
  Shell Scripting
  Batch System
  Security (NSR)
31 Participants = 6 Seniors + 10 Graduated + 15 Undergrad
4 days program transferring computing knowledge
needed for data-intensive fundamental research supported by GSDC
(1st Feb ~ 4th Feb 2016)

## Slide 34: conclusion

## Slide 35
KISTI contributes to Grid Computing for LHC specially ALICE with Tier-1
  Raw data reconstruction and preservation
  Mass MC production and User analysis via LEGO Train
  Chaotic User Analysis
KISTI is at your disposal for supporting any kind of issues related Computing
  User Analysis Facility and Technical Support
  Training program

## Slide 36: 감사합니다. آپ کا شکریہ . धन्यवाद। ขอบคุณ 谢谢。 ありがとうございます。 Terima kasih . Благодаря. Dank u. Ευχαριστώ. Dziękuję. Grazie. Vielen Dank. Dank je. Merci. Thank you.