## Slide 2
NSW structural improvements

## Slide 3: Why ?
Modifications in the design were done after the FDR for the following reasons :
To relax some tight tolerances to decrease the production cost
To deduce the size of some pieces to ease the fabrication, transport and installation
To make some items standard for side A and C and to reduce the number of drawing and ease the production and assembly logistic.
To improve the positioning for a better control of the geometry shape.
To improve connection stiffness and ease their production and assembly

## Slide 4: nSW A-plate
The old version of the A-plate was entirely welded and considered like a single part
The new version is fully bolted and not anymore welded with a bottom plate mounted with slot holes
We also remove the top middle plate so the lateral plates are now independant
The reinforcement ribs is now bolted and we add cut-out for the sTGC frame on the new version
Old
New
Central plate mounted with slot holes
sTGC Frame cut-out

## Slide 5: Inner area
Old
The A-plate as a single part needed a jig to correctly locate the holes for the Hub pins
In the new design , the jig is not needed because the 2 lateral plates are independant (easier for transport, manufacturing and assembly)
As a conséquence
  it disconnects the dependancy between the production of the Hub and the A-plate
  It reduce the manufacturing tolerance and therefore shall decrease the production cost
HUB pins holes
Jig Hole and slot Hole
JIG

## Slide 6: Outer area
The anchorage is now adjustable => reduce the production tolerance for the same stiffness
The counterdrilled pins is not anymore in the same positions => better control and access
Old
New
Fixed L-shaped anchorage
Adjustable anchorage
Couterdrilled pins
Couterdrilled pins

## Slide 7: Shims and bolted design simplification
Old
New
As you can see, the new shims shape are simpler and easier to install (screwed instead of welded) => less deformation are expected and production cost reduce
We also remove all the slotted holes all along the lateral plates. This slotted holes were there to weld the reinforcement ribs => less deformations are expected
Slot holes for welding

## Slide 8: LS spoke links
Old
New
According with the FEA calculation, we discover that the A-plate is stiffer than the LS spoke itself so we decide to decrease the size and the numbers of holes (from 28 M12 to 6 M8 )
Note : we decreased also the size of the central plate as it has no influence on the stability (the scale on the two pictures are the same )

## Slide 9: Let’s talk about drawings
Obsolete
According to the new design , we reduced the amount of drawings (put in obsolete 14 drawings and add 10)
We made a huge effort to relax the geometrical tolerances => cost reduction

## Slide 10: A-plate - conclusion
We decreased the overall Weight to approx 350 Kg
We reduced at the minimum the welded connections to avoid out of plane deformation.
We avoided the need for a JIG to suppressed any dependency between the differents manufacturer.

## Slide 11: LS spoke outer part
Old
New

## Slide 12: Plates connection 1/2
The old design requires 2 different lateral plates with 3 welded ribs on each
The positionning angle and tolerance between the plate and the ribs were very important to garanty the assembly, but were nearly impossible to reach without complex remachining
If these angle are not respected, the connecting plates can break the weld (FEA talk by Augusto)

## Slide 13: Plates connection 1/2
So we decided to completly change the design of the connecting plates between lateral plates by removing the old ribs and add several standard triangle ribs
There are not anymore welded parts and everything is bolted => less deformation and cost reduction
We added the KM plate as an angle reference for the full box
KM plate

## Slide 14: Plates connection 2/2
We changed how the connecting plate are linked (simpler)
On the old version, there were cut-outs on the lateral plate and screwed on the side
We changed the design to avoid this cut-out and concentrate the machining only on positioning surfaces
Finally, the lateral plate is now used on both sides (left-right) of each LS spokes

## Slide 15: Lateral plate
The generic lateral plate is simpler and easier to realize
You can see now slotted holes in place of holes. This was done to use it both on Side C and side A => standardisation and cost reduction

## Slide 16: Let’s talk about drawings
Obsolete
According to the new design , we reduced the amount of drawings (we put in obsolete 16 drawings and add only 2)
We make a huge effort to make the design simpler to reduce costs and also release some tolerances

## Slide 17: LS spokes outer part - conclusion
Decreased the number of parts and fasteners
We avoided welded parts
Standardisation all the way

## Slide 18: LS spoke inner part
Old
New

## Slide 19: Base part
The old base part was bolted on the main part (bottom and side) and welded all along
We redisigned the base to avoid gaps between parts before welding for a better precision and rigidity while decreasing the production cost.
Screws + weld

## Slide 20: Main part
We added a cutout to connect the LSI-LSO connection bar => reduction of the deformation
We also changed the fillet on the side to a chamfer (easier to make)
Filet
Chamfer
LSI-LSO connection bar

## Slide 21: Let’s talk about drawings
Obsolete
According to the new design , we reduced the amount of drawings (we put in obsolete 1 drawings)
We made a huge effort to make the design simpler to reduce costs (filet > chamfer )
The result is a more precise and rigid base part

## Slide 22: LS spokes inner part - conclusion
Simplifying the design
Stiffer base

## Slide 23: SS spoke
Old
New

## Slide 24: Base part 1/4
The old design was made with severals plates bolted togheter and also a welded beam, welded to these plates, the bending rigidity of this assembly was not optimum
Welded Beam
Welded all around

## Slide 25: Base part 2/4
How the spokes angle was driven :
Angle is given by the base part (A)
Go through lateral straight plates (B)
Touching the Beam face (C)
Correct angle betwen C (D)
A
B
C
D

## Slide 26: Base part 3/4
The new design is made with less plates and position pin between parts for a well defined positioning

## Slide 27: Base part 4/4
How the spokes angle is now driven :
Angle is given by the interface plate (A) With 3 pins and slot holes system for more accuracy and more rigidity (B)
Interface plate (A)
Pins (B)
Pins (B)

## Slide 28: JD joint 1/3
Old
New

## Slide 29: JD joint 2/3
The old design was made with :
Shim (A)
Support (B)
Square profile (C)
Threaded masselote (D)
D
C
A
B
The cutout on support B was very difficult to do and the thickness went down to 5 mm
This cutout was requiring also to be ajusted to the square prolife before welding them togheter

## Slide 30: JD joint 3/3
The new design is made with:
Spacers (A)
JD-adjust shim (B)
JD joint (C)
Positions pins (D)
B
C
A
The JD joint itself is made with several plate welded on a standard rectangular profile for a better rigidity and a direct load transfer to JD
C

## Slide 31: JD connection
old
new
On the old version , the JD was not threaded and the screws passthrough JD and go to the masselote
On the new design the JD is threaded and we don’t need to go on the other side to put the screws (all the assembly is done from HO face)

## Slide 32: Other improvements
In order to maximize the standardization, we made few ajustement like adding the AL-KM on both side or adding holes on the JD joint to be used on side A as well
AL-KM supports
Generic Side C/side A JD joints

## Slide 33: Let’s talk about drawings
Obsolete
According to the new design , we reduced the amount of drawings (we put in obsolete 13 drawings and add 10 drawings)
We made a huge effort to make the design simpler to reduce costs (filet > chamfer )

## Slide 34: SS spokes - conclusion
Increased the accuracy of the spoke angle
Avoided difficult welded part
Simplified mounting opperation (Screws passthrough nJD)
More rigid JD-joints

## Slide 35: Feet spoke
Old
New

## Slide 36: Bottom Plate 1/
The old design was made with a very massive and difficult to adjust/machining parts
The new one is much easier and relys on standard joints and simple design wedges
Old
New

## Slide 37: Bottom Plate 2/
The new design is made with parts much easier to manufacture and with a kinematic feature to escape the hub pins during the insertion sequence
The bottom plate can lift up to 25 mm from the NJD feet and when the spoke touch the NJD feet , there is enough room to insert the spoke below the hub
Bottom plate
Wedges
25 mm

## Slide 38: Hub connection
We made a huge effort for standardize the design and now the feet have the same hub connection like the SS spokes. Instead in the old design, feet spokes were connected to the hub using dedicated rails
old
New

## Slide 39: Bottom legs 1/
The old design was made with a full-single-body stainless steel extention with welded ajusting plate and bolted to the welded profile This extention was very massive, hard to adjust inside the profile and difficult to machine
For the new design, we just extended the welded profile and use a wedge to adjust and de facto reduce the production tolerances.
New
Old

## Slide 40: Bottom legs 2/
The old design was made with a full-single-body stainless steel extention with welded ajusting plate and bolted to the standard profile This extention was very massive, hard to adjust inside the profile and difficult to machine
For the new design, we added a standard profile link with position pins plates
New
Old

## Slide 41: Bottom legs 3/
The old design contains 3 differents reinforcement pipes and several shims
The new design relys on only 1 reinforcement pipe as the effort driven through this element is less than expected (verified with FEA model)
Old
New

## Slide 42: Other improvements
In order to maximize the standardization of the parts, some of them are used both in foot 1 and foot 2 and also in side C and side A
For exemple, the Foot 2 got only 2 detail drawings (bottom plate and welded profile) all the other parts are the same for SS spoke and Foot 1

## Slide 43: Let’s talk about drawings
Obsolete
According to the new design , we reduced the amount of drawings (we put in obsolete 23 drawings and add 12 drawings)
We used more standard parts like JD joints

## Slide 44: Feets spokes - conclusion
Decreased the number of parts and adjustment
Standardized the design according to the SS spokes
Released fabrication tolerances by adding adjusting wedges

## Slide 45: Hub
Old
New

## Slide 46: Pin dimension
According to the FEA calculation, we changed the diameter of the spoke pins from Ø100 to Ø30 and we reduced the length
We also removed the rails for the Feet spoke (see slide 37) to standardize the Ø30 all around the hub
Old
New
Pin Ø30
Pin Ø100
Feet rails

## Slide 47: Pin dimension
The old design was made with six inserts inserted into one-meter precise (very tight tolerances) holes in the HUB
The new design allow gap between insert and hole with the addition of a anti-rotation pin and nut on the other side to ease both fabrication and installation operations
Old
New
Anti-rotation pin
Washer and nut

## Slide 48: Lifting
The lifting interface can use the same threaded holes used for spoke fixation

## Slide 49: Hub - conclusion
More realistic locking insert design
Standardized the design according to the SS spokes and feet spokes

## Slide 50: nJD
After several months of calculations, it has been agreed to remove the return flux ring
Old
New

## Slide 51: Contact faces
In order to be more precise and to guaranty the plane assembly, we decided to machine all interfaces surfaces in contact by removing 2 mm between them
All the positions according to IP are respetect
New

## Slide 52: Other improvements
The NJD reflects the modification done on spokes and Hub
Spokes holes patterns

## Slide 53: NJD - conclusion
More precise structure (fonctional faces are not raw anymore )
Lighter structure