## Slide 1: The detector read-out in ALICE during Run 3 and 4 Filippo Costa ALICE O2/CRU for the ALICE collaboration
CHEP 2016 Conference, San Francisco, October 8-14, 2016

## Slide 2
1st PART: INTRODUCTION TO ALICE UPGRADE
  Motivation.
  Requirements.
2nd PART : THE DETECTOR READOUT
  Main difference from the current readout schema.
  System operation in triggered mode.
  System operation in continuous mode.
3rd PART : RESULT and CURRENT STATUS
OUTLINE

## Slide 3
INTRODUCTION TO
ALICE RUN3

## Slide 4
ALICE Upgrade Strategy
GOAL:
High precision measurements of rare probes at low pT which cannot be selected with a trigger. Target a recorded Pb-Pb luminosity > 10 nb-1 => 9x1010 events to gain a factor 100 in statistics over the Run1 + Run2 programme.
Significant improvements of vertexing and tracking capabilities
DETECTOR:
Read-out all Pb-Pb interactions at a maximum rate of 50kHz (i.e. L = 6x1027 cm-1s-1) upon a minimum bias trigger
Read-out all pp and p-Pb interaction at a maximum rate of 200 kHz.
Perform online data reduction based on reconstruction of cluster and tracks
Improve vertexing and tracking at low pT => New Inner Tracking System (ITS)
TPC continuous readout to keep up with 50 kHz interaction rate, to deal with event pile-up and avoid trigger generated dead time.

## Slide 5
Partial calibration and reconstruction online, replacing the original raw data with compressed data
90 GB/s
3.6 TByte/s into PC farm
O2 (Online Offline) System
ALICE UPGRADE
O2 computing farm:
~ 100 k CPU cores
~ 5000 GPUs and ~500 FPGAs
~ 60 PB of storage
STORAGE
Acq rate:
Pb-Pb 50 kHz
pp and p-Pb up to 200 kHz
Complete change in detector readout
continuous
triggered
New DAQ - HLT - OFFLINE systems.

## Slide 6
Main differences
between
RUN2 & RUN3

## Slide 7
TRIGGER
SYSTEM
FEE
FEE
FEE
FEE
DAQ
CRORC
CRORC
RORC
DATA
RUN2
Trigger connected to the FEE
Triggered readout mode
1 readout link, DDL (Detector Data Link)

## Slide 8
TRIGGER
SYSTEM
FEE
FEE
FEE
FEE
DAQ
CRU
CRU
CRORC
DATA
Detector that receives trigger and clock from CRU
TPC
MCH
MID
MFT
TOF
FIT
ZDC
RUN3
CRU:
CommonReadout
Unit
Trigger connected to the FEE and CRU
Triggered and Continuous readout mode
2 readout link, DDL and GBT

## Slide 9
The detector readout
during RUN3

## Slide 10
TRIGGER
SYSTEM
FEE
FEE
FEE
FEE
DAQ
CRU
CRU
Readout
card
DATA
BUSY
BUSY
TRIGGERED MODE
Upon reception of a trigger signal, each detectors respond and send the corresponding data.

## Slide 11
TRIGGER
SYSTEM
FEE
FEE
FEE
FEE
O2
CRU
CRU
CRU
DATA
DATA is sent regardless the triggers
CONTINUOS MODE
Data are not delimited by physics trigger, but are composed by several data streams

## Slide 12
Time
Heart Beat Frames (HBF):
data stream delimited by two HBs
HBF and TF rates programmable
Typical values:
HB: 1 per orbit, 89.4 µs: ~10 kHz
TF: 1 every ~20 ms: ~50 Hz
 1 TF = ~256 HBF
(Front-end &)
CRU
Continuous read-out
Heart Beat (HB)
issued in continuous &
triggered modes
to all detectors

## Slide 13
Heart Beat (HB)
issued in continuous &
triggered modes
to all detectors
Time
Heart Beat Frames (HBF):
data stream delimited by two HBs
Physics trigger
can be sent to upgraded detectors
will be sent to
non-upgraded detectors
Trigger data fragments
(Front-end &)
CRU
Triggered read-out
HBF and TF rates programmable
Typical values:
HB: 1 per orbit, 89.4 µs: ~10 kHz
TF: 1 every ~20 ms: ~50 Hz
 1 TF = ~256 HBF

## Slide 14
Heart Beat (HB)
issued in continuous &
triggered modes
to all detectors
Time
Heart Beat Frames (HBF):
data stream delimited by two HBs
Time Frame (TF):
grouping of all STFs from all FLPs for the same time period from triggered or continuously read out detectors
Physics trigger
can be sent to upgraded detectors
will be sent to
non-upgraded detectors
Trigger data fragments
(Front-end &)
CRU
FLP
EPN
FLP 1
FLP n
Triggered read-out
Sub-Time Frame (STF) in FLP 0:
grouping of (~256) consecutive HBFs from one FLP
HBF and TF rates programmable
Typical values:
HB: 1 per orbit, 89.4 µs: ~10 kHz
TF: 1 every ~20 ms: ~50 Hz
 1 TF = ~256 HBF

## Slide 15
HB trailer
HB header
Payload (if no hits empty)
STF @ FLP0
HB0
HB1
HB2
HB3
HB4
HB5
HB6
HB7
HB8
HB9
HB255
..
STF @ FLP1
STF @ FLP2
STF @ FLPn
FLP .. First Level Processor
EPN .. Event Processing Node
STF .. Sub Time Frame
TF .. Time Frame
HB .. Heart Beat Trigger
HBF .. Heart Beat Frame
HB0
HB1
HB2
HB3
HB4
HB5
HB6
HB7
HB8
HB9
HB255
..
HB trailer
HB header
Deleted HBF (no or partial data)
TF0 @ EPN
TF1 @ EPN
Time Frames/Heart Beat Frames

## Slide 16
HB trailer
HB header
Payload (if no hits empty)
HB trailer
HB header
No or partial HBF data
STF @ FLP0
HB0
HB1
HB2
HB3
HB4
HB5
HB6
HB7
HB8
HB9
HB255
..
STF @ FLP1
STF @ FLP2
STF @ FLPn
HB0
HB1
HB2
HB3
HB4
HB5
HB6
HB7
HB8
HB9
HB255
..
TF0 @ EPN
TF1 @ EPN
FLP .. First Level Processor
EPN .. Event Processing Node
STF .. Sub Time Frame
TF .. Time Frame
HB .. Heart Beat Trigger
HBF .. Heart Beat Frame
The main goal is to collect one complete TF or at least one or more HBFs
What happens if CRU buffers get full?

## Slide 17
STF @ FLP0
HB0
HB1
HB2
HB3
HB4
HB5
HB6
HB7
HB8
HB9
HB255
..
STF @ FLP1
STF @ FLP2
STF @ FLPn
TF0 @ EPN
HB0
HB1
HB2
HB3
HB4
HB5
HB6
HB7
HB8
HB9
HB255
..
TF1 @ EPN
HB trailer
HB header
Payload (if no hits empty)
HB trailer
HB header
No or partial HBF data
FLP .. First Level Processor
EPN .. Event Processing Node
STF .. Sub Time Frame
TF .. Time Frame
HB .. Heart Beat Trigger
HBF .. Heart Beat Frame
What happens if CRU buffers get full?

## Slide 18
  CRU will autonomously abort the read-out of corresponding HBF
  Delete HBF data from buffer
  Send negative HB acknowledge to CTP
  Send negative acknowledge to FLP in the HB header/trailer pair
  Read-out continues
  Counter and state machine stay consistent
In nominal conditions occurrence assumed to be negligible
What happens if CRU buffers get full?

## Slide 19
CTP
FLP
CRU
CTP FLP
Readout
Links
HBF/trigger acknowledge/
message
3b
HBF/Trigger
Transmitted ?
2
HB trigger/message
1
HBF Header
(Payload)
Trailer
3a
HB Map
1 1 1 0 1
1 0 1 1 1
HB Map
1 1 1 0 1
1 0 1 1 1
Delete HBF from buffer
4
Delete HBF from memory
5
HB Map
6
What happens if CRU buffers get full?

## Slide 20
Current status of
the development
&
RESULTS

## Slide 21
Detector | number of GBT | readout mode
TOF | 2 | triggered
ITS | 1 | triggered
FIT | 1 | triggered
MCH | 1 | triggered
MID | 1 | continuous
TPC | 2 | continuous
Several detectors have a readout chain using GBT to test their FEE prototype. The readout modes are triggered and continuous
Current status

## Slide 22
700 MB/s
2 GBT links connected to the readout system
FEE # 1
FEE # 2
DAQ
TOF setup
160 kHz

## Slide 23
Readout system used to collect data in continuous mode and to configure the FEE electronics using the GBT protocol
TPC setup

## Slide 24
THANK YOU
QUESTIONS?

## Slide 25
2020-2021
Design
R&D
Demonstrators
TDR
Products selection
Detailed design
R&D
Prototyping
Development
Products selection
Prototypes
Detailed design
R&D
Prototyping
Development
Products selection
Prototypes
Final components
Deployment
Commissioning
Development
Products selection
Final components
Deployment
Commissioning
Production
2018-2019
2016-2017
2014-2015
2012-2013
High-Level Design
R&D
Project organization
Schedule
https://cds.cern.ch/record/2011297/files/ALICE-TDR-019.pdf

## Slide 26
Busy, throttle schema