## Slide 1
Configuration validation in the
art event-processing framework
Kyle J. Knoepfel, Fermi National Accelerator Laboratory
The art event-processing framework loads at run-time a set of modules to create workflows that serve in data acquisition, simulation generation, reconstruction algorithm execution, and physics analysis.
art processes are configured by a collection of user-specified parameters defined using the FHiCL language. To aid users in properly configuring their processes, a configuration retrieval, description, and validation suite has been implemented that:
has a single point of maintenance for users,
can represent in C++ an arbitrary FHiCL structure, and
can be enabled at the user level without breaking existing workflows and C++ source code.
Atom: a named value with no underlying structure.
Sequence: a named list of un-named values.
Table: a named collection of name-value pairs.
FHiCL language
Configuration representation in C++
Module description and validation
C++ implementation aspects
Additional features
verbose: false
particleIDs: [11, 13]
g4settings: {
shape: sphere
radius: 2.0 # mm
}
The Fermilab Hierarchical Configuration Language is the language used for configuring art processes. Configuration parameter names and their associated values are classified in three ways:
If a user wants to validate the above configuration in his/her module, the following would be specified in the C++ source code:
struct Config {
Atom<bool> verbose { Name("verbose") };
Sequence<int> particleIDs { Name("particleIDs") };
struct G4Settings {
Atom<string> shape { Name("shape"), "sphere" };
Atom<double> radius { Name("radius"),
Comment("Units are mm.") };
};
Table<G4Settings> g4Settings { Name("g4Settings") };
};
The above example is a typical module configuration. Note that nested tables and sequences (and tables in sequences) are allowed, leading to configurations with arbitrary depth.
$ art --print-description G4Module
moduleLabel: {
module_type: G4Module
verbose : <bool>
particleIDs: [ <int>, ... ]
g4Settings : {
shape: "sphere" # default
## Units are mm.
radius: <double>
}
}
For a module that supports the configuration above (e.g. G4Module), a description similar to the one at the right is provided by art.
Suppose a user were to mis-specify shape as ‘Shape’, an error similar to the following would be emitted:
The implementation of the suite relies heavily on modern C++ facilities (C++11/14):
variadic templates for representing heterogeneous sequences,
lambda expressions for configuration tree-walking and conditional configuration based on the value of a previously validated parameter,
automatic type deduction, etc.
Adoption of such C++ techniques provides a type-safe suite, moving error detection, when possible, to the compile-time stage instead of the run-time stage.
Any parameters prefaced with '#' are optional.
Unsupported parameters:
+ g4Settings.Shape [ ./module.fcl:6 ]
File name and
line number of parameter.
The design of the suite was informed from interactions with art users. Based on those discussions, a large number of additional features have been included in the suite. Additional parameter types include:
optional parameters – where it is permitted to omit supported parameters without specifying a default in source code,
delegated parameters – where the parameter itself must be present, but its value (atom, sequence, or table) is unspecified,
conversion parameters – where a configuration sequence can be converted directly to a user-specified type, without having to retrieve “by hand” individual sequence elements and convert them to the relevant type.
Introduction
The Atom, Sequence, and Table class templates receive a template argument that specifies the type to which the FHiCL parameter should be converted within the C++ code.
The validation system supports defaults in source code (e.g. the shape parameter), as well as comments to be printed out when the description is requested (e.g. the radius parameter).
Deployment in art and its experiments
User feedback regarding the suite has been positive. Almost all art-provided facilities enable configuration validation and description. Individual experiments that use art are adopting the suite in their own code according to their own needs.