## Slide 1: Computing at CERN International High School Teacher Programme 2016
Niko Neufeld, CERN/EP

## Slide 2: Fundamental questions…
How to explain that particles have mass?
  Theories and accumulating experimental data…getting close
What is 96% of the Universe made of?
  We only observe 4% of the apparent mass
Where is all the anti-matter?
  Why is Nature not symmetric?
What was the state of matter just after the Big Bang?
  “Soup” of quarks and gluons before they condensed into matter?

## Slide 3: Tools: LHC and detectors
Exploration of a new energy frontier
in p-p and Pb-Pb collisions
LHC ring:
27 km circumference
CMS
ALICE
LHCb
ATLAS
General Purpose, proton-proton, heavy ions
Discovery of new physics:
Higgs, SuperSymmetry
pp, B-Physics, CP Violation
(matter-antimatter symmetry)
Heavy ions, pp
(state of matter of early universe)
Notes: 3

## Slide 4: The LHC Experiments today
ALICE – “A Large Ion Collider Experiment”
  Size: 26 m long, 16 m wide, 16m high; weight: 10000 t
  35 countries, 118 Institutes
  Material costs: 110 MCHF
ATLAS – “A Toroidal LHC ApparatuS”
  Size: 4 6m long, 25 m wide, 25 m high; weight: 7000 t
  38 countries, 174 institutes
  Material costs: 540 MCHF
CMS – “Compact Muon Solenoid”
  Size: 22 m long, 15 m wide, 15 m high; weight: 12500 t
  40 countries, 172 institutes
  Material costs: 500 MCHF
LHCb – “LHC beauty” (b-quark is called “beauty” or “bottom” quark)
  Size: 21 m long, 13 m wide, 10 m high; weight: 5600 t
  15 countries, 52 Institutes
  Material costs: 75 MCHF
Regular upgrades … next 2019/20 (Long Shutdown 2)
1 CHF ~ 1 USD

## Slide 6: Higgs-boson in CMS

## Slide 7: Lead meets lead in ALICE

## Slide 8: Mr. Higgs’es boson is also in ATLAS

## Slide 9: An extremely rare event in LHCb

## Slide 10: And much more than just the LHC…

## Slide 11: Anti-matter factory

## Slide 12: So apart from hunting daemons… What are we doing with the anti-matter?

## Slide 13: What are these data?
Raw data:
  Was a detector element hit?
  How much energy?
  What time?
Reconstructed data:
  Momentum of tracks (4-vectors)
  Origin
  Energy in clusters (jets)
  Particle type
  Calibration information
  …
150 Million sensors deliver data … 40 Million times per second
Up to 6 GB/s to be stored and analysed after filtering

## Slide 14: Data and Algorithms
HEP data are organized as Events (particle collisions)
Simulation, Reconstruction and Analysis programs process “one event at a time”
  Events are fairly independent  Trivial parallel processing
Event processing programs are composed of a number of Algorithms selecting and transforming “raw” event data into “processed” (reconstructed) event data and statistics
Pseudo-physical information:
Clusters, track candidates
Physical information:
Transverse momentum,
Association of particles, jets,
id of particles
RAW
Detector digitisation
~2 MB/event
ESD/RECO
~100 kB/event
AOD
~10 kB/event
TAG
~1 kB/event
Relevant information
for fast event selection
Triggered events
recorded by DAQ
Reconstructed
information
Analysis
information
Classification
information

## Slide 15: Know Your Enemy: pp Collisions at 14 TeV at 1034 cm-2s-1
(pp) = 70 mb --> >7 x 108 /s (!)
In ATLAS and CMS* 20 – 30 min bias events overlap
HZZ Z mm H 4 muons: the cleanest (“golden”) signature
And this
(not the H though…)
repeats every 25 ns…
*)LHCb @4x1033 cm-2-1 isn’t much nicer and in Alice (PbPb) is even more busy

## Slide 16: What’s mother nature’s menu?
A typical collision is “boring”
  Although we need also some of these “boring” data as cross-check, calibration tool and also some important “low-energy” physics
Interesting physics: one in a million to one in 100 million collisions
Exciting physics involving new particles/discoveries: one in a billion or less
 Need to efficiently identify these rare processes in the overwhelming background, such that we need to store only a “smaller” highly enriched subset of the raw data
Nobel dreams are here

## Slide 17: Data Rates
Particle beams cross every 25 ns (40 MHz)
  Up to 25 particle collisions per beam crossing
  Up to 109 collisions per second
Basically 2 event filter/trigger levels
  Data processing starts at readout
  Reducing 109 p-p collisions per second to O(1000)
Raw data to be stored permanently: >15 PB/year
 | Incoming data rate | Outgoing data rate | Reduction factor
Level1 Trigger (custom hardware) | 40000000 s-1 | 10^5 – 10^6 s-1 | 400-10,000
High Level Trigger (software on server farms) | 2000-1000000 s-1 | 1000 -10000 s-1 | 10-2000
Physics Process | Events/s
Inelastic p-p scattering | 108
b | 106
W → eυ ; W → µυ ; W → τυ | 20
Z → ee ; Z → µµ ; Z → ττ | 2
t | 1
Higgs boson (all; mH = 120GeV) | 0.04
Higgs boson (simple signatures) | 0.0003
Black Hole (certain properties) | 0.0001

## Slide 18: Defeating the data-torrent
Thresholding and tight encoding
Real-time selection based on partial information
Final selection using full information of the collisions
These selection systems are called “Triggers” in high energy physics

## Slide 19: Collisions in motion 

## Slide 20: The first level trigger

## Slide 21: Selection based on partial information
A combination of (radiation hard) ASICs and FPGAs process data of “simple” sub-systems with “few” O(10000) channels in real-time
  Other channels need to buffer data on the detector
this works only well for “simple” selection criteria
long-term maintenance issues with custom hardware and low-level firmware
crude algorithms miss a lot of interesting collisions
Notes: No single computer or electronical system can process the enormous amount of data produced in the LHC experiments.
A divide and conquer approach is used.
The many regions of the large LHC experiments are treated separately and in parallel. Sophisticated custom-built electronics (top right-hand picture from ATLAS) is connected to a small part of the detector. From there it reads out the collision data in this region only but 40 Million times a second. Many, many such electronics modules are needed to cover the huge LHC detectors. The bottom left picture shows a small part of the trigger electronics of ATLAS, where in each column there are 40 modules as shown above.
Since the information is limited, because it only comes from a small segment, only a preliminary decision can be taken. The filtering can only tell the difference between collisions which look quite different to the electronics (to the naked eye they still look the same, of course).
The number of collisions retained after this step is still enormous: between 100.000 and 1.000.000 every second. But the filtering, which is needed to select the interesting events out of these 100.000 needs to be much more sophisticated.

## Slide 22: Level 1 Trigger
The Level 1 Trigger is implemented in hardware: FPGAs and ASICs  difficult / expensive to upgrade or change, maintenance by experts only
Decision time: ~ a small number of microseconds
It uses simple, hardware-friendly signatures  looses interesting collisions
Each sub-detector has its own solution, only the uplink is standardized 

## Slide 23: Finding Muons (2d view)

## Slide 24: Calorimeter data

## Slide 25: Data Acquisition

## Slide 26: Data Acquisition (generic example)
GBT: custom radiation- hard link from the detector 3.2 Gbit/s
DAQ (“event-building”) links – some LAN (10/40/100 GbE / InfiniBand)
Links into compute-units: typically 10 Gbit/s (because filtering is currently compute-limited)
Detector
DAQ network
100 m rock
Readout Units
Compute Units
Every Readout Unit has a piece of the collision data
All pieces must be brought together into a single compute unit
The Compute Unit runs the software filtering (High Level Trigger – HLT)
10000 x
~ 1000 x
~ 3000 x

## Slide 27: Future LHC DAQs in numbers
 | Data-size / collision [kB] | Rate of collisions requiring full processing [kHz] | Required # of 100 Gbit/s links | Aggregated bandwidth | From
ALICE | 20000 | 50 | 120 | 10 Tbit/s | 2019
ATLAS | 4000 | 500 | 300 | 20 Tbit/s | 2022
CMS | 4000 | 1000 | 500 | 40 Tbit/s | 2022
LHCb | 100 | 40000 | 500 | 40 Tbit/s | 2019

## Slide 28: High Level Trigger

## Slide 29: High Level Trigger
Pack the knowledge of tens of thousands of physicists and decades of research into a huge sophisticated algorithm
Several 100.000 lines of code
Takes (only!) a few 10 - 100 milliseconds per collision
“And this, in simple terms, is how we find the Higgs Boson”
Notes: To find the Higgs Boson or other rare events among the remaining 100.000 or so collisions we need the collected knowledge of the physicists working at LHC. All this physics knowledge brought together over generations is incorporated in huge, highly sophisticated computer programs, which despite their size take only a fraction of a second to run on a modern computer.
These programs will select the most promising collisions. The selected collisions will be written to permanent storage and kept for further analysis by physicists.
Despite the speed of the algorithms a huge number of computers is required to perform this selection, because so many collisions need to be decided upon every second.

## Slide 30: High Level Trigger: Key Figures
Existing code base: 5 MLOC of mostly C++
Almost all algorithms are single-threaded (only few exceptions)
Currently processing time on a X5650 per event: several 10 ms / process (hyper-thread)
Currently between 100k and 1 million events per second are filtered online in each of the 4 experiments

## Slide 31: Reconstruction & Analysis

## Slide 32: Data Handling and Computation for Physics Analysis
Online
Offline Reconstruction
Offline Simulation w/GEANT4
Offline Analysis w/ROOT
Batch
physics
analysis
detector
Event
summary
data
Raw
data
Event
simulation
Analysis objects
(extracted by physics topic)
Selection &
reconstruction
Processed
Data (Active tapes)
100%
10%
1%
Online trigger and filtering
Interactive
analysis
Event
reprocessing

## Slide 33: Reconstruction
Track: f = 0.23, h = 0.75, pT = 2.3 GeV/c
Probability to be a Pion: 70%, Kaon: 28%, Proton: 2%
Small part of a collision
Reconstruction = Conversion of electronic signals into physical „objects“
Address = which detector/sensor has read these data?
Data = what was detected?

## Slide 34: Reconstruction steps
Abstraction of electronic signals from the detector
  Detector-element 1244 has measured a signal of 120 at time 1333096259.344245  Signal at position x = 1.2 cm, y = 4.5 cm, z = 3.2 cm, deposited energy of 100 keV
  Requires precise information about location of the detector element (alignment) and of its signal sensitivity (calibration)
Particles frequently create signal in adjacent detetor-elements These signals are combined into “clusters”
The clusters are combined into “tracks” (pattern-recognition)
Tracks are combined to reconstruct collision points (“primary vertices” == where an orignal beam-proton has hit another beam-proton) and decay (“secondary” and “tertiary”)) vertices

## Slide 35: Pattern recognition
Recognition of tracks
  Straight in the direciton of the magentic field
  Deviation on a curved trajectory in a normal plane around the magentic field  radius of curvature allows to determine the momentum
Primary vertex
Secondary vertices
  Allows detection of particle decays

## Slide 36: Pattern-recognition(2)
p
p
p
L
X

## Slide 37: Combination of detector-systems

## Slide 38: Simulation
Understanding the detector-response requires a detailed simulation
A detector-simulation tries to reproduce the behaviour of the detector as faithfully as possible
HEP simulation software consists of
  Physics simulator: simulates which elementary particles are created by a collision in the detector: e.g. Pythia
  Geometry: detailed description of all active(= capturing signals) and passive (= mechanical support, cooling, power-supply, …) elements in the detector
  Particle transport: simulates the interactions of particles with the material of the detector. E.g. GEANT4
    Particles can be deflected, absorbed, they can decay or even be created
    Energy-transfer is recorded in detail
Afterwards the simulated signals are passed through the exact same reconstruction chain as the “real” data

## Slide 39: Simulation (2)
Simulation results allow to estimate the influence of the detector itself on the measurements
Important examples
  Track reconstruction efficiency – how probable is it to actually find a track?
  Resolution – how precise is a known quantity being measured?
  Error-rate / ghost-rate ("fake rate") – how often do we reconstruct a particle where there actually was none?
pT (GeV/c)
Effizienz
Relative Abweichung der Energie

## Slide 40: Analysis
Interpretation of reconstruction results (tracks, vertices, calorimeter information)
  Processing of many collisions to get a statistically significant result
  Most frequent task for the (research) physicist
Work-flow:
  Selection of suitable collisions
  Combination of required quantities extracted from the collisions (often in histograms)
  Correction of detector effects
  Extraction of physical quantities
  Estimation of uncertainties
  Comparision of results with theoretical predictiosn
Sociology: while reconstruction is usually a “central” task done by a relatively small team of dedicated “experts”, analysis is being done by many (almost) all groups and/or individuals collaborating in an experiment.

## Slide 41: Analysis – Example: momentum distribution
pT (GeV/c)
Particles per GeV/c
extraction of
measurements in a “histogramm"
Reconstructed
collisions
Correction
of detector-
effects
Reconstruction-
efficiency
(from simulation)
result+ comparison
with model
This is of course simplified 
Question: How many particles have which momentum and how often?
pT (GeV/c)
efficiency
pT (GeV/c)
Momentum distribution

## Slide 42: The ROOT framework
ROOT is a large, object-oriented framework for data-processing and analysis
Being developed at CERN with a core team of professional developers and many contributions from the community
Implemented in C++
Comprehensive 2D and 3D Tools for visulalization of data
Libraries for mathematics and statistics
Can be used as a library (from scripts and applications) or as a stand-alone program for data-analysis
Available for Linux, Mac, Windows
Information & Download  http://root.cern.ch
Histogramm:
3D Funktion:

## Slide 43: Example: ROOT histogram
Histogramms store data in value intervals (“bins")
  A measurement value is “put” into a bin of appropriate width
  This allows visualization and statistical analysis
Histogrammbeispiel (C++ code)
hist = new TH1F("hist", "Vertex distribution ;z (cm);Events", 20, -10, 10);
hist->Fill(0.05);
hist->Fill(-7.4);
hist->Fill(0.2);
hist->Draw();

## Slide 44: IT facility

## Slide 45: Data to keep

## Slide 46: WLCG: A global collaboration…
Tier 0
Tier 1
Tier 2
~150 sites
>250k CPU cores
>150 PB disk
Tier-0 (CERN):
Data recording
Initial data reconstruction
Data distribution
Tier-1 (11 centres):
Permanent storage
Re-processing
Analysis
Tier-2 (~140 centres):
Simulation
End-user analysis

## Slide 47: Summary
CERN is the leading particle physics laboratory in the world hosting more than 100 experiments
The flagship programme is the LHC, whose experiments produce an unprecedented amount of data
Sophisticated IT is needed at all stages to cope with these data
The IT needs of the experiments are always growing and (often) more interesting physics requires more networking and more computing, while budgets stay constant 