## Slide 1
Lessons from 2015
Scrubbing at 450 GeV allows to mitigate e-cloud instabilities and beam degradation occurring at low energy
After this stage, relying on ADT and high Q’ and octupoles, it is possible to preserve good beam quality from injection to collision in spite of the e-cloud still present in the machine, however high heat load in the arcs
Parasitic scrubbing accumulated during intensity ramp up and physics run has lowered the heat load in the dipoles by roughly a factor two (in two months)
  The doses needed to see an evolution at this stage are very large, practically incompatible with a dedicated scrubbing run
  Relatively high intensity runs without electron cloud can cause deconditioning, visible both in heat load and beam quality, for which quick re-conditioning fills might be needed
Doublet trains were tested for the first time in the LHC during the Scrubbing Run
  e-cloud enhancement could be confirmed experimentally
  Due to violent e-cloud instabilities, it was impossible to inject enough beam and keep sufficient beam quality for efficient scrubbing with doublets

## Slide 2
Proposal for the 2016 start-up
  Arcs will be kept under vacuum  scrubbing should be – at least partially – preserved during the YETS
Scrubbing proposal for 2016:
  4 days scrubbing run deemed reasonable to recover high intensities at 450 GeV (assuming all necessary setup for high intensity is done before, e.g. injection, ADT)
  A few “refresh” scrubbing fills during first 1-2 weeks of intensity ramp up in physics (to fight deconditioning)
  During intensity ramp up:
    As long as no limitation is encountered, try to maximize electron dose by using long trains (up to 288b. per injection)  it will pay off later
    If/when cryo limit is reached, move to optimized filling schemes to gain luminosity
    Use physics fills to accumulate more scrubbing for further intensity increase
Doublet test to be performed when SEY is sufficiently low (e.g. at least after recovering the end-2015 situation) to check whether good beam quality can be preserved
    In case of positive outcome, first scrubbing stores with doublets

## Slide 3
Schedule

## Slide 4
Some points to check in preparation
  Setup to be done beforehand
    25 ns beam in injectors
    ADT, diagnostics (including ObsBox and bunch-by-bunch tune)
  Scrubbing with some beam screens at higher temperature (~100 K) – some test cells
  Cryogenic transients and limits
  TDI (do we still have pressure interlocks, has the retraction policy stayed the same?)
  MKI-Q5 (we know from 2015 that it could limit the total intensity in beam 2)
  Magnetic field in the experimental areas (discussed with G. Arduini, G. Bregliozzi, M. Taborelli, communicated to M. Lamont):
    Turning off the magnetic field of the CMS, ATLAS, ALICE solenoids for the scrubbing run does not seem to be necessary, because
      In terms of SEY, the solenoid field in standard operation anyway inhibits the electron cloud formation + SEY is low due to the NEG coating
      Vacuum-wise, the area is 99%+ NEG-coated, no additional surface cleaning needed at this stage
    LHCb dipole should be on with positive polarity