## Slide 1: HL-LHC
Lucio Rossi
Project Leader
1st International Workshop of the Supeconducting Magnet Test Stands
CERN – Globe of innovation, 13 June 2016

## Slide 2: LHC

## Slide 3: LHC the largest scientific instrument
LHC dipoles: the collider backbone
27 km, p-p at 7+7 TeV 3.5+3.5 start, 4+4 in 2012 6.5+6.5 TeV in 2015
1232 x 15 m Twin Dipoles
Operational field 8.3 T @11.85 kA (9 T design)
HEII cooling, 1.9 K with 3 km circuits (130 tonnes He inventory).
Field homogeneity of 10-4, bending strength uniformity better then 10-3. Field quality control (geometric and SC effects) at 10-5.
The dipole line in the LHC ring
All fully cold tested

## Slide 4: More than dipoles…
The pletora of SC magnets…
392 Main Quads Two-In-One rated for a peak field of 7 T.
About 100 other Two-in-One MQs
32 MQX (low-) single bore for luminosity (design L=11034 cm-2s-1), 70 mm apertures, about 8 T peak field, high quality
A «zoo» of 7600 «small» Sc magnets (correctors and higher order magnets
Total: 9 MJ stored energy (at nominal)
Large detector magnets ATLAS toroid – 25 m long 1.2 GJ CMS solenois – 12 m long 2.5 GJ
All fully cold tested

## Slide 5: SC radiofrequency, Cryogenics,
LHC: much more than magnets…
400 MHz Standing wave RF
4 single cell cavities in cryomodule, 2 crym per beam. Total 16 cavities.
Sputtered niobium design (as LEP)
Gradient 5.5 MV/m nominal (8 MV/m available)
Nominal 2MV, up to 3 MV at 8 MV/m
Cryo : 8 x 18 kW@4.5K
Collimators: 146
All fully cold tested

## Slide 6
The Higgs: the needle in a haystack
luminosity: collision rate)
Z μμ
Z μμ event from 2012 data with 25 reconstructed vertices

## Slide 7: Why upgrading the LHC?
0.75 1034 cm-2s-1
50 ns bunch high pile up 40
1.5 1034 cm-2s-1
25 ns bunch pile up 40
1.7-2.2 1034 cm-2s-1
25 ns bunch pile up 60
Technical limits to lumi increase (Machine & Experiments)
50  25 ns

## Slide 8: The project started in 2010 as EC-FP7 Design Study
The main objective of HiLumi LHC Design Study is to determine a hardware configuration and a set of beam parameters that will allow the LHC to reach the following targets:
A peak luminosity of Lpeak = 5×1034 cm-2s-1 with levelling, allowing:
An integrated luminosity of 250 fb-1 per year, enabling the goal of Lint = 3000 fb-1 twelve years after the upgrade. This luminosity is more than ten times the luminosity reach of the first 10 years of the LHC lifetime.
From FP7 HiLumi LHC Design Study application

## Slide 9: The bolt advance in luminosity

## Slide 10
FP7-HiLumi classified as «success story» by EC
Cryo@P4
Cryo@P1-P5
Beam diagnostics
BGV
New TAS and VCX

## Slide 11: HL-LHC project breakdown structure

## Slide 13: Deep changes in the Inner Triplet region (around ATLAS & CMS experiments)
International collaborations: an opportunity and a challenge, also for testing!

## Slide 14: International collaboration regards also tests
SM18 @ CERN
    HiLumi has triggered the SM18 upgrade and pays about half of it.
    HiLumi IT string is in the plan since 2015 (see talk)
US/LARP-AUP : FNAL and BNL
INFN-LASA (Milano)
UPPSALA univ.
CEA ?
More?

## Slide 15: HiLumi counts on cryogenic full power tests: no harware will be installed without test
First test in the chain is the strand/conductor! Try also to be synergic to these test!
A Magnet not testet is not worth anything, yet!
Testing, for HiLumi like for LHC, is integral part of the design-construction-qualification cycle:
    Validation of design & basic choice
    Verification of performance and of conformity to specs
    Most crititical acceptance,releasing payment and tranfer of properties (from Industry or Collaboration)
       time and schedule are IMPORTANT!!!
    Anticipate HWC and operation issues (stand-alon test and especially IT string)

## Slide 16: Thanks to Marta for orgnaizing this meeting and all of you for the great support to HiLumi