## Slide 1: Data exchange for HL LHC magnets
Ezio Todesco, CERN
With feedbacks from G. Ambrosio, H. Bajas, M. Bajko, L. Bottura, G. Chlachidze, G. De Rijk, P. Ferracin, M. Guinchard, J. Muratore, S. Russenschuck
Workshop on test stands, CERN, 13 June 2016

## Slide 2: Contents
Before the test
During the test
After the test

## Slide 3: General remarks
Each team is responsible of data reduction (transforming raw data in post-processed data)
Post-processed data should be made available to all collaboration for analysis
Systemic conflict between
  Waiting all the necessary cross-checks to distribute the data
  Having the data, even if incomplete, to be able to judge and fast react

## Slide 4: General remarks
Five types of data
    I will not consider electrical checks, which are part of manufacturing
  Mechanical measurements
  Quenches: training, voltages, current, quench start time, MIITs
  Magnetic Measurements (MM)
  Optional:
    Quench antenna
    Optic fiber
Two types of storage
  Repository-like (developed in most cases)
  Database (to be developed in some cases)
    Databases can be different (as it is today for quench and MM) – or should we have just one?

## Slide 5: Before the test
We have a standard test plan
  Indeed, in the prototype phase and possibly also during the production, different strategies can be adopted depending on the type and features of magnet
  Meeting(s) to define the test plan
    Should be like a menu, with priorities associated to each case
    The test responsible carries out the day-by-day optimization
    Temporal sequence is important since interruptions may happen due to different causes (test station, limitations of the magnet, etc)
    Test plan should be stored in EDMS

## Slide 6: During the test
Experience shows that having a person in situ (in the place where the test is taking place) is useful, especially for the first tests
  Helps the keep a strong link between CERN and the Labs
  On the other hand, should we always have somebody from the manufacturing lab on the test site ? To be discussed
It is findamental to have a daily report to an ad hoc distribution list
  Including project engineer, key persons working on the magnet, and few persons at the management level
  Even if nothing happens it is good to know

## Slide 7: During the test
The following major decisions should be agreed with CERN
  Warming up
  Test that might endanger the magnet (high MIITs)
  Change of test plan or of the sequence
Regular follow up meetings with the project engineer
  In these meetings one does not need to have all the collaboration
One or more WP meetings with the presentation and discussion of the results
  With slides available to all collaborations

## Slide 8: Data exchange: mechanical measurements
Mechanical measurements are extremely important for understanding magnet performance
  They are also the most difficult and fragile
  Cross-check between systems is important
Post-processing done by the team in charge of the equipment
Diffusion of plots and Xcel tables during the test is necessary
  Very efficient system at CERN: mechanical data available after each quench
  Do we store numerical values in CERN DB ?

## Slide 9: Data exchange: training
Training data (communicated daily with Xcel table, plus plot) and stored in CERN DB
  Time: Date, hour (sometimes forgotten but very important)
  Temperature, Current, Voltage
  Localization
What to do with the signals (voltages, current, etc during a quench)?
  Have a copy in a CERN DB (ideal, but is it possible?)
  Store locally in the lab and make them available in case of need (more realistic)

## Slide 10: Data exchange: magnetic measurements
We should have the post-processed data distributed rapidly during the test (not after)
  File with time, current, multipoles
  Give priority to the most important measurements!
    Machine cycle, w-c correlation, stairsteps first
    Ramp rate has much lower priority
As for mechanical measurements and for training, magnetic measurements extraction from raw signals is the task of the responsible of the measuring system
  But a rapid distribution to the collaboration allow to detect if there are problems, and if some measurements should be repeated
Also in this case, store the post-processed data in a CERN DB

## Slide 11: After the test
Test report to be written
  Level of detail to be clarified – it can go from a few pages to 20-30
    Equilibrium between completeness and too much paper
Better an incomplete version available soon, with « in work » status, or final version much later?
  I would prefer the first one