'hit-pattern'
hit pattern: bit pattern that tells which layers are hit
track
*
*
*
*
*
*
hit pattern: 0 1 1 0 1 1 1
- can be constructed from LHCbIDs
  - extract subdetector and 'layer' from LHCbID
  - only input from geometry: number of bits == number of layers (hardcoded)
- my main purpose: select overlap tracks for alignment trigger
  - but can also be used for ghost rejection

---
LHCbLernel/Kernel/HitPattern
- new class in LHCb kernel, uses 'std::bitset' as bit patterns
  - constucted from std::vector<LHCbID>
  - contains hit patterns for all tracking detectors
  - does not know anything about real geometry, besides the number of layers
- example for VELO
  - separate R and phi → can count clusters
  - separate A side and C-side → can count overlaps
  - 21 layers + 2 pile uplayers
- other tracking detectors
  - TT: 1 pattern with 4 bits
  - IT: 4 patterns (top,bottom,A-side,C-side) with 12 bits
  - OT: 4 patterns (Q0...Q3) with 12 bits (e.g. only one bit per double layer)
  - MUON: 1 pattern of 5 bits
- besides the usual logical operations, std::bitset also has a 'count' function
std::bitset<23> m_velo[4]

---
overlap regions
example: counting the number of overlap stations in the velo:
N = (( m_velo[VeloRA] | m_velo[VeloPhiA] ) &
     ( m_velo[VeloRC] | m_velo[VeloPhiC] )).count() ;
  - about 1% of long tracks has overlap in >=5 velo stations
  - about 1% of long tracks goes through 2 boxes in at least one IT station
  - about 10% of long tracks goes through OT and IT in at least one station

---
holes
hit pattern also useful for identifying 'holes' in the track
0001101111010
- could be useful for track selection
- note: not as reliable as a real 'ExpectedHits' tool
  - hit pattern doesn't know about real holes in detector
  - cannot identify missing hits at begin or end of segment
  - e.g. not very usefull if you want to find out if track is secondary or from V0
- best of both: fill hit 'expected' pattern from ExpectedHitTool (to be done)
holes

---
holes and chisquare
- large correlation between track chisquare and missing hits
  - hypothesis: tracks with holes have high probability to be ghosts

---
cluster = R and phi hit in same station
but then … also large correlation between number of VELO hits and chisquare