## Slide 2: MD planning 2016 LIU-PSB meeting 22/3/16
E. Benedetto
With input from: S. Albright; M. A. Angoletta; H. Bartosik; A. Blas; M. Cieslak-Kowalska; G.P. Di Giovanni, A. Findlay; V. Forte, M. Fraser, G. Guidoboni, M. Jaussi, B. Mikulec, J. Molendijk, Y. Papaphilippou, G. Rumolo, F. Schmidt, G. Sterbini, R. Tomas, A. Valdivieso.

## Slide 3: Major questions LIU
Can we produce 2.8 eVs longitudinal emittance beams, within 220 ns, and transfer them to the PS?
  Longitudinal emittance blow-up
  Risetime recombination kickers
  (PS injection&capture)
Brightness curve
  Optimization, Measurements and Code benchmark
What is the effect of multipoles on beams (emittance, tails, losses)?
  Building PSB linear & non-linear model
Losses control and minimization
Beam instrumentation and Hardware in view of LIU

## Slide 4: Longitudinal Dynamics / LLRF (1/2)
Longitudinal Blow-Up Studies (8 days):
  Testing new features for blow-up
  Investigating blow-up reliability
  Study of maximum blow-up possible with high and low intensity beams
Blow-up to 2.8eVs (220ns bunch length), of highest priority for LIU
 to ease Space-Charge requirements @ injection and meet LIU/HL-LHC parameters
  Supported by simulation and measurements (by Simon)
  Hollow-bunches
* Quoting Alan, “Good starting point” of the RF team requests
180ns, 1.8eVs reached last year

## Slide 5: Longitudinal Dynamics / LLRF (2/2)
Finemet Reliability Run Studies (8 days, start in Jun):
  Recommission R0 beam control with ferrite cavities,
  Recommission Finemet cavity to replace C02 &/or C04,
  Set-up Finemet cavity as C04 replacement for a reliability run on R4 of the ISOLDE beams.
Alternative Phase Pick-up Studies (4 days, any time May to Sep):
  Investigate if the operational phase pick-up in 14L4 can be replaced by the phase pick-up in 8L1 for all 4 rings.
Measuring Relative Phase Between C02 - C04 (4 days, any time May to Sep):
  Investigate methods of measuring the relative phase between the C02 & C04 cavities.
Development & Upgrade Of Low-Level (5 x 4h, in Apr and May):
Transverse Feedback (10 x 4h in May-Jun):
  Test of the new digital processing @ 160 MeV and @1.4GeV
* Quoting Alan, “Good starting point” of the RF team requests

## Slide 6: Transverse dynamics & LIU beam brightness
Brightness Curve Optimization
  Assess 2016 performance.
  Coherent settings among the different rings
Measurements for code benchmark & validation simulated curve with L4
  Emittance as a function of injected parameters (WP, position/angle (*), KWS slope, L2 current), parametric scans
(*) needs understanding of the fluctuations @ the injection PUs

## Slide 7: Transverse Beam dynamics (1/2)
Effect of multipoles on beams & building PSB optics model
  Tune scans for loss-maps
  LOCO studies
  Non-linear chromaticity and detuning with amplitude
  Effect of the half-integer and of the integer on beam
Turn-by-turn beam position measurements
  BTMS commissioning
  AC dipole excitation or Qmeter kicker
  Characterization of the machine, tune ripple, instability @ 160 Mev, Qx=0.3,… (for full resonance driving terms need full BTMS, i.e. all the PUs)

## Slide 8: Transverse Beam dynamics (2/2)
Tail repopulation MD
  Shaved and large emittance (i.e. scraped) beams
  Diffusion coefficients, validation pyOrbit
Instability at C378 (…that’s about 160 MeV!!!):
  As a function of bunch intensity, bunch length, chromaticity
  Record intra-bunch motion with TFB PickUp
  Look at risetime with Qmeter PickUp
  In view of new simulations with pyHeadTail (+impedance model from C. Zannini)

## Slide 9: Transfer to the PS (1/2)
Measuring recombination kickers rise time:
  Limitations in bunch length transfer (is 220ns possible?)
  Short bunches (~10ns) to probe kicker function:
    Produced by desynchronizing KFA.14, longitudinal shaving or resonance-driven bunch shortening
    Asses resolution of BPM, BTVs in the line for small intensities
    Profit also of PS instrumentation (BPM, BLM, wideband PU)
  Nominal bunch & transverse tomography &SEM grids to reconstruct kicker waveform
  Long bunches (220ns, low Dp/p), measure in PS & TLine
  Inject & dump at 50 MeV
    Measure risetime using microbunches from the linac at 200 MHz
    Assess feasibility

## Slide 10: Transfer to the PS (2/2)
160 MeV extract and dump:
  Can we use it for L4 connection commissioning start-up?
  Assess feasibility
  Check optics @ low-energy
Optics changes in the BTM line:
  New optics by J. Abelleira's (seems promising also for current extraction @1.4GeV)
  Check losses and emittance measurement systematically
BTY optics model validation:
  Kick response measurements

## Slide 11: BI related MDs
BTMS commissioning
  Fundamental as the plan is to have the new electronics already in 2017
MDs to understand fluctuations in the injection PUs
  Optics degeneracy
  Impact on injection
Energy and energy spread at injection
  Time of Flight measurement in the injection line
  How to optimize debuncher settings
Emittance measurements
  Wire scanners along the cycle
  Extraction SEM grids (comparison with WS & review optics model)
  Emittance difference evaluation with different lab calibration curves and with online calibration

## Slide 12: MD page for MD requests

## Slide 13: Conclusions
Preliminary plan
Already a dense program!
Most of the MDs:
  rely on the collaboration between many groups and different experts.
  will have a positive impact on the present machine/ LIU will profit of optimization on the present machine
Please submit your requests to the official web-page:
      https://md-coord.web.cern.ch/app/#/