## Slide 2: PS Intensity Limitations for LHC-type Beams
LIU Beam Parameter Working Group
08/04/2016
H. Damerau
Many thanks for input and discussions to:
S. Hancock, G. Sterbini, L. Ventura and many more

## Slide 3
Overview
Introduction
  Objectives: 2015 LIU baseline and HL-LHC request
Transverse
  Space charge
  Large longitudinal emittance and low chromaticity
  Transition crossing
Longitudinal
  Direct and 1-turn delay feedbacks
  Coupled-bunch feedback
  PS-SPS transfer with both 40 MHz cavities
Summary

## Slide 4
Introduction
 | Parameter | 
Injection | Intensity per bunch | 2.8 1012 ppb (12  2.3 1011)
 | Transverse emittances | 1.6 mm
 | Longitudinal emittance | 3.0 eVs
 | Bunch length | 205 ns
PS | Beam loss | 5%
 | Transverse emittance growth | 5%
 | Controlled longitudinal blow-up | ~50%
 | Tolerable space charge tune shift, DQy | -0.31
Ejection | Intensity per bunch | 2.2 1011 ppb
 | Transverse emittances | 1.7 mm
 | Longitudinal emittance | 0.35
 | Bunch length | 4 ns
  Objectives: LIU baseline, pre-2016

## Slide 5
Introduction
 | Parameter |  | achieved
Injection | Intensity per bunch (total: 2 1013 ppp) | 3.3 1012 ppb (12  2.7 1011) | 
 | Transverse emittances | 1.8 mm | 
 | Longitudinal emittance | 3.0 eVs | 
 | Bunch length | 205 ns | 
PS | Beam loss | 5% | 
 | Transverse emittance growth | 5% | 
 | Controlled longitudinal blow-up | ~50% | 
 | Tolerable space charge tune shift, DQy | -0.31 | 
Ejection | Intensity per bunch | 2.6 1011 ppb | 1.7 1011 ppb
 | Transverse emittances | 1.9 mm | 2.2 mm
 | Longitudinal emittance | 0.35 | 
 | Bunch length | 4 ns | 
  Objectives: HL-LHC request

## Slide 6
Injection flat bottom
Space charge
Headtail instability
Flat top
Longitudinal CBI
Electron cloud
Transverse instabilities
Intensity limiting effects in the PS
Acceleration/Bunch splittings
Longitudinal CBI
Transient beam loading
Transition crossing
S. Gilardoni

## Slide 7
Transverse

## Slide 8
Limitation | Mitigation
Space charge | Upgrade of injection energy 1.4 to 2 GeV Reduce space charge by ~1.6 Increase bunch length at flat-bottom Blow-up studies in PSB in 2015
Head-tail instability | Use coupling or transverse damper Past mitigation coupling Upgrade transverse damper Damper operation with present power
Transition crossing | To be defined Beam studies in 2016 (started in 2015)
Electron cloud at flat-top | Keep bunches long enough Present mitigation Transverse damper against oscillation Mitigation/delay shown with beam in 2013
Overview – Transverse
Main brightness gain expected from injection energy increase
Coherent instabilities handled by transverse damper

## Slide 9
Space charge
Maximum acceptable tune shift based of 0.31 based on measurements
Allow larger loss budget (only at 2 GeV) for smaller emittances?
G. Sterbini, R. Wasef
With integer tune Q6 vertical tune spread limited to 0.25 by 8qv=50 res.
Compromise of losses versus transverse blow-up
5% emittance budget
5% loss budget
Lower chromaticity
Reduces tune spread
Requires transverse damper
Improve wire-scanner data analysis

## Slide 10
Space charge, large el and small chromaticity
Reaching the HL-LHC request requires large longitudinal emittance (3.0 eVs) and longest possible bunches at flat-bottom ~205 ns
No margin, all scalings must be correct
Higher brightness only available after LS2
Studies:
Change integer working point to Q5/7
Resonance compensation using skew sextupoles (reduce integer resonance)
Vertical dispersion by introducing coupling
Hollow bunches, double harmonic RF (h = 7+14) or lower RF voltage at flat-bottom
Possible issues:
Precision of wire scanner measurement to qualify emittances
Measurement of transverse blow-up during the cycle  BGI
Control of emittance blow-up  tune control during ramp

## Slide 11
Controlled longitudinal emittance blow-up
Reduce space charge at PS flat-bottom
  Large longitudinal emittance of 3.0 eVs needed for LIU
Extensive beam tests of controlled blow-up in PSB
Maximum emittance of only el = 1.8 eVs achieved so far
Close to textbook water-bag distribution: constant phase space density
Studies to continue in 2016 to produce up to 3.0 eVs
Critical for PS space charge
S. Hancock, A. Oeftiger

## Slide 12
Large el and small chromaticity
Promising results from 2015
Horizontal emittance
Vertical emittance
Nb at ejection [1011 ppb]
eV [1011 ppb]
eH [1011 ppb]
~15% reduction of horizontal emittance
Present transverse feedback stabilizes beam with zero chromaticity at 2.5 GeV
Upgrade of power amplifiers required to maintain efficiency in damping injection oscillations
Nb at ejection [1011 ppb]
G. Sterbini

## Slide 13
Beam loss at transition crossing
Losses at transition crossing with LHC-type beams for el > 1 eVs
  Longitudinal or transverse?
2016: Modify triple splitting to h = 7  21 re-bucketing
Losses only at intensities well beyond LIU needs with single-bunch
  Check other RF harmonics than h = 21 and possibly more bunches
Studies to continue in 2016
t [ns]
Pure h = 7
Pure h = 21
60 ms
Nb > 2.0 · 1012 ppb in el = 1.2 eVs
2.7 · 1012 ppp

## Slide 14
Transverse MD priorities in 2016
Priorities with protons:
Low-chromaticity/low-coupling along complete cycle
    Commission new transverse damper LLRF
Confirm rise-time of recombination kickers with beam
Working point studies
  Move integer tunes to Q7/7, Q7/5 and Q5/7
  Detailed scan of fractional tune at Q6/6: losses  emittance blow-up
  Possibilities to reduce integer stop band width
Improve analysis of wire scanner data
Space charge studies
  Transverse quadrupolar oscillations (excitation, detection)
Tests with 80b at extraction
  Beyond LIU baseline

## Slide 15
Longitudinal

## Slide 16
Overview – Longitudinal
Limitation | Mitigation
Longitudinal beam stability Coupled-bunch oscillations | Reduced impedances of all RF cavities Improved wide-band feedback 10 MHz Replaced 1-turn delay feedbacks 10 MHz New 1-turn delay feedbacks for 20, 40 and 80 MHz cavities Dedicated coupled-bunch feedback Wide-band Finemet longitudinal kicker Increased longitudinal emittance PS-SPS transfer with both 40 MHz cav.
Bunch-to-bunch equalization | 1-turn delay feedbacks
Reduce impedance sources and mitigate consequences

## Slide 17
- Fast wide-band feedback
around amplifier (internal)
 Gain limited by delay
Main 10 MHz RF system
  10 + 1 ferrite loaded cavities, tunable from 2.8…10 MHz
Drive
+
FB ret.
- 1-turn delay feedback
 High gain at n  frev
+
1-turn delay feedback
Beam
Final amp.
Maximize loop gain of direct wideband feedback
Add 1-turn delay feedback
D. Perrelet

## Slide 18
Gain [dB]
Frequency [MHz]
Wide-band feedback of 10 MHz cavities
  Power amplifier upgrade: New working point and grid resonator
    Increased gain of direct RF feedback around amplifier
Upgraded prototype: 3 MHz
Standard amplifier: 3 MHz
Gain [dB]
Frequency [MHz]
Prototype amplifier
  Impedance reduction by factor of ~2 (at 10 MHz  h = 21)
  First cavity being upgraded during YETS2015/16
  Ready for beam tests on one cavity in 2016
Full implementation during (E)YETS and LS2
~24 dB
~25 dB
G. Favia

## Slide 19
Gain [dB]
Frequency [MHz]
Wide-band feedback of 10 MHz cavities
  Power amplifier upgrade: New working point and grid resonator
    Increased gain of direct RF feedback around amplifier
Upgraded prototype: 10 MHz
Standard amplifier: 10 MHz
Prototype amplifier
  Impedance reduction by factor of ~2 (at 10 MHz  h = 21)
  First cavity being upgraded during YETS2015/16
  Ready for beam tests on one cavity in 2016
Full implementation during (E)YETS and LS2
Gain [dB]
Frequency [MHz]
~24 dB
~30 dB
G. Favia

## Slide 20
1-turn delay feedbacks 10 MHz (2014)
  Further reduce impedance at harmonics of frev (comb filter feedback)
    Transient beam loading fully suppressed at 1.3 · 1011 ppb
Digital 1-turn delay feedback for all 11 main accelerating cavities used for operational beams in 2015
72 bunches, Feedbacks off
72 bunches, feedbacks on
2 ms
2 ms
D. Perrelet

## Slide 21
1-turn delay feedbacks 10 MHz (2014)
  Further reduce impedance at harmonics of frev (comb filter feedback)
    Transient beam loading fully suppressed at 1.3 · 1011 ppb
Excellent longitudinal beam quality
Study splitting with lower emittance to scale to higher intensity
New 1-turn delay feedbacks on 20 MHz, 40 MHz and 80 MHz cavities in 2016/17
3 ms

## Slide 22
Coupled-bunch instability
Simulations with
10 MHz cavities + Finemet cavity impedance model
Measured mode spectra
  Same mode pattern and strength reproducibly observed (2013 data)
  21 bunch case simulation, main impedance: 10 MHz cavities
L. Ventura
Same mode number n = 2 predicted as observed
Similar growth rate

## Slide 23
Coupled-bunch instability simulations
Simulations with MuSiC code
Impedance model with 10 MHz RF cavities, little effect of other cavities
1.3 · 1011 ppb (h = 84), 18 bunches, 15 GeV
2.6 · 1011 ppb (h = 84), 18 bunches, 15 GeV
1.3 · 1011 ppb (h = 84), 18 bunches, 26 GeV
2.6 · 1011 ppb (h = 84), 18 bunches, 26 GeV
The coupled-bunch feedback is designed to damp all cases
On paper it works
1/t = 4.0 s-1
1/t = 5.7 s-1
1/t = 3.4 s-1
1/t = 5.3 s-1
L. Ventura
n = 1
n = 1
n = 1
n = 1

## Slide 24
Coupled-bunch feedback
-3 dB
6
Splitter + amp.
Coupled-bunch feedback
Comb. + att.
Beam-loading compensation
Wall current monitor
fclk = 256 frev
Cavity return sum
Suppress synchrotron frequency side-bands at n · frev
Two feedbacks: 1. Beam  Finemet cavity, 2. Cavity return  cavity
Frequency domain approach
Prototype Finemet cavity

## Slide 25
Coupled-bunch feedback
 | Finemet cavity | 
2014 | 1/6 gaps | Beam-loading reduction feedbacks for Finemet cavity
2015 | 4/6 gaps | Excitation of coupled-bunch oscillations 1st damping on single harmonic Function prototype system with 10 processing chains
2016 | 5/6 gaps | Explore beam parameters with feedback Define voltage requirement for final cavity
Functional prototype working at end of 2015:
  Covering all modes simultaneously
  2/3 of the voltage capability of final system
Expected to deliver close to full performance of operational system

## Slide 26
Benefit of coupled-bunch feedback
  Arrival on the flat-top and voltage reduction (splitting disabled)
Feedback off
Feedback on
  Even with feedback not fully stable

## Slide 27
  Coupled-bunch instability with wide mode spectrum
Bunches on flat-top, feedback off
Last turn, feedback off
Mode spectrum, feedback off
Damping of all 20 modes on the flat-top

## Slide 28
Damping of all 20 modes on the flat-top
Bunches on flat-top, feedback on
Last turn, feedback on
  Coupled-bunch instability with many modes
Reached 1.7 · 1011 ppb with good longitudinal parameters
Full evaluation of prototype with beam during 2016 run
Critical to reach LIU baseline
Mode spectrum, feedback on

## Slide 29
What to expect at higher intensity?
  Dipole oscillations seem well stabilized
  High order modes of instability?
  MD priority: Evaluation of performance during 2016 run
    Maximum intensity with coupled-bunch feedback
    When in the cycle does the instability develops?
    Unstable modes (dipolar, quadrupolar, etc.)?
Feedback off
Feedback on
Quadrupolar coupled-bunch?
C2595
C2595

## Slide 30
Large longitudinal emittance at transfer
H. Timko
  Several attempts to complete measurements with larger el in 2015
    Cavities not available due to various technical issues
  Complete measurements in 2016
  Passive stabilization: increased longitudinal emittance
  Use both 2  40 MHz cavities for bunch rotation
  BUT: 0.4 eVs assumption in SPS leaves little/no margin for PS
Bunch length, 4s [ns]
Transmission, [norm.]

## Slide 31
Longitudinal MD priorities in 2016
Priorities with protons:
Validate 10 MHz direct feedback upgrade on C10-11
Explore performance reach of coupled-bunch feedback
Transfer of large longitudinal emittance from PSB (h = 1+2)
Test 1-turn delay feedbacks on high-frequency cavities
PS-SPS transmission with both 40 MHz cavities
Conceptual tests preparing beam control upgrade

## Slide 32
Summary
2.6…2.7·1011 ppb with 25 ns spacing for LHC is well beyond present achievements, transversely and longitudinally
  May observe new limitations
No direct limitation built into the upgrades
Need input from beam studies in 2016 to
  conclude on potential beam brightness before and after LS2
  explore longitudinal limitations with coupled-bunch feedback
Major step in brightness only after upgrades during LS2
Need commission and study time after LS2

## Slide 33
THANK YOU FOR YOUR ATTENTION!