## Slide 1
Field Control of TL Switching Dipole
Expected issues: - history-dependence (10-3 at low field)
- Compounded by asymmetric field profile  complex hysteresis and eddy currents patterns - More difficult to measure and simulate
Main dipole unit test supercycle (different combinations of energy levels in succession)
Variability due to cycling

## Slide 2
Possible control strategies
Feed-forward current control: test on the bench, then apply a I taken in real-time from a table:
I = f (Ecurrent cycle, Elast cycle ) (4 combinations)
I = f (Ecurrent cycle, Elast cycle , Esecond-to.last cycle ) (16 combinations)
Possible problems: complex, new energy levels require re-measurement
Field feedback control
Hall probe  FGC3 controller (as in HIE ISOLDE bendings): at best few 10-4, must be tested
NMR teslameter  Java application (as in ISOLDE HRS): too slow
NMR teslameter  FGC3 controller: planned, but does not exist yet
Full fledged B-train  FGC3 controller: safest solution, subset of the ring system, requires new PCB coils + one field marker
2 X 1 mm thick PCB integral coils
magnet gap