## Slide 1: Update on the FASTION code development, and new results
L. Mether, G. Rumolo
CLIC Beam Physics meeting March 31st 2016

## Slide 2: Outline
The fast beam-ion instability
Simulating the fast beam-ion instability
Code development & new results
  FASTION development and challenges
  CLIC Main Linac revisited
  Fast beam-ion instability with PyECLOUD and PyHEADTAIL
Summary & outlook

## Slide 3: Fast beam-ion instability
Gas molecules ionized by beam
Beam electrons accelerated by ions
Coupled electron-ion oscillations
Positive ions oscillate in beam field
Instability
In synchrotrons without clearing gap, ion density builds up over several turns
  Conventional ion instability
For bunch train followed by gap, ions build up only during one train passage
  Fast beam-ion instability (FBII)

## Slide 4: Fast beam-ion instability
Ion density increases for every bunch passage – effect stronger at tail of train
Ions transfer information on offsets from bunch to bunch – head and tail of train coupled
Over time can lead to multi-bunch instability, tune shift, emittance growth

## Slide 5: FBII theory
Treatment based on linear approximation of Bassetti-Erskine formula
  Velocity kick for ion with mass number A
    Nb = bunch intensity, σx,y = rms transverse beam sizes, rp = classical proton radius
Fast beam-ion instability. I. Linear theory and simulations
Raubenheimer et al. Phys. Rev. E 52, 5, 5487

## Slide 6: Ion trapping condition
For a bunched beam, ions will drift between bunch passages
  Using the stability condition of a linear beam trajectory, |Tr(M)| < 2:
    Ion motion is stable if |2 - k*Tb| < 2  kTb < 4
      Tb = bunch spacing, k = kick
    Otherwise oscillation amplitude grows monotonically
This leads to a trapping condition for the ion mass number
  Trapping condition must be fulfilled in both horizontal and vertical plane
    For electron machines, typically σy << σx  Atrap = Atrap,y

## Slide 7: FBII theory
Treatment based on linear approximation of Bassetti-Erskine formula
  For A > Atrap, estimated instability rise time
    Tb = bunch spacing, nb = nr of bunches, P = pressure, ωβ = betatron frequency
  High pressure, long train, high intensity, small beam  short rise time
Fast beam-ion instability. I. Linear theory and simulations
Raubenheimer et al. Phys. Rev. E 52, 5, 5487

## Slide 8: Observations
Observed in several machines under vacuum degradation
Measurements at CESR-TA with injected gas (Dec. 2013, Apr 2014)
  Varying ion species, pressure, bunch charge, train structure, feedback etc.
A. Chatterjee et al. Phys. Rev. ST Accel. Beams 18 (2015) 6, 064402
Feedback on
Feedback on

## Slide 9: Numerical FBII studies
Aim to estimate the effect of parameters on instability rise-time
  Beam parameters: intensity, emittance, etc.
  Vacuum pressure and composition
Simulation with multi-bunch macro-particle (PIC) tracking code
CERN simulation tool: FASTION
  Self-consistent strong-strong, 2D
  Developed by G. Rumolo
  Written in C
  Based on HEADTAIL for electron cloud
  Used e.g. for CLIC linear structures, CESR-TA
  Currently working on adapting to future synchrotrons

## Slide 10: Simulation outline
The machine lattice is divided into a number of interaction points (IP)
  An electron bunch train is tracked through the lattice
  In every IP, the beam-ion interaction is simulated
IP

## Slide 11: Simulation outline
In every interaction point, the beam is passed bunch by bunch
Calculate e-fields
Generate ions
Give velocity kick
Introduce bunch

## Slide 12: Simulation outline
Transport bunch
Transport bunch
In every interaction point, the beam is passed bunch by bunch
Calculate e-fields
Generate ions
Give velocity kick
Introduce bunch
Electric fields of ions and electrons calculated separately on same grid
Represent ions generated between two IP’s
Ion distribution σion = σbeam
Generate ions
Introduce bunch
Give velocity kick
Drift ions
Calculate e-fields
Ion densities given by partial pressures and ionization x-sections, or field ionization
Velocity kicks applied according to e-field of opposite particles (no self space charge)

## Slide 13: Simulation outline
In every interaction point, the beam is passed bunch by bunch
Calculate e-fields
Generate ions
Give velocity kick
Drift ions
Introduce bunch
Transport bunch
Electric fields of ions and electrons calculated separately on same grid
Velocity kicks applied according to e-field of opposite particles (no self space charge)
Ion densities given by partial pressures and ionization x-sections, or field ionization
Represent ions generated between two IP’s
Ion distribution σion = σbeam

## Slide 14: FASTION development
Main objective: modify code to be practically applicable to rings
  Implement required additions and modifications
    Full twiss matrices, radiation damping, synchrotron motion, feedback…
Main challenge: run-time performance
  Synchrotron radiation damping can help prevent instability
  want to be able to simulate at least over a damping time, τd ≈ 1400 turns
    Test case: 1 turn, 27 min  26 days for 1400 turns (on fast desktop)
  After basic code optimization
    Test case: 1 turn, 16 min  15 days
    Still too long for systematic scans
  Solutions?
    Parallelization
    Compromise on number of IP’s

## Slide 15: Beam resolution
Unexpected challenge: resolution
  Ion trajectories can extend far beyond beam
    Linear approximation only good if A >> Atrap, but need to scan all vacuum components
Sample ion trajectories, H2O
CLIC Damping ring

## Slide 16: Beyond linear approximation
Linear approximation is only good in a small region around centre of beam

## Slide 17: Beyond linear approximation
Linear approximation is only good in a small region around centre of beam

## Slide 18: Beyond linear approximation
Stability condition and ion trapping
Trajectories for ion of mass A, during the passage of one CLIC-like bunch train
  x0 = 0.7σx, y0 = 0.7σy
Beyond trapping, kTb > 4
Weak trapping, kTb = 2.5
Strong trapping, kTb = 0.56

## Slide 19: Beyond linear approximation
Stability condition and ion trapping
Trajectories for ion of mass A, during the passage of one CLIC-like bunch train
  x0 = 1.5σx, y0 = 1.5σy
Beyond trapping, kTb > 4
Weak trapping, kTb = 2.5
Strong trapping, kTb = 0.56

## Slide 20: Beam resolution
Unexpected challenge: resolution
  Ion trajectories can extend far beyond beam
    Linear approximation only good if A >> Atrap, but need to scan all vacuum components
  Adapting grid to expanding ion distribution to track ions
   poor resolution, even for very large grids  impossibly long run-time for large grids
Sample ion trajectories, H2O
CLIC Damping ring
CLIC Damping ring

## Slide 21: Two-grid method
Solution:
  Keep inner grid around beam fixed
  Use second, coarser grid to track ions outside
    Treat inner grid as usual, but add correction to beam from outer grid
  Performance
    1 turn, 15 min  14 days for 1400 turns
    With much improved resolution
Two-grid

## Slide 22: CLIC Main Linac revisited
FBII in linear CLIC structures has been studied with FASTION in the past
  Revisited with improved simulation resolution
  Especially for Main Linac, past results did not agree well with theoretical expectations:
    Instabilities, and ion trapping even for A << Atrap
    Instability rise time in horizontal < vertical
    e.g. CLIC-Note-930, 2011
CLIC Main Linac (2012) |  |  | 
Length [km] | 22 | Normalized emittances [nm] | 660, 10
Injection energy [GeV] | 9 | Bunch population, Nb | 4 x 109
Collision energy [GeV] | 1500 | Bunches per train, nb | 312
 |  | Bunch spacing , Τb [ns] | 0.5

## Slide 23: Beam size and ion trapping
Due to acceleration, beam size decreases along linac
  Atrap increases along linac
  Due to small vertical beam size, ions are not trapped along most of linac
CO2
CO2
Kr
Kr
Atrap
Atrap

## Slide 24: New results
Simulation scan with single vacuum species, with varying A and P

## Slide 25: New results
Simulation scan with single vacuum species, with varying A and P
New results agree well with theory
  Constraints on vacuum less stringent than previously, due to limited trapping

## Slide 26: FBII with PyECLOUD and PyHEADTAIL
Several CERN beam dynamics codes re-designed in the past few years
  Aim to make codes more user friendly, maintainable and flexible
  Electron cloud build-up: ECLOUD  PyECLOUD
  Collective effects: HEADTAIL  PyHEADTAIL
Decision to incorporate fast beam-ion instability simulations into framework of PyECLOUD and PyHEADTAIL codes
coupled

## Slide 27: PyECLOUD
Simulation code for electron cloud formation
  Developed and maintained at CERN since 2011 by G. Iadarola
  Following the legacy of the ECLOUD code (F. Zimmermann et al., 1997…)
  2D macro-particle code
  Written in Python with Fortran (f2py) and C (CYTHON) extensions
Features
  Gas ionization
  Boris algorithm for moving particles in magnetic fields
  PIC module with multiple solver methods for arbitrarily shaped chambers
E-cloud pinch: Dipole
E-cloud pinch: Quadrupole
G. Iadarola

## Slide 28: PyHEADTAIL
Simulation code for collective effects: impedance, e-cloud instability, etc.
  Developed and maintained at CERN since 2014 by H. Bartosik, K. Li et al.
  Based on the HEADTAIL code (G. Rumolo et al., 2000)
  2D macro-particle code
  Written in Python with C (CYTHON) extensions
Features
  RF systems and synchrotron motion
  Chromaticity
  Transverse feedback
github.com/PyCOMPLETE
  PyHEADTAIL
  PyECLOUD
  PyPIC
Kevin Li
Wakefield
Wake kick

## Slide 29: FBII with PyECLOUD and PyHEADTAIL
For e-cloud studies: HEADTAIL  PyECLOUD + PyHEADTAIL
  Since FASTION based on HEADTAIL for e-cloud, decided to follow suite
Calculate e-fields
Generate ions
Give velocity kick
Drift ions
Introduce bunch
PyECLOUD
PyHEADTAIL
PyHEADTAIL
Transport bunch

## Slide 30: Motivation
Facilitate continued maintenance
Share workload of common developments, e.g. parallelization
Benefit from features already implemented in PyECLOUD/PyHEADTAIL
  Separate build-up and instability simulations for multi-turn ion trapping
  Ion self space charge
  E-field boundary
  Synchrotron motion
  Transverse feedback
Trajectories for H2O ion during passage of CLIC-like bunch train
B-field off
Dipole
Quadrupole
  Magnetic fields
  Bunch slices

## Slide 31: Progress
Generalization to arbitrary charge and mass in PyECLOUD + PyHEADTAIL
Implementation of multi-bunch in PyHEADTAIL
Extension of PyECLOUD gas ionization routines
  Multiple species, field ionization
Implementation of grid methods
  Rectangular (non-square) grid cells (for flat electron beams)
  Two-grid method
Testing
  Compare with FASTION results
Parallelization?
In progress
To do

## Slide 32: Summary & conclusions
The FBII can affect electron machines with clearing gaps
  Usually not a problem in current machines with nominal vacuum
  May be important for future machines: CLIC, FCC-ee, LHeC, new light sources
  Simulations to study effect of beam and vacuum parameters on instability
FASTION studies
  Code optimized, and modified for improved resolution and reliability
  Ready for new CLIC baseline parameters
    In good shape for simulating linear structures
    Allows first studies for damping rings, but still quite heavy for systematic scans
FASTION  PyECLOUD + PyHEADTAIL
  Add maintainability and flexibility, share workload of common development
  Introduces many new features and possibilities for studies
  Work in progress

## Slide 33
Thank you!

## Slide 34: Grid convergence scans: Main Linac
Amplitude of vertical bunch train oscillation
Grid center shifted 0.5 cells

## Slide 35: Dual-grid solver
Sample ion trajectories