## Slide 1: Performance reach Update
G. Arduini, R. Tomas for WP2
9th HL-LHC Technical Coordination Committee – 23/06/2016

## Slide 2: Impact of the changes from previous baseline
Triplet beam stay clear reduced taking into account beam screen/cold bore tolerances
Increase of the length of the triplet due to reduction of the gradient form 140 T/m to 133 T/m
Reduction of the coil aperture of Q4 from 90 to 70 mm (MQYY  MQY). Q5 as per baseline. Expected limitations:
  Min b* = 20 cm (round) – limited by triplet
  Min b* ~ 40/15 cm (flat) – limited by Q4
Half crab cavities (2 per IP side/beam operated at nominal voltage of 3.4 MV each)

## Slide 3: Preliminary performance estimate
 | Crossing angle [mrad/s] | Lint [fb-1/y] | Max Pile-up | Max. pile-up density [ev./mm] | Opt. Fill length [h]
Nominal | 590 (12.5) | 260 | 140 | 1.2 | 8.2
New Round | 510 (12.5) | 240 | 140 | 1.2 (lev.)* | 7.5
New flat | 420 (14.5) | 240 | 140 | 1.1 | 7.2
Performance loss of the order of 10%
Nominal performance can be recovered reducing crossing angle (BBLR compensation) and/or pushing flat optics (limited by Q4 aperture)
*levelling on pile-up density in addition to pile-up. Initially not foreseen.

## Slide 4: Preliminary performance estimate
 | Crossing angle [mrad/s] | Lint [fb-1/y] | Max Pile-up | Max. pile-up density [ev./mm] | Opt. Fill length [h]
Nominal | 590 (12.5) | 320 | 200 | 1.7 | 5.6
New Round | 510 (12.5) | 280 | 200 | 1.7 (lev.)* | 5.3
New flat | 420 (14.5) | 280 | 200 | 1.6 | 5.2
The loss is larger (of the order of 15%) for the ultimate performance for the same pile-up density as compared to nominal case
*levelling on pile-up density in addition to pile-up. Initially not foreseen