## Slide 1: EuroCirCol Status of block design mechanics
Clément Lorin
Maria Durante
Michel Segreti
CEA
Cern, 12 May 2016
ECC WP5 1st review

## Slide 2
  Two cables
    HF cable: Ф = 1.1 mm, 24 strands
      13.85 mm x 2 mm
    LF cable Ф = 0.7 mm, 37 strands
      13.85 mm x 1.25 mm
Reminder of the block magnet
Quantity | Value | Unit
Inom | 8470 | A
Bpeak | 16.56 | T
LL margin | 9.3 | %
Inductance diff. (2 ap) | 88.19 | mH/m
Stored energy (2 ap) | 3340 | kJ/m
Conductor area (2 ap) | 190* | cm²
Fx (per ½-coil) | 8817 | kN/m
Fy (per ½-coil) | -3703 | kN/m
Hotspot | 310 | K
*10800 tons

## Slide 3
  Single Aperture (SA) configuration: Фyoke = 800 -250 = 550 mm
Mechanical specifications
  Baseline :
  Investigation at 16.8 T central field
  (105% of nominal current)
  Mechanical structure must withstand 18 T
  Coil maximum stress
    @ 4.2 K: 200 MPa
    @ 300 K: 150 MPa

## Slide 4
  Single Aperture (SA) configuration: Фyoke = 550 mm [(800-250)]
  Investigation at 16.8 T central field (105% of nominal current)
  Mechanical structure must withstand 18 T
  Coil maximum stress
    @ 4.2 K: 200 MPa
    @ 300 K: 150 MPa
Mechanical specifications
Iron @ 4.2 K stress < 200 MPa in tension (brittle) ?
Material | E [GPa] |  | pr | (L4.3K-L293K)/L293K
 | 293 K | 4.3 K | 293K /4.3K | 293 K -> 4.3K
Coil | EX = 44 EY = 52 GXY = 21 | EX = 44 EY = 52 GXY = 21 | 0.3 | X = 3.36e-3 Y = 3.08e-3
StSt | 193 | 210 | 0.28 | 2.84e-3
Iron | 213 | 224 | 0.28 | 1.97e-3
Aluminum | 70 | 79 | 0.34 | 4.2e-3
Titanium | 130 | 130 | 0.3 | 1.74e-3
Nitronic 40 | 210 | 225 | 0.28 | 2.6e-3
Material | Rp 0.2 [MPa] | 
 | 293 K | 4.3 K
Al 7075 | 480 | 690
SS 316 LN | 286 | 930
NITRONIC 40 | 353 | 1240
MAGNETIL | 180 | 723
Ti 6Al 4V | 827 | 1654

## Slide 5
Comparison Roxie @ 16 T central field (Ansys + Cast3m)
Lorentz forces
Ansys Bp = 16.62 T
Al
Iron
Ti
CuAl
Steel
Roxie Bp = 16.45T

## Slide 6: Assembly steps

## Slide 7: Assembly steps
Pole Ti6Al4V

## Slide 8: Assembly steps
Pole Ti6Al4V
Windings Nb3Sn
Pad StSt

## Slide 9: Assembly steps
Pole Ti6Al4V
Windings Nb3Sn
Pad Iron
Pad StSt

## Slide 10: Assembly steps
Pole Ti6Al4V
Windings Nb3Sn
Pad Iron
Pad StSt
-> Coil pack

## Slide 11: Assembly steps
Yoke Iron
Shell Aluminium

## Slide 12: Assembly steps
Pole Ti6Al4V
Bobines Nb3Sn
Pad StSt
Pad + Yoke Iron
Shell Aluminium

## Slide 13: Magnet at ease

## Slide 14: Bladder inflation
Not simulated so far, estimated only

## Slide 15: Key insertion
σx

## Slide 16: Spring back
↓ Horizontal key: nominal + 150 µm
← Vertical key: nominal + 1050 µm
scale: -122 MPa to -37 MPa
σx

## Slide 17: Cool-down
Shell thickness: 50 mm
scale: -218 MPa to -56 MPa
σx

## Slide 18: Powering to 105% (16.8 T)
16.8 T
scale: -215 MPa to +50 MPa
σx

## Slide 19: Contact coil-pole at 105 % (16.8T)
scale: -57 MPa to +134 MPa
16.8 T
Contact: 2 MPa in the middle of the cable
σx

## Slide 20: Summary for windings + contact
Key (bladder tbc)
Cool-down
Powering 105%
Peak 218 MPa
Peak 215 MPa
Contact coil-pole 105%
Contact coil-pole 100%
scale: -57 MPa to +134 MPa
scale: -34 MPa to +132 MPa
σx
σx
σx

## Slide 21
Pole slit
Pole with slit
  218 MPa at cold
pole slit to make the pole flexible and avoid too high peak stress in the coil
Initial pole
  249 MPa at cold
Cool-down step: 4.2 K, 0 T
Cool-down step: 4.2 K, 0 T

## Slide 22
Cool-down
18 T
Key in
Mechanical structure (18 T)
17 MPa to 722 MPa
Material | Rp 0.2 [MPa] | 
 | 293 K | 4.3 K
Ti 6Al 4V | 827 | 1654
38 MPa to 1420 MPa
33 MPa to 643 MPa
von Mises stress

## Slide 23
Cool-down
18 T
Key in
Mechanical structure (18 T)
Material | Rp 0.2 [MPa] | 
 | 293 K | 4.3 K
Magnetil | 180 | 723
0 MPa to 368 MPa
0 MPa to 450 MPa
0 MPa to 494 MPa
Iron @ 4.2 K stress < 200 MPa in tension (brittle) ?

## Slide 24
Material | Rp 0.2 [MPa] | 
 | 293 K | 4.3 K
Magnetil | 180 | 723
Cool-down
18 T
Key in
Mechanical structure (18 T)
0 MPa to 284 MPa
0 MPa to 509 MPa
0 MPa to 542 MPa
Iron @ 4.2 K stress < 200 MPa in tension (brittle) « SSC », investigation on going at Cern

## Slide 25
Material | Rp 0.2 [MPa] | 
 | 293 K | 4.3 K
Al 7075 | 480 | 690
0 MPa to 189 MPa
0 MPa to 275 MPa
0 MPa to 301 MPa
Cool-down
18 T
Key in
Mechanical structure (18 T)

## Slide 26
Material | Rp 0.2 [MPa] | 
 | 293 K | 4.3 K
SS 316 LN | 286 | 930
NITRONIC 40 | 353 | 1240
Cool-down
18 T
Key in
Mechanical structure (18 T)
0 MPa to 700 MPa
0 MPa to 965 MPa
0 MPa to 1030 MPa
Key in

## Slide 27: Peak stress in the structure
Von Mises max [MPa] | Material | Key in | Cool-down | 105% power
Pole | Ti6Al4V | 722 | 1420 | 643
Pads | Iron | 368 | 450 | 494
Pads | SS 316 LN | 121 | 298 | 386
Key | Nitronic40® | 760 | 965 | 1030
Yoke | Iron | 284 | 504 | 542
Shell | AL 7075 | 189 | 275 | 301
PAGE 25
Material | Rp 0.2 [MPa] | 
 | 293 K | 4.3 K
Al 7075 | 480 | 690
SS 316 LN | 286 | 930
NITRONIC 40 | 353 | 1240
MAGNETIL (IRON) | 180 | 723
Ti 6Al 4V | 827 | 1654

## Slide 28: Summary – single aperture
Bladder&key pre-stress method
Windings:
  Peak stress values up to 220 MPa
  Good contact up to nominal (100% powering)
  Contact degraded at 105% (still acceptable?)
Mechanical structure:
  Shell, pole in the yield stress limit
  Iron parts in tension need deeper investigation (200 MPa or more?) and better shaping

## Slide 29: Extra
Relative x-displacement between CD and NF
NF – CD

## Slide 30: Contact at 18 T
18 T