## Slide 1: Cost considerations
D. Schoerling, CERN
Maria Durante, Clement Lorin, CEA
Teresa Martinez, Fernando Toral, CIEMAT
May 12th, 2016

## Slide 2
Status
Goal: Provide preliminary estimates of the cost of the dipole magnets as a function of field and temperature based on cross-sections scaled from the EuroCirCol 16 T dipole design and from LHC magnet cost
Reference parameters: 50 mm aperture, 4578 magnets, 14.3 m long, 16 T
Jcu ≤ 1200 A/mm2 (magnet protection at short sample) and Cu/Non-Cu ≥ 1:1(optimized strand production)

## Slide 3
Target cost of magnet
Cost of LHC dipole magnet taken as reference and target
LHC dipole cost was around 1 MCHF/dipole, 2000 (around 660 kEUR/dipole, 2000)
The conductor cost was around 200 kEUR/dipole, 2000
Assuming 2% inflation over 16 years for the dipoles one finds 900 kEUR/dipole, 2015
The cost of the LHC dipole without conductor is 630 kEUR/dipole, 2015
The volume of the structure is larger, the manufacturing process involves more steps due to heat treatment, different insulation technique, etc., but also number of units is larger. A detailed study started to work out the cost of the structure & assembly has been started with CEA & CIEMAT.

## Slide 4
Analytical model (CIEMAT)
4

## Slide 5
Conductor Jc-fit
Chart: B in T
Where:
with Bp peak field on the conductor
Tc0 = 16 K, Bc20 =29.4 T, α = 0.96, C0 = 270 kA/mm2 T.
Cable degradation: 0%.
Fit for the target value of Jc(4.2 K, 16 T) = 1500 A/mm2

## Slide 6
Conductor amount vs field @ 4.2 K
Conductor amount is very sensitive to the operational field and margin
Conductor mass in kt
kt | 15 T | 16 T
10% | 8 | 10
15% | 10 | 16
20% | 16 | >25
Constant integrated field
Chart: Temperature 4.2 K
| 15.52 | 15.040000000000001 | 14.719999999999999 | 14.32 | 13.92 | 13.280000000000001 | 12.240000000000002
20% | 21482.3209 | 16503.3349 | 14052.9667 | 11793.2405 | 10245.198 | 8765.1253 | 7143.2987
15% | 20209.9649 | 15524.6611 | 13218.9379 | 11092.7378 | 9636.3242 | 8244.1556 | 6718.9299
10% | 18976.7608 | 14558.3195 | 12384.9571 | 10382.083 | 9011.6436 | 7704.6232 | 6276.0454
 | 0 | 25000

## Slide 7
Conductor amount vs field @ 1.9 K
Conductor amount is sensitive to the operational field and margin
Conductor mass in kt
kt | 15 T | 16 T
10% | 6 | 7
15% | 8 | 9
20% | 10 | 12
Constant integrated field
Chart: Temperature 1.9 K
| 16 | 15.600000000000001 | 15.12 | 13.92 | 13.12 | 12.08
20% | 12159.005 | 10908.4227 | 9701.7877 | 7618.2872 | 6551.8692 | 5654.5124
15% | 11443.7694 | 10266.7507 | 9131.0943 | 7170.1526 | 6166.4651 | 5321.8941
10% | 10808.0045 | 9696.3757 | 8623.8113 | 6771.8108 | 5823.8837 | 5026.2333
 | 0 | 25000

## Slide 8
Elasticity of conductor mass (CEA)
We can define a field elasticity as
An operational field of 14 T requires ~50% of the conductor required for 16 T
1% more field at 14 T cost 3.5% more mass of conductor,
1% more field at 16 T cost 7.5% more mass of conductor
Chart: Operational field B in T
| 8 | 8.25 | 8.5 | 8.75 | 9 | 9.25 | 9.5 | 9.75 | 10 | 10.25 | 10.5 | 10.75 | 11 | 11.25 | 11.5 | 11.75 | 12 | 12.25 | 12.5 | 12.75 | 13 | 13.25 | 13.5 | 13.75 | 14 | 14.25 | 14.5 | 14.75 | 15 | 15.25 | 15.5 | 15.75 | 16 | 16.25 | 16.5
 | 1.0076 | 1.0106 | 1.0148 | 1.0203 | 1.0276 | 1.0373 | 1.05 | 1.0664 | 1.0876 | 1.1146 | 1.1489 | 1.1921 | 1.2462 | 1.3133 | 1.3959 | 1.4968 | 1.6189 | 1.7655 | 1.9398 | 2.1447 | 2.383 | 2.6568 | 2.9674 | 3.3148 | 3.6978 | 4.1135 | 4.5576 | 5.0244 | 5.5068 | 5.9972 | 6.4877 | 6.9705 | 7.4388 | 7.8865 | 8.3091

## Slide 9
Conductor composition
Non-Cu and conductor mass in kt
kt | 15 T | 16 T
Non-Cu | 3 | 4
Total | 8 | 10
Evaluation for 10% margin at 4.2 K and ~18% margin at 1.9 K
Constant integrated field
Chart: Operational field in T
| 17.46 | 16.920000000000002 | 16.559999999999999 | 16.11 | 15.659999999999998 | 14.940000000000001 | 13.770000000000001
Non-Cu mass | 8815.7658 | 6523.3564 | 5408.1385 | 4389.8311 | 3696.7174 | 3017.389 | 2105.7301
Conductor mass | 19388.7673 | 14876.7298 | 12657.2481 | 10611.7708 | 9212.057 | 7876.8607 | 6417.1286
 | 0 | 25000

## Slide 10
Target cost of conductor
Performance based cost cp | Mass based cost cm
cpt = 5 EUR/kA.m at 4.2 K and 16 T | cmt = 430 EUR/kg
cpp = 10 EUR/kA.m at 4.2 K and 16 T | cmp = 860 EUR/kg
Cp = cp x Jc x ASC x N x L = cm x 2mSC | Cm = cm (ASC + ACu) x  x N x L = cm (mSC + mCu)
Discussion between mass and performance based cost is on-going
Target performance is set to Jc(4.2 K, 16 T) = 1500 A/mm2
Outer layers require larger Cu/non-Cu ratios than inner layers
Jc (4.2 K, 16 T) =1500 A/mm2
ASC & ACu : Total area of SC and Cu in conductor
mSC & mCu: Total mass of SC and Cu
N = 4578 units
L = 14.3 m : Length of per magnet unit
 = 8.7 kg/dm3
We will then multiply these numbers by 1.3 to account for waste & testing

## Slide 11
Conductor cost for FCC-hh dipoles
Total cost of conductor | 15 T [MEUR] | 16 T [MEUR]
Cmt with 430 EUR/kg | 4,500 | 5,600
Cpt with 5 EUR/kA.m | 3,400 | 4,500
Total cost of conductor | 15 T [MEUR] | 16 T [MEUR]
Cmp with 860 EUR/kg | 9,000 | 11,200
Cpp with 10 EUR/kA.m | 6,800 | 9,000
Target cost
Pessimistic cost

## Slide 12
Conductor amount vs aperture
Increasing the aperture from 50 to 60 mm would increase the required conductor amount by ~13%
This estimate coincides well with the approximate estimate:
, ,
with ri  50-60 mm (aperture); Jeng  880 A/mm2 (equivalent average engineering current density), B1 = 16 T, = 60
In terms of magnet cost this would represent a cost increase of approximately ~10%, i.e., the magnet cost increase is of the order of half of the aperture increase:
at around 50 mm and 16 T

## Slide 13
Total cost of FCC-hh dipoles
FCC with LHC magnet cost without conductor: 630 kEUR/unit x 4578 unit= 2900 MEUR
Magnets at 4.2 K at 10% margin and at 1.9 K at ~18% margin have a similar cost
The cost for 15 T magnets is given for 4883 units (constant integrated field)
Total cost | 15 T [MEUR] | 16 T [MEUR]
Cmt with 430 EUR/kg | 7,400 | 8,500
Cpt with 5 EUR/kA.m | 6,300 | 7,400
Total cost | 15 T [MEUR] | 16 T [MEUR]
Cmp with 860 EUR/kg | 11,900 | 14,100
Cpp with 10 EUR/kA.m | 9,700 | 11,900
Target cost
Pessimistic cost

## Slide 14: Conclusion
Margin is very expensive
5% (15%->20%) margin at 1.9 K => 25% more conductor cost (~ 2 GEUR)
The conductor cost represents more than half of the magnet cost: any effort shall be pursued to minimize this cost