## Slide 1: Highlights from MAX IV commissioning and operation
Pedro F. Tavares on behalf of the MAX IV team
ELETTRA – September 2016

## Slide 2: Summary
The MAX IV Facility
The MAX IV 3 GeV Ring
Commissioning Highlights
Next Steps
Future Perspectives

## Slide 3: Conceptual Basis of the MAX IV Design
Scientific Case calls for high brightness radiation over a wide spectral and time range: IR to Hard R-rays, Short X-Ray Pulses.
Need for high brightness: low emittance and optimized insertion devices.
This is hard to achieve in a single machine:
higher electron beam energy  harder photons
lower electron beam energy  softer photons
One size does not fit all !

## Slide 4: The MAX IV Approach
Different machines for different uses:
  A high energy ring with ultra-low emittance for hard X-ray users.
  A low emittance low energy ring for soft radiation users
  A LINAC based source for generating short pulses and allowing for future development of an FEL source.

## Slide 5: MAX IV – an overview
Annika Nyberg, MAX IV-laboratoriet, 2012
Linear Accelerator
3 GeV Storage Ring
1.5 GeV SR
Short Pulse Facility
Notes: MAX-lab – a national research facility jointly financed by the Research Council and Lund University. Synchrotron radiation is produced and used for experiments.
Three storage rings and an injector.
MAX I: 550 MeV, 32.4 m circumference, commissioned 1986
MAX II: 1.5 GeV, 90 m circumference, commissioned 1996
MAX III: 700 MeV, 36 m circumference, commissioned 2007

## Slide 6
© Photo: Perry Nordeng
18-Sept-2014

## Slide 7: MAX IV - An integrated Solution
MBA Lattice
Ultra-low emittance
robust, high stability. large momentum aperture
Large Number of Magnets
Small Magnet Apertures
Wake-Fields
Low RF frequency
Full Energy Injector LINAC: Short Pulses
Long Bunches
Landau Cavities
Compact Magnet Design. High precision, High vibration frequencies
Narrow vacuum Chambers
Multi-purpose Strong Magnets
IBS
Low Vacuum Conductance
High Heat Load Density
Copper Chambers
100 % NEG Coating

## Slide 8: The MAX IV 3 GeV ring Lattice
7-bend achromat
20 periods
Picture MAX IV DDR
Matching Cells
Unit Cells

## Slide 9
FemtoMAX fs dynamics in solid
NanoMAX Nano-imaging & - spectroscopy
BALDER Chemical spectroscopy: operando
BioMAX Protein crystallography
Veritas Electronic & magnetic excitations: solids
Hippie Photoemission: near ambient pressure
ARPES Electronic structure: solids
FinEstBeaMS Electronic structure: gases, aerosols
SPECIES Electronic & magnetic excitations: surfaces
Transfer_PEEM Microscopy: surfaces
Transfer_XPS Electronic structure: surfaces & gases
CoSAXS Geometric structure & correlation: (bio) liquids
SoftiMAX Microscopy & method development
DanMAX Powder diffraction & imaging: materials science
ForMAX Wood & paper: structure & processing
MicroMAX Most relevant (difficult) protein structures
DiffMAX Crystal structure of bulk & surface
iMAX Imaging of engineering materials
8
4
3
2
1
6
5
7
9
10
12
11
13
14
15
Slide by C. Quitmann

## Slide 10: Project Timeline – MAX IV 3 GeV Ring

## Slide 11: 3 GeV Ring Commissioning Timeline
Beam in TR3
Aug 11
2015
First Turn
Aug 25
2015
Stored Beam
0.1 mA
Sep 15
2015
Stacking
4 mA
Oct 08
2015
First Light
Nov 2
2015
198 mA
July 9, 2016
Feb&March 2016
First IVUs

## Slide 12: Early Commissioning Results
Beam observed at the end of TR3 and into the ring.
M1
2015/08/11
Picture J.Alhbäck

## Slide 13: Threading the beam – first turn – many turns
2015/08/26
2015/08/27
3 passes
35 passes
2015/08/25
All correctors OFF
Picture S.Leemann

## Slide 14: First Stored Beam
Injected beam
Injection
Stored beam 2 seconds after previous injection pulse
Kicker Current
Revolution period
2015/09/15

## Slide 15: Linear Optics Characterization: Integer Tunes
Fractional tunes: 0.2087/0.2676

## Slide 16: Bare Vertical Orbit
Example calculation for one random seed
MAX-lab Internal Note 201211071 by S.Leemann
Plot by M.Sjöström

## Slide 17: LOCO: reduction in dispersion beating
Before LOCO
Before LOCO
After LOCO: July 2016

## Slide 18: Beta-beat Reconstructed from LOCO

## Slide 19: BPM Offsets
Measured by BBC using trim coils in sextupole magnets
RMS: 144 µm H / 138 µm V

## Slide 20: Orbit Stability / Slow Acquisition
Plot by M. Sjöström

## Slide 21: Aperture scans, scraper measurements
Vertical aperture scaled to center of LS 2.3 mm
2016-02-03 measurement by J. Sundberg
2011 simulations by S.Leemann

## Slide 22: Injection Efficiency&Top-up (closed shutters)
>24 hr top-up at 160 mA
>95 %

## Slide 23: Collective Effects – Single Bunch
No signs of TMCI up to 8.55 mA (nominal 2.8 mA/bunch).
Significant bunch lengthening even without harmonic cavities
Data by J.Breunlin, A.Andersson, G.Skripka, R.Nagaoka

## Slide 24: Bunch Lengthening
Slide by G. Skripka

## Slide 25: Collective Effects - Multibunch
Possible to store >170 mA without feedback and without harmonic cavities. Predicted RW threshold was only ~ 40 mA !
HOM driven longitudinal motion is evident at a few mA in uniform fill.
Temperature tuning has proved effective in fighting longitudinal CBI.
HC stabilization of CBMs at 120 mA
Picure by G.Skripka
Up to 198 mA in multibunch mode

## Slide 26: Bunch-By-Bunch feedback
Longitudinal
Spectrum
Stable beam with feedback on at 90 mA
Unstable beam with feedback off at 100 mA
Transverse
Profile

## Slide 27: Vacuum System
>6 A.h product lifetime*Current
> 100 A.h Accumulated Dose
Plots by M.Grabski
Chamber Heating downstream of absorber
Photo by M. Sjöström

## Slide 28: Insertion Devices 3 GeV ring
2 In vacuum undulators in spring 2016
1 in vacuum wiggler + 2 EPUs (Autumn 2016)
Biomax undulator in the 3 GeV ring tunnel
First light from IVU in Biomax
2016/04/29 0.5 mA, 14 mm gap

## Slide 29: Insertion Devices in the 3 GeV Ring
Balder In-vacuuum wiggler
Hippier EPU
Veritas EPU chamber

## Slide 30: Sigma polarized SR, 632.8 nm, SRW calculation (left) and measured image (right). The simulation is done for εx = 320 pm rad, βy = 1.5 m. Both figures show a 2 x 2 mm^2 area of the image plane. The fringe pattern is too weak to be visible. Optical magnification of m=-2.28 is taken into account in the SRW model Horizontal opening angle: 6 mrad Vertical opening angle: 8 mrad Exposure time: 2.9 ms
Slide by J.Breulin
Emittance Measurement

## Slide 31: Horizontal intensity profile of imaged sigma polarized SR. Due to the reduced horizontal opening angle the fringe pattern is not as pronounced as it could be, but easier to understand and to calculate. Present setup is limited by optical aberations (from misalignments) and surface quality from optical components (some are inherited from MAX II, MAX III). Steady improvements during the next weeks are planned. Camera linearity might also be an issue! Challenges on the SRW model side are to include for example: variation of dipole field, variation of beta_x, variation of vertical opening angle, along the observed electron beam path.
Slide by J.Breulin

## Slide 32: Vertical Emittance Measurement
y=6.94 ± 0.9 pm.rad
Figs by J.Breunlin and Å.Andersson

## Slide 33: Beam parameters Thermionic Gun
Kicker & septum
Extraction 3 GeV
BC1 @ 260 MeV
SPF
BC2 @ 3 GeV
Extraction 1.5 GeV
L2A
L2B
L3A
L9B
L19B
L1B
L0
Thermionic RF gun
Photo cathode RF gun
Energy | 270 MeV
Energy spread | 0.5 % (fwhm)
Norm emittance x | 5.5 mm mrad
Charge | ~ 280 pC
MS1
Energy | 270 MeV
Energy spread | 0.5 % (fwhm)
Norm emittance x | 12 mm mrad
Norm emittance y | 4.7 mm mrad
Charge | ~ 280 pC
MS2
Energy | 3 GeV
Energy spread | 0.6 % (fwhm)
Norm emittance x | 15 mm mrad
Charge | ~ 220 pC
MS3/TR3
Slide by S.Thorin

## Slide 34: LINAC Mode Switching and Feedback

## Slide 35: Installation and Start of Commissioning 1.5 GeV Ring

## Slide 36: Main Problems/Difficulties
RF Cavity Conditioning
Diagnostic System Commissioning
  BPMs
Kicker Magnet PS failure
Gun Klystron Failures
Long Radiation Surveys
Cooling System Failures
PS Failures
Heating of chambers (in photon beam pipe)

## Slide 37: Next Steps
  3 GeV Ring
    Further conditioning of RF cavities
    Further linear optics trimming/Non-linear optics trimming
    Collective Effects studies (Harmonic cavity tuning)
    Fast Orbit feedback
    Multipole Kicker (SOLEIL&BESSY collaboration)
1.5 GeV ring Commissioning
November 2016: Commissioning users (3 GeV ring)
Spring 2017: First open call users (3 GeV ring)
Spring 2017: First Ids in the 1.5 GeV ring
May-June 2017: LINAC RF upgrade

## Slide 38: Future Perspectives
LINAC
Soft X Ray FEL (proposal User Community)
Hard X Ray FEL
3 GeV Ring
Brightness Improvements: current lattice and Ids (150 pm rad)
Brightness Improvements: additional focussing (100 pm rad)
1.5 GeV Ring
Timing modes (requested by User Community)
Completely new lattice (diffraction limit at 10 keV)
Full Delivery of the DDR Parameters – User operations

## Slide 39: Thank You !
Photo:S.Thorin
Photo:H.Tarawneh
Photo:L. Isaksson

## Slide 40: Backup slides

## Slide 41
Alignment error model S.Leemann October 2011

## Slide 42: Pulsed Magnets – Dipole Kickers
Kickers and Pingers (4 units) delivered to MAX IV in October 2014.
Site Acceptance tests done December 2014.
Kicker and Pinger chamber installed in the 3 GeV ring
Pulsed Magnet Cabinets
Assembled Pinger Magnet on 3 GeV Ring
Kicker Magnet Chamber on 3 GeV Ring

## Slide 43: MAX IV 3 GeV Ring DC Magnets
Slide by Martin Johansson
• Each cell is realized as one mechanical unit containing all magnet elements.
•Each unit consists of a bottom and a top yoke half, machined out of one solid iron block, 2.3-3.4 m long.

## Slide 44: DC Magnet Production History

## Slide 45
One achromat
MAX IV 3 GeV ring vacuum system layout
BPM
Ion pump location
Absorber location
Beam direction
Sector valve location
VC10
VC1
VC2
VC3
VC4
VC5
VC6
VC7
VC8
VC9
Slide by E.Al-dmour

## Slide 46: Chamber Production History
“standard “ chambers

## Slide 47: MAX IV 3 GeV ring RF System
Passive Harmonic Cavities
100 MHz Main Cavities
SS UHF Transmitters

## Slide 48: Capture and Bunching
2015/09/23
First pass
500 MHz from Chopper
100 turns
150 turns
175 turns
200 turns
Plots S.Leeman

## Slide 49: Orbit Stability – Fast Acquisition
Plot by Brian Jensen

## Slide 50: Beam parameters Thermionic Gun
Kicker & septum
Extraction 3 GeV
BC1 @ 260 MeV
SPF
BC2 @ 3 GeV
Extraction 1.5 GeV
L2A
L2B
L3A
L9B
L19B
L1B
L0
Thermionic RF gun
Photo cathode RF gun
Energy | 270 MeV
Energy spread | 0.5 % (fwhm)
Norm emittance x | 5.5 mm mrad
Charge | ~ 350 pC
MS1
Energy | 270 MeV
Energy spread | 0.5 % (fwhm)
Norm emittance x | 12 mm mrad
Norm emittance y | 4.7 mm mrad
Charge | ~ 350 pC
MS2
Energy | 3 GeV
Energy spread | 0.6 % (fwhm)
Norm emittance x | 15 mm mrad
Charge | ~ 300 pC
MS3/TR3
Slide by S.Thorin

## Slide 51: Compactedness is the key !
Picture by E. Aldmour

## Slide 52: Beyond MAX IV – exploring future possibilities
Can the MBA concept be used to design a storage ring that provides a bare lattice natural emittance ̴ 10 pm rad within the MAX IV 3 GeV ring circumference (528 m) ?
If we take the present trend to smaller gaps to a new level, and consider that “…when it is necessary that a magnetically significant dimension of a magnet is very small, a permanent magnet will always produce higher fields than an electromagnet”, K. Halbach J.App.Phys (1985), Vol. 57, N. 1.
Large scale use of permanent magnet technology could play a key role in this development.

## Slide 54: Current SR Projects using PM Technology (for dipole magnets)
Sirius
ESRF-II
Spring 8-II

## Slide 55: Diffraction Limited @ 10 keV within ~ 500 m
Novel Injection Schemes
High Gradient Permanent Magnets
NEG coating very small apertures
Long(er) Bunches
Compact Design – Small Aperture
Enabling Technologies

## Slide 56
Beyond MAX IV – an exercise
Existing 7 BA
Future Lattice Candidate – 19 BA

## Slide 57: Beyond MAX IV – an exercise
BH
SD
SD
SF
QF
QF
BH
Unit cell phase advances: ,
19-BA lattice in the MAX IV 3 GeV ring tunnel
Lattice design: OPA (A.Streun)
Elegant (M.Borland)

## Slide 58: Beyond MAX IV – an exercise 19-BA lattice in the MAX IV 3 GeV ring tunnel

## Slide 59: 19-BA lattice in the MAX IV 3 GeV ring tunnel - Dynamic and momentum aperture
No errors !

## Slide 60: 19-BA lattice in the MAX IV 3 GeV ring tunnel – Magnet Parameters
Magnet bore radius = 5.5 mm