## Slide 1: CMS HL-LHC EM Calorimeter Upgrade
M. Hansen, CERN

## Slide 2: ECAL barrel Phase 2 Upgrade Requirements
Trigger rate up to 750 kHz
  Legacy max ~150 kHz
Trigger latency up to 12.5 us
  Legacy max ~5 us
Full installation during LHC Long Shutdown 3
Maintained or improved reliability and availability
Improved ECAL spike detection and mitigation
Front End specific
  Magnetic field tolerant (4T)
  Radiation tolerant ~5Mrad (1 Mrad expected)

## Slide 3: ECAL barrel Phase 2 Upgrade High on the wish list
Re-optimize front end ASIC parameters in order to maintain performance despite crystal and APD degradation due to radiation damage
Decrease the physical volume required for services on YB0
  E.g. by decreasing the Low Voltage Current delivered to the Front End and thus use thinner or less cables
  E.g. by decreasing power consumption in the front end and thus use thinner cooling lines
Review front end grounding and shielding scheme in order to make the system less sensitive to EMI
Solid failure mitigation scheme
  E.g. avoid dependence between neighbours

## Slide 4: Phase 2 ECAL Barrel FE electronics system - Design idea
Modularity
  1 channel for readout and trigger
  As legacy for services (bias, LV)
Features
  Trigger-less (streaming)
Requires 10 Gbps GBT
  4 fibres per legacy tower with 80 Msamples, 8 fibers for 160 Msamples and HP timing
HSSer
HSSer
HSSer
GBT
GBT
GBT
ADC?
PreAmp?
PD1
APD
PD2
APD
PbW crystal
VFE card
FE card
PreAmp/ADC?
QIE?
10.24Gbps
10.24Gbps
10.24Gbps
2.56Gbps
Controls
Data stream + control handshake
Data stream
Data stream
LV regulator board, e.g 3 to 6 rad tol DCDC

## Slide 5: External constraints
YB0 and YE1+- services will be completely removed early in LS3
  Cables, fibres and pipes cut in 1m pieces by a team without silk gloves and discarded
As a consequence essentially all cables between UXC55 and USC55 will have to be replaced
  Essentially fibers and HV cables for the EB
One full year for 36 Supermodule removal, re-work, and re-installation

## Slide 6: Internal constraints
Modularity
  25 readout channels organized as 5 phi strips
  APD and low voltage connectors fully defined
VFE and LVRB form factor known
  3D limits including hard connection to cooling system
  Motherboard (APD) connector fully defined
  Need good reasons to change the FE connector
FE form factor known
  2D limits
  Again, need good reasons to change the VFE connector
Power budget within legacy limits, essentially 2W per channel; Goal perfectly within reach is 1W per channel

## Slide 7: External aid
Applicable and useful common developments
  lpGBT @ 10.24 / 2.56 Gbps
    Development ongoing, cost estimated to 35 CHF
  Versatile link +
    Development ongoing, cost estimated to 100 USD per connection (rad hard optics plus fiber, OD parts excluded)
  Low voltage regulator
    Radiation and magnetic field tolerant DCDC converter in production, development of enhanced ASIC ongoing, module available for 35 CHF
  Radiation tolerance qualified tool kit for TSMC 130nm and 65nm available
    Including e.g. eLink macros for ADC – GBT integration
CMS ECAL may want to contribute to these multi-institutional / multi-national projects

## Slide 8: Development Timeline
Kick-off about a year ago
This workshop
  Essentially about VFE specification and strategy for technology selection
Comprehensive review June 2016
  Essentially a report from this workshop and current actions
December 2016
  Baseline VFE design
  Demonstration of FE DCDC power feasibility
September 2017
  TDR
  Here we have to demonstrate that we know what we need, what to do and that the resources are sufficient to deliver the project on time

## Slide 9: LpGBT
Down-link: 2.56 Gb/s (64 –bit frame)
  User bandwidth with FEC12: 1.44 Gb/s or 36 bits / 40MHz clock
Up-link: 10.24 Gb/s (256 –bit frame)
  User bandwidth
    FEC12: 8 Gb/s
    FEC5: 9.13 Gb/s
Phase/Frequency programmable clocks
  4 independent clocks with 50ps phase resolution
  Frequencies: 40 / 80 / 160 / 320 / 640 / 1280 MHz

## Slide 10: LpGBT
ASIC control: IC channel: 80 Mb/s
  I2C interface
    LpGLD control:I2C master
Experiment control: EC channel: 80 Mb/s
  Two I2C masters
  Programmable parallel port:16 x DIO
  Environmental parameters monitoring
    10-bit ADC with 8 inputs
    Temperature sensor on chip
    Programmable current source to drive an external temperature sensor
Replaces the current GBT-SCA

## Slide 11: Link and bit counts
eLinks FEC5 @ 10.24 Gb/s
  Bandwidth: 320 / 640 / 1280 Mb/s
    8 / 16 / 32 bits per 40 MHz clock
  # eLinks*: 28 / 14 / 7
eLinks FEC12 @ 10.24 Gb/s
  Bandwidth: 320 / 640 / 1280 Mb/s
    8 / 16 / 32 bits per 40 MHz clock
  # eLinks*: 24 / 12 / 6
eLink Macro exists for TSMC 130nm and 65nm

## Slide 12: Link and bit counts
Three 10 Gbit up-links would allow 24 (26) bits per channel
  Three 320 Mbit Elinks
  11 (12) bits ADC plus gain flag @ 80MHz. Enough?
  Requires e.g. one 3+1 versatile link+ module per FE (foreseen)
Four 10 Gbit up-links would allow 32 (34) bits per channel
  Four 320 Mbit or two 640 Mbit or one 1280 Mbit Elinks
  15 (16) bits ADC plus gain flag @ 80MHz. Better?
  Requires e.g. one 4+1 versatile link+ module per FE (foreseen)
Six 10 Gbit up-links would allow 48 (52) bits per channel
  Six 320 Mbit or three 640 Mbit Elinks
  11 (12) bits ADC plus gain flag @ 160MHz.
  15 (16) bits ADC plus gain flag @ 120MHz.
  Requires e.g. two 3+1 versatile link+ module per FE
    Only one FE control link would be used; the other receiver used for precision sampling clock?

## Slide 13: VFE to FE Data transmission
Implement a number of eLinks in every ADC / QIE for data streaming
  A few idle characters required in order to word-align at reception in the off detector electronics
    E.g. upon BC0 reception; note that the arrival time of the BC0 needs to be skewed together with the clock or at least dealt with
    Imagine e.g. an all zeros – all ones – all zeros transition as ADC response to the BC0

## Slide 14: LVRB replacement
A radiation and magnetic field tolerant ACDC power module has been developed which meets, a priori, our electrical requirements
  Investigate noise levels with an initial demonstrator; essentially done
  Verify behavior in radiation and magnetic field; started
  Develop LVRB respecting the mechanical requirements; first version essentially ready

## Slide 15: Bulk power system
Essentially all LHC upgrade projects are planning to use DCDC POL converters in or close to the front end system
The DCDC converters developed to date allow up to 12V input, essentially non-regulated.
A common project, similar to the legacy, is started in order to investigate the feasibility of operating COTS bulk power supplies
  In the service cavern
    Radiation level as essentially zero
    Magnetic field 50 – 100 Gauss
  In the experimental cavern, e.g. X0
    Radiation level as essentially as in service cavern
    Magnetic field 200 – 400 Gauss; balconies essentially excluded: up to 1200 Gauss

## Slide 16: Bias (HV) power system
Essentially, the requirements have not changed, thus the HV power system can be maintained.
  The key word is “maintained” rather than “kept”
  The complete system will very likely need to be renewed purely due to age
Profit from the complete YB0 de-installation to review the grounding and shielding implementation in order to become less sensitive to EMI

## Slide 17: Phase 2 ECAL Barrel FE electronics system
HSSer
HSSer
HSSer
lpGBT
lpGBT
lpGBT
ADC
- I2c interface?
- Clock phase adjust
Synch signal time skew
Test pulse skew
Baseline DACs?
Pre-Amplifier
Test pulse injection
I2c interface?
Baseline DACs?
VFE card
FE card
10.24Gbps
10.24Gbps
10.24Gbps
2.56Gbps
Controls
Data stream + control handshake
Data stream
Data stream
LV regulator board, with rad tol DCDC

## Slide 18: End

## Slide 19: Backup

## Slide 20: FE clock distribution
Option 1
  Use the (non-skewable) eLink clocks as the only clock in the ADC / QIE (sampling, internally multiplied for eLink transmission)
  Implement a clock skew function in each ADC in order to align sampling to beam
    Requires a control interface, e.g. i2c
Option 2
  Develop a clock fan-out chip with a clock skew function for each output
    Here, the ADC is somewhat (but not much) simpler but an additional ASIC is required
Option 1 appears attractive as it safely solves essentially all problems with a smaller number of ASICs