## Slide 1
LVR – SLVR overview
CMS ECAL VFE phase II upgrade workshop
CEA-Saclay INSTN
11-13 May 2016
B. Betev, L. Djambazov, W. Lustermann, ETH Zurich

## Slide 2
Present front electronics
Front End Electronics
LVR
VFE
VFE
VFE
VFE
VFE
Mother Board
HV in
Power in
Digital Voltage
Distribution (DCU)
‘Analog’ Voltage
Distribution:
MGPA + ADC
Trigger Fiber(s)
Data Fiber
Flexible Connection to APD’s / VPT’s
Control
Token Ring Board
Fiber Patch Panel
Fiber Patch Panel

## Slide 3
VFE power nets
VFE has 11 power nets:
5 x 2.5 V analog (MGPA)
5 x 2.5 V digital (ADC)
1 x 2.5 V digital (DCU)
10 of the power nets arrive via the MB
1 is connected to the FE card

## Slide 4
Power nets in the motherboard
Motherboard internal power planes
2.5 V digital
2.5 V analog

## Slide 5
Power nets in the LVR
LVR hosts 11 linear regulators providing:
4 digital voltages to the FE:
  3 voltages for the FE
  1 voltage for the DCUs on the VFE
7 voltages to the mother VFE:
  5 x 2.5 V for the MGPAs
  2 x 2.5 V for the ADCs

## Slide 6
SLVR with FEASTMP_CLP
First version designed by Magnus
6 power nets == FEASTMP_CLP:
  5 x 2.5 V for the VFE
  1 x 2.5 V for the FE
- Tested in TT setup: B. Betev
- Tested at Virginia University
Design and layout iteration: make it fit into super-modules:
- Prototypes are in production

## Slide 7
SLVR with FEASTMP_CLP
The SLVR becomes an almost passive board, hosting connectors for the FEASTMP_CLP modules and 3 DCU chips for voltage, current and temperature monitoring
 Properties and performance are (almost exclusively) determined by the FEASTMP modules
Output voltage variation:
Load and line regulation
Spread of output voltages
Radiation effects
Temperature effects
Developed and fabricated by CERN
radiation tolerant
over current protection
over temperature protection
under voltage protection

## Slide 8
SLVR power interface
Interface to the MB unchanged
VFE analog and digital power grouped
new
original

## Slide 9
SLVR power interface
Interface to the FE unchanged
All voltages on a single net

## Slide 10
SLVR 3D view
TOP view: will be covered by the housing and coupled to the cooling bar
BOTTOM view
FEASTMP modules plug through the SLVR card

## Slide 11
TT testsetup
SLVRB
Linear LV Power Supply
for input voltage of SLVRB
(Input voltage = 10 Volts)
Trigger Tower Test Setup in
B.892. The SLVR Board integrated in TT4 (CCU=6)
Wiener LV power supply for input voltage of TT 1, 2 and 3

## Slide 12
TT noise measurements
LVR  SLVR: Performance remains unchanged

## Slide 13
TT testsetup
new SLVR
old LVR
LVR  SLVR: no significant difference