## Slide 1: Estimates of heat load from synchrotron radiation for HL-LHC

## Slide 2: What changes from LHC to HL-LHC (LSS1 and LSS5)
  Scenarios with beam current up to almost double x 2 intensity
  Shorter D1 and D2, closer together  shorter bending radius = x 4.3 (D1) and x 1.6(D2) factor both on photon flux and and critical energy
  Larger aperture  smaller Q gradients 
  Crab cavities
A. Rossi BE-ABP-HSS meeting 20/04/16

## Slide 3: Synchrotron Radiation basics
Power emitted per unit length
Or per proton per unit length
Photon critical energy and average energy
Frank Zimmermann LHC Project Note 237 (http://cds.cern.ch/record/691934?ln=en)
A. Rossi BE-ABP-HSS meeting 20/04/16

## Slide 4: Bending radius
Dipoles (for separation dipoles geometrical factors)
Quadrupoles (assuming point-like beam distribution)
  K1 [m-2] quadrupole magnetic gradient
  x, y [m]
For D1 and D2 one can use the bending necessary to go from 194 to 0mm separation
from twiss file provided by RdM
A. Rossi BE-ABP-HSS meeting 20/04/16

## Slide 5: Calculation parameters IR1&5
 | HL-LHC |  | LHC | 
 | Magnetic length (m) | Magnetic grad (1/m2) | Magnetic length (m) | Magnetic grad (1/m2)
Q1 | 2 x 4.2 | +/-5.5E-03 | 6.37 | +/-8.7E-03
Q2 | 2 x 7.15 | -/+5.5E-03 | 2 x 5.5 | -/+8.7E-03
Q3 | 2 x 4.2 | +/-5.5E-03 | 6.37 | +/-8.7E-03
D1 | 6.27 | 194mm beam sep. and 66.941m distance D1-D2 | 21 | 194mm beam sep. and 85.913m distance D1-D2
D2 | 7.78 |  | 9.45 | 
Q4 | 3.83 | (different at different location*) | 3.4 | *
Q5 | 3.4 | * | 4.8 | *
Q6 | 4.8 | * | 4.8 | *
 | HL-LHC |  | LHC
Beam current | 2.22E11 ppb x 2748 bunches |  | 1.15E11 ppb x 2808 bunches
X angle (µrad) | Nom 590 | Flat 550 | 370
A. Rossi BE-ABP-HSS meeting 20/04/16

## Slide 6: Synchrotron radiation power [W] in IR1/5: HL V1.2 round, β*=15cm coll. vs LHC round, β*=40cm coll. (2016)
 | L1 & R5 B1 R1 & L5 B2 | R1 & L5 B1 L1 & R5 B2 | Photon critical energy | L1 & R5 B1 R1 & L5 B2 | R1 & L5 B1 L1 & R5 B2 | Photon critical energy
Q1 | 1.92E-01 (4.3) | 2.58E-01 (4.6) | 5-6 eV | 4.43E-02 | 5.60E-02 | 6-7 eV
Q2 | 2.69E-01 (2.7) | 8.36E-01 (2.7) | 7-8 eV | 9.91E-02 | 3.13E-01 | 8-9 eV
Q3 | 8.61E-01 (6.6) | 4.26E-01 (5.3) | 10 eV | 1.30E-01 | 8.11E-02 | 4-6 eV
D1 | 1.09E+00 (10.3) | 1.09E+00 (10.3) | 28.4 eV | 1.06E-01 | 1.06E-01 | 14.7 eV
D2 | 8.78E-01 (3.7) | 8.78E-01 (3.7) | 22.9 eV | 2.36E-01 | 2.36E-01 | 6.7 eV
Q4 | 0 | 0 |  | 0 | 0 | 
Q5 | 0 | 0 |  | 0 | 0 | 
Q6 | 0 | 0 |  | 0 | 0 | 
arc | 4.14E-01 (W/m) (1.87) |  | 43.8 eV |  |  | 43.8 eV
SR estimated as irradiated by each element per beam –> PHOTON code to estimate heat load distribution
Quadrupole SR estimated assuming point like beam, dipole equivalent. Q1-Q2-Q3 in 16 slices, Q4-Q5-Q6 in 4 slices.
A. Rossi BE-ABP-HSS meeting 20/04/16
SR power [W] per element per beam
Notes: Separation off

## Slide 7: Synchrotron radiation power [W] in IR1/5: HL V1.2 round, β*=15cm collision + flat collision
 | L1 & R5 B1 R1 & L5 B2 | R1 & L5 B1 L1 & R5 B2 | L1 & R5 B1 R1 & L5 B2 | R1 & L5 B1 L1 & R5 B2
Q1 | 1.92E-01 | 2.58E-01 | 1.67E-01 | 2.24E-01
Q2 | 2.69E-01 | 8.36E-01 | 2.34E-01 | 7.76E-01
Q3 | 8.61E-01 | 4.26E-01 | 7.48E-01 | 3.70E-01
D1 | 1.09E+00 | 1.09E+00 | 1.09E+00 | 1.09E+00
D2 | 8.78E-01 | 8.78E-01 | 8.78E-01 | 8.78E-01
Q4 | 0 | 0 | 0 | 0
Q5 | 0 | 0 | 0 | 0
Q6 | 0 | 0 | 0 | 0
SR estimated as irradiated by each element per beam –> PHOTON code to estimate heat load distribution
Quadrupole SR estimated assuming point like beam, dipole equivalent.
A. Rossi BE-ABP-HSS meeting 20/04/16
SR power [W] per element per beam
Notes: Separation off

## Slide 8: Aperture and knobs effects V1.2
 | Coil aperture | Beam1 aperture | H,V2full gaps | Sep. knob | Crossing Knob | Crab shift knob | Crab slope knob | Offset knob
 | [mm] |  | [mm] | [mm] | [mm] | [mm] | [mm] | [mm]
TAXS |  | Circle | 60, 60 | 0.8 | 6.1 | 0.0 | 0.0 | 2.0
MQXFA.[AB]1 | 150 | Octagon | 99, 99 | 0.8 | 11.2 | 0.0 | 0.0 | 2.4
MQXFB.[AB]2 | 150 | Octagon | 119, 119 | 1.2 | 16.7 | 0.2 | 0.0 | 3.6
MQXFA.[AB]3 | 150 | Octagon | 119, 119 | 0.8 | 16.6 | 0.4 | 0.0 | 2.8
MBXF | 150 | Octagon | 119, 119 | 0.5 | 15.5 | 0.5 | 0.0 | 2.4
TAXN |  | Circle | 85, 85 | 0.2 | 5.5 | 0.9 | 0.0 | 3.0
MBRD | 105 | Octagon | 84, 84 | 0.1 | 3.3 | 1.0 | 0.0 | 3.3
MCBRD | 105 | Octagon | 84, 84 | 0.1 | 1.7 | 1.0 | 0.1 | 3.4
MCBYY | 90 | Octagon | 70.8,70.8 | 0.0 | 0.1 | 1.0 | 0.5 | 4.0
MQYY | 90 | Octagon | 70.8,70.8 | 0.0 | 0.0 | 1.0 | 0.5 | 3.9
TCLMB.5 |  | RectEllipse | 57.8, 48 | 0.0 | 0.0 | 0.4 | 0.2 | 3.7
MCBY[HV].5 | 70 | RectEllipse | 57.8, 48 | 0.0 | 0.0 | 0.0 | 0.0 | 3.6
MQY.5 | 70 | RectEllipse | 57.8, 48 | 0.0 | 0.0 | 0.2 | 0.1 | 3.5
TCLMC.6 |  | RectEllipse | 45.1,35.3 | 0.0 | 0.0 | 0.0 | 0.0 | 2.3
MCBC[HV].6 | 56 | RectEllipse | 45.1,35.3 | 0.0 | 0.0 | 0.0 | 0.0 | 2.1
MQML.6 | 56 | RectEllipse | 45.1,35.3 | 0.0 | 0.0 | 0.0 | 0.0 | 2.1
1Either Beam screen or beam pipe;
2 Mechanical tolerances already removed. Rectellipse types are exchanges the H,V orientation depending on the polarity.
R. de Maria BE-ABP-HSS (ColUSM #67, 05/02/16)

## Slide 9: Synchrotron radiation power [W] in IR1/5: HL V1.2 round, β*=15cm collision + same with offset knobs
 | L1 & R5 B1 R1 & L5 B2 | R1 & L5 B1 L1 & R5 B2 | L1 & R5 B1 R1 & L5 B2 |  | R1 & L5 B1 L1 & R5 B2 | 
Q1 | 1.92E-01 | 2.58E-01 | 1.94E-01 F |  | 2.60E-01 F | 
Q2 | 2.69E-01 | 8.36E-01 | 2.87E-01 F |  | 8.54E-01 F | 
Q3 | 8.61E-01 | 4.26E-01 | 9.08E-01 F |  | 4.61E-02 F | 
D1 | 1.09E+00 | 1.09E+00 | 1.09E+00 F |  | 1.09E+00 F | 
D2 | 8.78E-01 | 8.78E-01 | 8.78E-01 F |  | 8.78E-01 F | 
 |  |  | L1 & L5 |  | R1 & R5 | 
 |  |  | B1 | B2 | B1 | B2
Q4 | 0 | 0 | 6.06E-04* | 6.51E-04* | 6.69E-04* | 7.74E-04*
Q5 | 0 | 0 | 3.38E-04* | 2E-04* | 5.85E-04* | 5.85E-04*
Q6 | 0 | 0 | 1.31E-04* | 1.4E-04* | 2.24E-04* | 1.76E-04*
F 30 to 60% more with operational offset
~zero w/o operational offset
A. Rossi BE-ABP-HSS meeting 20/04/16
SR power [W] per element per beam
Notes: Separation off

## Slide 10: Calculation parameters IR2&8
 | HL-LHC | 
 | Magnetic length (m) | Magnetic grad (1/m2)
Q1 | 6.37m | +/-8.7E-03
Q2 | 2 x 5.5m | -/+8.7E-03
Q3 | 6.37m | +/-8.7E-03
D1 | 9.45m | 194mm beam sep. and 62.7265m distance D1-D2
D2 | 9.45m | 
Q4 | 2 x 3.4m | *
Q5 | 2 x 3.4m (only in L2 and R8) | *
Q6 | 4.8m | *
A. Rossi BE-ABP-HSS meeting 20/04/16

## Slide 11: Synchrotron radiation power [W] in HL-LHC IR2/8: Nominal optics V1.2 round, β*=15cm collision and flat collision
SR estimated as produced by each element per beam –> PHOTON code to estimate heat load distribution
Quadrupole SR estimated assuming point like beam, dipole equivalent.
 | !R2/8
Q1 | 0
Q2 | 0
Q3 | 0
D1 | 4.40E-01
D2 | 8.23E-01
Q4 | 0
Q5 | 0
Q6 | 0
A. Rossi BE-ABP-HSS meeting 20/04/16
SR power [W] per element per beam
Notes: Separation off

## Slide 12: Summary
Synchrotron radiation power produced at HL-LHC larger than LHC for
  Higher beam current
  Different magnets (smaller bending angles)
  Optics
Preliminary values estimated for experimental insertion regions main quads and separation magnets
  Up to 10 times the power irradiated by single elements (D1 IR1/5)
  Up to 2 times the photon critical energy => larger gas desorption and photo-electrons.
Heat load distribution to be evaluated with MonteCarlo like code PHOTON.
A. Rossi BE-ABP-HSS meeting 20/04/16

## Slide 13
Frank Zimmermann LHC Project Note 237 (http://cds.cern.ch/record/691934?ln=en)

## Slide 14: From LHC Project Report 675
ΓLHC(arc) ≈ 1E17 ph/ms, <ε> ≈ 13 eV
<ΓLHC(LSS)> ≈ 3.6E15 ph/ms, <ε> ≈ 5 eV, max heat load 0.5W per element
1e18 –
1e17 –
1e16 –
1e15 –
1e14 –
1e13 –
1e12 –
1 –
1E-1 –
1E-2 –
1E-3 –
1e-4 –
1e-5 –
-200 -100 0 100 200
-200 -100 0 100 200
A. Rossi BE-ABP-HSS meeting 20/04/16