## Slide 1: Axel Lindner (DESY) Benno Willke (AEI Hanover) Herman Ten Kate (CERN)
Future options for searching axion-like particles through light-shining-through-a-wall experiments

## Slide 2: A LSW roadmap
axion-like particle mass
Two-photon-coupling

## Slide 3: A LSW roadmap
2010, CROWS @ CERN 2013
ALPS II @ DESY 2019
ALPS III 202X ?
OSQAR @ CERN 2015
axion-like particle mass
Two-photon-coupling
This presentation.

## Slide 4: Outline
Basics
  Motivation
  Challenges
  Fundamentals of Light-Shining-through-a-Wall
A future LSW experiment (“ALPS III”)
  Pros and cons
  Design criteria
  Magnets, optics, detectors
  Expected performance
Summary

## Slide 5: Introduction to WeaklyInteractingSlimParticles
WISPs are hypothetical bosons with masses below 1eV (< 0,000002 me).
Axion: a neutral pseudoscalar predicted to explain the CP conservation in QCD. Its physics is determined just by a symmetry breaking scale fa:
  Mass: ma = 0.6eV · (107GeV / fa)
  Coupling to two photons: ga = α·g / (2π·fa)
  Abundancy in the universe: Ωa / Ωc  (fa / 1012GeV)7/6
Axion-like particles (ALPs): Coupling strength and mass are not related by one fa.
Hidden photons: neutral vector bosons.
Mini-charged particles, Chameleons, massive gravity scalars, … (some of these might be related to dark energy).

## Slide 6: (Vague) hints for WISPs in the sky?
There are allowed regions in parameter space where an ALP can simultaneously explain the gamma ray transparency, the extra energy loss of stars, and the soft X-ray excess from Coma and be a subdominant contribution to CDM.
Phenomenon | ALP mass [eV] | ALP- coupl. [GeV-1] | Reference
TeV transparency | < 10-7 | > 10-12 | arXiv:1302.1208 [astro-ph.HE]
Star developments | < 103 |  3·10-11 | arXiv:1512.08108 [astro-ph.HE] arXiv:1605:06458 [astro-ph.SR]
CAB (Coma Cluster) | < 10-13 | 10-12 to 10-13 | arXiv:1406.5188 [hep-ph]

## Slide 7: The big picture: ALPs
Energy scale of “new physics”
10 TeV
105 TeV
109 TeV
LHC
104·LHC
Three main regions of interest:
Axion-like particles: “new physics” around 105 TeV.
QCD axions: “new physics” around 105 TeV.
QCD axions as dark matter: “new physics” around 109 TeV.
This presentation.

## Slide 8: Axion and axion-like-particle (ALP) couplings
Axion and other Nambu-Goldstone bosons arising from spontaneous breakdown of global symmetries are theoretically well-motivated very weakly interacting slim (ultra-light) particles. The coefficients are determined by specific ultraviolet extension of SM.
Courtesy A. Ringwald
a


## Slide 9: Axion and axion-like-particle (ALP) couplings
Axion and other Nambu-Goldstone bosons arising from spontaneous breakdown of global symmetries are theoretically well-motivated very weakly interacting slim (ultra-light) particles. The coefficients are determined by specific ultraviolet extension of SM.
Courtesy A. Ringwald
a


## Slide 10: How to look for ALPs …
… by exploiting their coupling to photons:
WISPs pass any barrier and could make light-shining-through-a-wall.
q = pγ – pΦ l: length of B field
Okun 1982, Skivie 1983, Ansel‘m 1985, Van Bibber et al. 1987
Axions, axion-like particles

## Slide 11: Exemplary plot on sensitivity (ALPS II)
LSW experiments working with optical photons (around 1 eV) provide high sensitivities for very low mass ALPs (below 0.1 meV).
The mass reach follows from a phase shift developing between the light and ALP fields due to the non-zero ALP mass.
http://iopscience.iop.org/article/10.1088/1748-0221/8/09/T09001/meta;jsessionid=1674E7ACB2293DB65394D34574F3AFED.c3.iopscience.cld.iop.org
ALP mass
Two-photon coupling

## Slide 12: ALPS II at DESY in 2019
ALPS II will be installed in a straight section of the HERA tunnel.

## Slide 13: How to look for ALPs …
… by exploiting their coupling to photons:
WISPs pass any barrier and could make light-shining-through-a-wall.
Okun 1982, Skivie 1983, Ansel‘m 1985, Van Bibber et al. 1987
ql << 1; conversion and re-conversion:
Axions, axion-like particles

## Slide 14: Outline
Basics
  Motivation
  Challenges
  Fundamentals of Light-Shining-through-a-Wall
A future LSW experiment (“ALPS III”)
  Pros and cons
  Design criteria
  Magnets, optics, detectors
  Expected performance
Summary

## Slide 15: Light-shining-through-a-wall in the laboratory

## Slide 16: Pros and cons for LSW in the laboratory
ALP parameter | LSW (laboratory) | Helioscopes | Dark matter searches

## Slide 17: Pros and cons for LSW in the laboratory
ALP parameter | LSW (laboratory) | Helioscopes | Dark matter searches
Parity and spin | yes | perhaps | yes
Coupling gaγ | yes | no | no
Coupling · flux | (does not apply) | yes | yes

## Slide 18: Pros and cons for LSW in the laboratory
ALP parameter | LSW (laboratory) | Helioscopes | Dark matter searches
Parity and spin | yes | perhaps | yes
Coupling gaγ | yes | no | no
Coupling · flux | (does not apply) | yes | yes
Mass | perhaps | perhaps | yes

## Slide 19: Pros and cons for LSW in the laboratory
ALP parameter | LSW (laboratory) | Helioscopes | Dark matter searches
Parity and spin | yes | perhaps | yes
Coupling gaγ | yes | no | no
Coupling · flux | (does not apply) | yes | yes
Mass | perhaps | perhaps | yes
Rely on astrophysical assumptions | no | yes | yes

## Slide 20: Pros and cons for LSW in the laboratory
ALP parameter | LSW (laboratory) | Helioscopes | Dark matter searches
Parity and spin | yes | perhaps | yes
Coupling gaγ | yes | no | no
Coupling · flux | (does not apply) | yes | yes
Mass | perhaps | perhaps | yes
Rely on astrophysical assumptions | no | yes | yes
QCD axion | no | yes | yes
LSW in the laboratory is very well suited to look for axion-like particles.

## Slide 21: Design criteria for LSW experiments

## Slide 22: Design criteria for LSW experiments with optical resonators
Use long strings of strong dipole magnets.
Implement optical resonators to recycle the light before the wall and to boost the re-conversion of ALPs to photons behind the wall.
The maximal length is given by the aperture of the magnets and the beam shape of the resonating mode in the optical resonators.
The maximal circulating light power before the wall is given by the damage threshold of the mirrors and the beam spot size.
Courtesy A. Spector (ALPS)

## Slide 23: Present and future dipole magnets for LSW experiments
https://fcc.web.cern.ch/Pages/Magnets.aspx
https://fcc.web.cern.ch/Documents/Publications/Magnets/CERN-ATS-2013-019.pdf
LSW experiments use dipoles developed for particle accelerators (and might use in future dipole magnets presently under development).
New demonstration dipole magnets under study for HE-LHC or FCC might provide
a magnetic field of 13 T (or later even up to 15 or 16 T)
in an aperture of 100 mm.

## Slide 24: Present and future dipole magnets for LSW experiments
https://fcc.web.cern.ch/Pages/Magnets.aspx
https://fcc.web.cern.ch/Documents/Publications/Magnets/CERN-ATS-2013-019.pdf
LSW experiments use dipoles developed for particle accelerators (and might use in future dipole magnets presently under development).
Thereafter one (or more) of these magnet designs may be produced in small series and become available for LSW experiments.
Depending of unit length, some 30-40 units may be needed for a 500 m long magnet string.

## Slide 25: Present and future dipole magnets for LSW experiments
LSW experiments use dipoles developed for particle accelerators (and might use in future dipole magnets presently under development).
For the “FCC” dipole parameters see for example:
  Bottura L, de Rijk G, Rossi L, Todesco E., IEEE Trans. Appl. Supercond. 22:4002008 (2012), http://ieeexplore.ieee.org/xpl/articleDetails.jsp?arnumber=6656892
  Todesco E, Bottura L, de Rijk G, Rossi L., IEEE Trans. Appl. Supercond. 24:4004306 (2014), http://ieeexplore.ieee.org/xpl/articleDetails.jsp?arnumber=6172724
Dipole | Aperture [mm] | Field strength [T] | LSW experiment | Number of used dipoles
HERA (straightened) | 50 | 5.3 | ALPS II (DESY) | 20
LHC | 40 | 9.0 | OSQAR (CERN) | 2
“FCC” | 100 | 13 | “ALPS III” | 

## Slide 26: Optical resonators in LSW experiments
The resonators before and after the wall have to resonate to the same mode.
Flat mirrors are placed in the center of the experiment around the wall.
The light power density is highest on the flat mirror before the wall (mirror damage threshold)!
Courtesy A. Spector (ALPS)

## Slide 27: Optics for LSW experiments I: resonator configuration
https://en.wikipedia.org/wiki/Optical_cavity

## Slide 28: Optics for LSW experiments I: resonator configuration
A confocal cavity:
longest resonator for a given aperture,
largest beamspot in the center and hence lowest power density on central mirror, therefore highest circulating power in the resonator before the wall.
https://en.wikipedia.org/wiki/Optical_cavity

## Slide 29: Gaussian beam in a confocal resonator
Using:
  L: length of the optical system, length of each resonator L/2.
  λ: wavelength of light
Beam waist: (ω0)2 = (L·λ) / 2π
Beam profile development: ω2(z) = (ω0)2 · (1+(z/zR)2), zR = π(ω0)2 /λ ω(L/2) = sqrt(2)·ω0
Clear aperture required for a cavity with a power built-up  100,000: r5 = 2.5·ω(z)
https://en.wikipedia.org/wiki/Gaussian_beam
b = L

## Slide 30: Optics for LSW experiments II: resonator examples
Aperture [mm] | Safety margin [mm] | Eff. aperture [mm] | ω (L/2) [mm] | ω0 [mm]
40 (LHC) | 10 | 30 | 6.0 | 4.2
50 (HERA) | 10 | 40 | 8.0 | 5.7
100 (FCC) | 10 | 90 | 18.0 | 12.7

## Slide 31: Optics for LSW experiments II: resonator examples
Aperture [mm] | Safety margin [mm] | Eff. aperture [mm] | ω (L/2) [mm] | ω0 [mm] | λ [nm] | L [m]
40 (LHC) | 10 | 30 | 6.0 | 4.2 | 1064 | 106
50 (HERA) | 10 | 40 | 8.0 | 5.7 | 1064 | 189
100 (FCC) | 10 | 90 | 18.0 | 12.7 | 1064 | 957
λ = 1064 nm is assumed following LIGO experience: mirror coatings for this wavelength can stand high power densities for long times.

## Slide 32: Optics for LSW experiments II: resonator examples
Aperture [mm] | Safety margin [mm] | Eff. aperture [mm] | ω (L/2) [mm] | ω0 [mm] | λ [nm] | L [m] | Maximal power [kW] | Magnetic length, one string [m]
40 (LHC) | 10 | 30 | 6.0 | 4.2 | 1064 | 106 | 280 | 43
50 (HERA) | 10 | 40 | 8.0 | 5.7 | 1064 | 189 | 500 | 81
100 (FCC) | 10 | 90 | 18.0 | 12.7 | 1064 | 957 | 2500 | 426
λ = 1064 nm is assumed following LIGO experiences: mirror coatings for this wavelength can stand high power densities for long times.
For the maximal power assume a damage threshold of 500 kW/cm2.
For the magnetic length
  subtract 10 m for the optical system outside the magnets and
  assume a “filling factor” for the magnetic field of 90%.

## Slide 33: Optics for LSW experiments IV: 532 nm options
Aperture [mm] | Safety margin [mm] | Eff. aperture [mm] | ω (L/2) [mm] | ω0 [mm] | λ [nm] | L [m] | Maximal power [kW] | Magnetic length, one string [m]
50 (HERA) | 10 | 40 | 8.0 | 5.7 | 1064 | 189 | 500 | 81
100 (FCC) | 10 | 90 | 18.0 | 12.7 | 1064 | 957 | 2500 | 426
50 (HERA) | 10 | 40 | 8.0 | 5.7 | 532 | 378 | ? | 166
100 (FCC) | 10 | 90 | 18.0 | 12.7 | 532 | 1913 | ? · 5 | 856
If high power, high quality mirror coatings for λ = 532 nm were available, LSW experiments could be doubled in length compared to λ = 1064 nm.
R&D is required to improve the power density damage threshold of coatings for 532 nm light.

## Slide 34: Long optical resonators in real life
The stable operation of an optical resonator becomes difficult, if both mirrors cannot be placed on one optical bench anymore.
The influence of seismic noise increases strongly.
LIGO has impressively proven that one can deal with such challenges.
By exploiting the LIGO expertise (AEI Hanover & Uni. of Gainesville, Florida) ALPS II has succeeded to install and operate a 20 m long resonator.
Publication in preparation

## Slide 35: A detector for LSW experiments
ALPS II uses a Transition Edge Sensor
  20 nm thin Tungsten film.
  Operated at 80 mK.
  Single 1064 nm photon detection.
  Single photon energy resolution < 8%.
  Intrinsic background around 10-4 1/s.
A heterodyne detection scheme is being developed as an alternative for the ALPS II experiment.
Conservative assumption: LSW experiments could detect a photon flux of 10-4 1/s.
20 nm x 25 x 25 µm2

## Slide 36: Ingredients for an “ALPS III” experiment
“ALPS III” sketch based on the following assumptions:
Magnetic field strength: 13 T
Magnetic length: 426 m
Light wavelength: 1064 nm
Circulating light power: 2.5 MW Photons against the wall: 1.4·1025 s-1
Power built-up behind the wall: 105
Detector sensitivity: 10-4 s-1
Resulting sensitivity for gaγ: 1·10-12 GeV-1 for m < 0.06 meV

## Slide 37: “ALPS III” in context
“ALPS III”
would dramatically increase the sensitivity for purely laboratory based experiments searching for axion-like particles.
would surpass even IAXO for very low mass ALPs.
would definitely probe astrophysics hints for ALPs.
would probe “dark matter” ALPs.
would perfectly complement IAXO!
“ALPS III”

## Slide 38: A little bonus
Assume to realize both magnet strings out of 40 dipoles each and
switch polarity between each dipole (“wiggler configuration”):
ALPS III
“Wiggler”
The full sensitivity is restored at a specific mass!
N
N
N
N
S
S
S
S
N
S
N
S
S
N
S
N

## Slide 39: Just for the fun of it: a little QCD axion bonus …
“ALPS III”
would dramatically increase the sensitivity for purely laboratory based experiments searching for axion-like particles.
would surpass even IAXO for very low mass ALPs.
would definitely probe astrophysics hints for ALPs.
would probe “dark matter” ALPs.
would perfectly complement IAXO!
“ALPS III”
“Wiggler”

## Slide 40: Summing up
By combining
present day expertise in optics (ALPS II lessons learned from LIGO)
and
present day expertise in detectors for very low photon fluxes (ALPS II)
with
new dipole magnets under development for future accelerators
purely laboratory based searches for axion-like particles will be possible well beyond the sensitivities of experiments under preparation.
The sensitivity might be increased even more by pushing for R&D on mirror coatings for 532 nm light.

## Slide 41: To-take-home
Accelerator dipole magnets under development at CERN could be the basis of an “ultimate” light-shining-through-a-wall experiment mainly searching for axion-like particles.
The costs of such an experiment would be dominated by the costs of the magnet strings.
  The costs probably strongly correlate with decisions on future accelerator projects.
Considering the development of the physics case for axion-like particles in the recent years, experiments have to move from the niche “make best use of existing equipment built for something else” to more dedicated installations:
  IAXO and “ALPS III”.