## Slide 1: HL-LHC LSSR5 integration - Alignment
Pablo Santos Díaz - Vincent Baglin
HL-LHC R5 integration – Alignment
CERN Geneva / 19-04-2016

## Slide 2: OUTLINE
Introduction: HI-LUMI LSSR5.
Vacuum chamber dimensions study.
Bellow dimensions study.
Alignment equipment.
Questions.

## Slide 3: Introduction: HI-LUMI LSSR5

## Slide 4: Introduction: HI-LUMI LSSR5
    Working on the LSSR5 integration establishing the vacuum equipment needed:
      Valves, bellows
      Vacuum Assemblies
      Gauges
      Vacuum chamber → setting the dimensions
      …

## Slide 5: Introduction: LSSR5 – between TAXN and D2
Detail A
5th axis = +/- 10 mm lateral displacement  specific bellows (VMT type)

## Slide 6: Introduction: LSSR5 – bellow-pipe transition
    Vacuum chamber inner diameter
    must be set to determine:
      If new bellows has to be design.
      Collisions between components.
BELLOW
PIPE

## Slide 7
What is required to set the dimensions
of the vacuum chamber?

## Slide 8: Vacuum chamber dimensions study

## Slide 9: Vacuum chamber dimensions study
    Inputs:
      Beam aperture: 85 mm.
    Data required for tolerance:
      Pipe mechanical tolerance&.
      Pipe alignment accuracy.
    Which is the alignment tolerance accuracy?
Assumed*
85 + yellow + yellow = 85+0.9+0.9 = 86.8
86.8 + purple + purple = 90.8  91 mm
Minimum value
* Today for LHC = 3 mm
& Mech Tol. = Cylindricity = concentricity+straightness+parallelism = 1.8 mm

## Slide 10: Bellow dimensions study

## Slide 11: Bellow optimization
Bellow body
Transition tube
RF fingers
Wen need to fit the inner diameter of the vacuum chamber with the inner diameter of RF bridge of the bellow in order to have no transition (tapering) between them.
RF bridge = transition tube + RF fingers

## Slide 12: Transition tube joint
Max. inner diameter
in transition tube joint

## Slide 13: Transition tube
3
2
1
2
1
Max. inner diameter
in transition tube
2
1
3

## Slide 14: RF Finger joint
Max. inner diameter
in RF finger joint

## Slide 15: Conclusions Bellow optimization and vacuum chamber study
Objective → to not have diameter transition between vacuum chamber and bellow:
Min inner diameter → 91 mm
Max inner diameter → 92 mm
Max vacuum module alignment accuracy* → 2.32 mm
TARGET :
ID91, Alignement +/- 1.8 mm
ID92, Alignement +/- 2.3 mm
All the tolerances shown are in radius

## Slide 16: Alignment equipment

## Slide 17: Alignment equipment
    In addition to vacuum chambers (VC), we have to align bellows (VMT), Supports (VHL) and vacuum assemblies (VA).
    For future design, improvement in alignment is
    needed. Today our alignment specification is 3 mm.
    What are the standard tools & means used to align an equipment?
    Which tools do we have to include in the design to do the alignment with your equipment?
Support
Vacuum assembly
    ?
    ?

## Slide 18: Alignment equipment
    Idea: to have a support aligned only once and its ancillaries easily exchangeable, without re-alignement, in order to follow ALARA recommendations.
      What is the alignment accuracy for this kind of support?
      What are the alignment tools do we need for this kind of support?

## Slide 19: Alignment equipment: VA
Alignment
tool
D2
(aligned)
BPM
(aligned)
Fix to D2
and aligned
Fix to BPM
and aligned
Need to
be aligned

## Slide 20: Alignment equipment: VC
Single
support
Double
support
Vacuum chamber supports have to be aligned
Movable & fixed supports

## Slide 21: Alignment equipment: VMT
Bellow
Support
Some Vacuum modules with double bellows have to be aligned

## Slide 22: Questions

## Slide 23: Questions
    What is the achievable alignment accuracy of an upgraded alignment system for the VA, VC, VMT?
Concerning the alignment equipment, what are the tools that you need to align an equipment?
If we design a new support, which tools do we have to include in the design to do the alignment with your equipment?
How do you do the alignment? Which tools or which methodology do you use?

## Slide 24: THANK YOU FOR YOUR ATTENTION!!!