## Slide 1: MPGD structures for reducing IBF
Fernando Amaro
LibPhys – Coimbra University
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal

## Slide 2: Ion Back Flow
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Gaseous Detectors
High gains (up to 106)
Back flowing ions
(move slowly)
charge build up and field distortion in the drift region (not good for TPC’s, specially high rate)
impact of ions on the surfaces : ions may trigger secondary avalanches and/or damage photocathodes (Gaseous Photomultipliers with visible photocathodes)
IBF is defined as the fraction of ions produced that reaches a region of interest in the detector (usually the drift region)

## Slide 3: Ion Back Flow
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Micro patterned Gaseous Detectors (GEM, MicroMegas, MHSP, COBRA) are game changers :
IBF is controlled by the electric fields: DVGEM, E1 and E2.
Cascading several GEM reduces the IBF to values of few %.
In “open” type detectors (Proportional counters) IBF = 1.
All ions eventually reach the cathode.
A gate is needed! But only works up to a certain rate… noise and instabilities increase.

## Slide 4: ALICE TPC upgrade
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Needs continuous readout (50 kHz)
IBF < 1% at a gain of 2000 (20 ions / primary electron)
Energy Resolution 12% (55Fe)
Ne-CO2-N2
Solution was a cascade of 4 GEM with different pitch size
[Piotr Gasik, for the ALICE Collaboration “FROM GATED TO CONTINUOUS READOUT- an upgrade of the ALICE TPC”, VCI 2016]
For the future ?
(ILC)

## Slide 5: Gaseous Photomultipliers
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Drift Field is higher than in TPC’s
Photocathode can be damaged by ion impact
Secondary emission from photocathode
[A. Bondar, et al., Study of ion feedback in multi-GEM structures, Nucl. Instr. And Meth. A 496 (2003) 325]
IBF increases linearly with drift field
Optimization of IBF is detector/application specific.
GPM’s require higher drift fields (>0.5 kV/cm) to ensure proper photo-electron extraction

## Slide 6: Alternative Solutions with the Micro Hole and Strip Plate
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Reversed/Flipped Reversed MHSP
[J.F.C.A. Veloso, F. D. Amaro, J.M. Maia, A. Breskin, A. Lyashenko, R. Chechik, J.M.F dos Santos, O. Bouianov, M. Bouianov “MHSP in reversed-bias operation mode for ion blocking in gas-avalanche multipliers” Nuclear Instruments and Methods in Physics Research A 548 (2005) 375–382.]
[A. Breskin, D. Mörmann, A. Lyashenko, R. Chechik, F.D. Amaro, J.M. Maia, J.F.C.A. Veloso, J.M.F. dos Santos “Ion-induced effects in GEM & GEM/MHSP gaseous photomultipliers for the UV and the visible spectral range” Nucl. Instrum. Meth. A 553 (2005) 46.]
[A.V. Lyashenko, A. Breskin, R. Chechik, J.F.C.A. Veloso, J.M.F. Dos Santos, F.D. Amaro “Advances in ion back-flow reduction in cascaded gaseous electron multipliers incorporating R-MHSP elements” 2006 JINST 1 P10004]
[A.V. Lyashenko, A. Breskin, R. Chechik, J.F.C.A. Veloso, J.M.F. Dos Santos, F.D. Amaro “Development of high-gain gaseous photomultipliers for the visible spectral range” 2009 JINST 4 P07005.]
[A. Lyashenko, et al. Nuclear Instruments and Methods in Physics Research Section A 610 (2009)] hole - multipliers” 2007 JINST 2 P08004]
[J.F.C.A. Veloso, C. Santos, F. Pereira, C. Azevedo, F.D. Amaro, J.M.F. dos Santos, A. Breskin, R. Chechik “THCOBRA: Ion back flow reduction in patterned THGEM cascades ” Nuclear Instruments and Methods in Physics Research A 639 (2011) 134–136]
Use of the secondary scintillation to propagate the signal in the detector
[J.F.C.A. Veloso, F. D. Amaro, J.M.F dos Santos, A. Breskin, A. Lyashenko, R. Chechik “The Photon-Assisted Cascaded Electron Multiplier: a concept for potential avalanche-ion blocking” JINST 1 P08003]
[F. D. Amaro, J. F. C. A. Veloso, J. M. F. dos Santos, A. Breskin, R. Chechik, A. Lyashenko “The Photon-Assisted Cascaded Electron Multiplier operation in CF4 for ion backflow suppression” IEEE Transactions on Nuclear Science 55-3 (2008) 1652-1656.]
[F. D. Amaro, J. F. C. A. Veloso, J. M. F. dos Santos, A. Breskin, R. Chechik, A. Lyashenko; “High pressure operation of the Photon-Assisted Cascaded Electron Multiplier” IEEE Transactions on Nuclear Science 56-3 (2009) 1097-1101.]
[F. D. Amaro et al. “Zero Ion Backflow electron multiplier operating in noble gases”, 2014_JINST_9_P02004]

## Slide 7: Micro Hole and Strip Plate
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Same technology as GEM but with 2 sets of electrodes in one of the sides (the bottom)
Normal mode of operation: the extra strips are used for electron multiplication, resulting in high gains and relatively low operation voltages. VT < VC < VA
[J. F. C. A. Veloso, J. M. F. dos Santos, C. A. N. Conde, "A proposed new microstructure for gás radiation detectors: The microhole and strip plate” Rev. Sci. Instrum. vol. 71 (2000) 2371-2376.]

## Slide 8: Micro Hole and Strip Plate – Reversed mode operation
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Same technology as GEM but with 2 sets of electrodes in one of the sides (the bottom)
Reversed mode operation: (for ion trapping) the anodes are at lower potential than the cathodes and are used to trap the back flowing ions. VT < VC > VA

## Slide 9: Micro Hole and Strip Plate – Reversed mode operation
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
The polarization of the strips was effective in trapping the ions. 2 orders of magnitude reduction was measured.
A large drop on the gain was also recorded. VAC = -140 V (Ar/10% CH4 at atmospheric pressure)

## Slide 10: Micro Hole and Strip Plate – Reversed mode operation
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Standard Cascaded Electron Multiplier
Electric Field Optimization
IBF = 0.5% at a gain of 104.
50 ions/primary electron

## Slide 11: Micro Hole and Strip Plate – Reversed mode operation
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Standard Cascaded Electron Multiplier
Electric Field Optimization
IBF = 0.5% at a gain of 104.
50 ions/primary electron
“Reversed” MHSP
Trapping of ions at the strips of the MHSP
IBF = 0.06% at a gain of 104.
6 ions/primary electron
Ar/CH4
IBF is dependent on gain

## Slide 12: The Photon Assisted Cascaded Electron Multiplier
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Standard Cascaded Electron Multiplier
Electric Field Optimization
IBF = 0.5% at a gain of 104.
50 ions/primary electron
“Reversed” MHSP
Trapping of ions at the strips on the MHSP
IBF = 0.06% at a gain of 104.
6 ions/primary electron
PACEM
Secondary scintillation emitted by the MHSP
propagates the signal in the cascade
IBF independent on GAIN
2 ions/primary electron (CF4)
Ar/CH4
Noble gases and CF4

## Slide 13: The Photon Assisted Cascaded Electron Multiplier
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Standard Cascaded Electron Multiplier
Electric Field Optimization
IBF = 0.5% at a gain of 104.
50 ions/primary electron
“Reversed” MHSP
Trapping of ions at the strips on the MHSP
IBF = 0.06% at a gain of 104.
6 ions/primary electron
PACEM
Ar/CH4
Noble gases and CF4
IBF is no longer dependent on gain
The gain bellow the Ion Blocking Grid can be increased without any influence of the total IBF
Voltages do not increase along the cascade: the ion blocking grid is at ground.
Focus is now on minimizing the IBF of the first stage while maximizing the optical gain
Secondary scintillation emitted by the MHSP
propagates the signal in the cascade
IBF independent on GAIN
2 ions/primary electron (CF4)
Only the first stage contributes to the IBF

## Slide 14: The Photon Assisted Cascaded Electron Multiplier
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
PACEM with 2 MHSP : Voltages on top MHSP are the same as on the bottom.
The second stage can be composed by any kind of gaseous electron multiplier (GEM, GEM cascade, MHSP, COBRA)
No loss of information between stages.
IBF and gain are independent!

## Slide 15: The Photon Assisted Cascaded Electron Multiplier
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Xenon
7 ions per primary electron at an optical gain of 10 (3x3 cm2 photocathode). EDrift = 0.5 kV/cm
Polarization of the strips leads to an optical gain increase by 2 orders of magnitude
2 ions per primary electron at an optical gain of 10 (3x3 cm2 photocathode). EDrift = 0.1 kV/cm

## Slide 16: The Photon Assisted Cascaded Electron Multiplier
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
CF4
2 ions per primary electron at an optical gain of 10 (3x3 cm2 photocathode). EDrift = 0.1 kV/cm
12 ions per primary electron at an optical gain of 10 (3x3 cm2 photocathode). EDrift = 0.5 kV/cm

## Slide 17: The Photon Assisted Cascaded Electron Multiplier
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Xe - CF4 mixtures
2 ions per primary electron at an optical gain of 10 (3x3 cm2 photocathode). EDrift = 0.1 kV/cm

## Slide 18: Zero Ion Back Flow
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Standard Cascaded Electron Multiplier
Electric Field Optimization
IBF = 0.5% at a gain of 104.
50 ions/primary electron
“Reversed” MHSP
Trapping of ions at the strips on the MHSP
IBF = 0.06% at a gain of 104.
6 ions/primary electron
PACEM
Use of secondary scintillation on MHSP
To propagate the signal
IBF independent on GAIN
2 ions/primary electron
ZERO IBF
NO ions produced in the proportional scintillation region
0 ions/primary electron
(only primary ionization)
Ar/CH4
Noble gases and CF4
Noble gases

## Slide 19: Zero Ion Back Flow
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Only the primary ions are present on the conversion region. The primary electron cloud is amplified and no secondary ions return to the conversion region.
Proportional scintillation region:
Primary electron cloud drifts under an electric field below the threshold for ionization. No secondary charges are created. Secondary scintillation is produced and emitted isotropically.
Gaseous Photomultiplier:
Collects a fraction of the secondary scintillation.

## Slide 20: Zero Ion Back Flow
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
Extraction field plays a critical part on ion back flow suppression as well as in photo-electron extraction

## Slide 21: Zero Ion Back Flow
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
The optical gain is strongly dependent on the gas purity.
Detector was operated in sealed mode, with the purification done by circulating the gas through non-evaporable getters.
Some geometrical factors that influence the optical gain:
  proportional scintillation region size (current setup was 6 mm). Increase to 10 mm would increase the optical gain from 4 to ~ 6
  Larger solid angle (photocathode area was was 28x28 mm2)

## Slide 22: Conclusions
18th RD51 Collaboration Meeting, 12th - 16th of September 2016 Aveiro, Portugal
The presence of ions is an inevitability in gaseous detectors. The higher the gain and rate, the more problematic they become.
MPGD provides us several solutions to decrease the IBF to acceptable values.
 | GEM Cascade | Reversed MHSP | PACEM | ZERO IBF
Current Status | 4 GEM - ALICE upgrade | . Successful operation of Visible Sensitive GPM | Novel Solution | Operation in noble gases and Mixtures
Strengths | GEM are solid and well established technology | Extra strips makes it versatile | . Gain can be increased without affecting IBF . Low Voltages | IBF at the level of the primary ionization
Limitations | . IBF dependent on GAIN | . IBF dependent on GAIN . Not yet produced in large areas | Noble gases/CF4 mixtures (purification) | Noble Gases (purification)
Future Developments | Misalignment / different pitch GEM | Large Area MHSP | Double PACEM (?) | Test beam