## Slide 1
DEVELOPMENT OF MEASURING SYSTEM FOR ENVIRONMENTAL CONDITIONS BASED ON ARDUINO YUN/MEGA AND WIN_CC OA
George Bakas
Giannis Papakrivopoulos
Yorgos Tsipolitis
National Technical University of Athens

## Slide 2
Introduction
Arduino
Sensors
OPC Server
WinCC_OA
Conclusions

## Slide 3: Introduction
The project aims to develop a low cost system, capable of measuring the environmental parameters using commercial sensors
The Arduinos Mega and Yun microcontrollers were used
WinCC_OA was used for data monitoring and elaboration
Integration of the system into the RD51 SLow Control SYstem

## Slide 4: Arduino
Microcontroller  Input and Output pins
Variety of Arduino Boards (Mega, YUN, etc)
Arduino Mega:
  54 digital pins
  16 analog pins
  USB port , power jack
  5,5V , 3.3V GND
  The Arduino Mega  used with Ethernet Shield
  Ethernet shield: allows to connect with Internet via RJ45 connection

## Slide 5: Arduino
Arduino Yun:
  13 digital pins
  6 analog pins
  USB and micro USB connection
  WiFi and Ethernet connectivity
Arduino YUN
Arduino Mega

## Slide 6: Sensors
Total of 5 sensors was used
  1 Digital Temperature, Humidity and Pressure Sensor
  (BME280)
  2 Digital Temperature and Pressure Sensors (BMP085, MPL3115A2)
  1 Analog Pressure Sensor (MPX5700AP)
  1 Digital Temperature and Humidity Sensor (DHT22)

## Slide 7: BME280 Sensor
Digital Sensor: Pressure, Temperature and Humidity
High Precision: Temperature±0,5 C, Pressure ±10 Pa , Humidity ±2%
Low Cost: ~14 Euros/ sensor
Communication via I2C Protocol and SPI

## Slide 8: BMP085 Sensor
Digital Sensor: Pressure and Temperature
High Precision: Pressure ±1 mbar, Temperature ± 1 0c
Communication via I2C protocol
Here we used the Atmel AVR4201 board

## Slide 9: MPL3115A2 Sensor
Digital sensor pressure and temperature
High Precision: Pressure ±4 mbar, Temperature ± 1 0c
Communication via I2C protocol
Here we used the Xtrinsic Sensor Board by Element14

## Slide 10: MPX5700AP
Analog Pressure Sensor
Accuracy: ±2,5% VFSS
5v Operating voltage
Transfer function, conversion voltage
to pressure

## Slide 11: DHT22 Sensor
Digital Temperature and Humidity Sensor (also analog connection)
High Precision: Temperature: ±0,5 0C , Humidity: ±2%
Long-term stability, long transmission
distance
5V Power Supply

## Slide 12: OPC Protocol
Open Platform Communication (Server/Client)
OPC DA  read and write data in real time
Ability to use multiple Arduino boards of any type simultaneously
Serial, Wifi and Ethernet Communication
Communication with Arduino via OPC.h library

## Slide 13: WinCC_OA
SCADA (Supervising Control and Data Acquisition)
A tool for the development of control system:
  Database
  GEDI (Graphics Editor)
  Control Scripts
  Connection with Hardware devices (OPC)
  JCOP (Joint Controls Project) framework

## Slide 14: Conclusions for Arduino/Sensors
DHT22 sensor used for relative measurements
BME280 used at last as a main sensor for the project
  Pressure, Temperature, Humidity data given by 1 sensor
  Low cost and easy connection with Arduino (digital and I2C)
Final 2 Configurations
  Arduino YUN: using WiFi connection
  Arduino Mega: using Ethernet connection
Arduino YUN memory very small  limited abilities

## Slide 15: Data 5/2016 during test beam
Arduino YUN
LCD Screen
BME280
DHT22

## Slide 16: WinCC_OA Panels Online

## Slide 17: Data offline during May/June TB

## Slide 18: Data offline during May/June TB

## Slide 19: Data offline during May/June TB

## Slide 20: Printed Circuit Board
The 2 boards were designed with EAGLE by Cadsoft
2 Boards used:
  ArdEnvino Main Board equipped with
    Pins for Aruino Mega or YUN Connection
    Pins for LCD Screen
    4 RJ45 adaptors that connect with smaller boards (sensor boards) and 1 RJ45 for external connection
  ArdEnvino sensor board equipped with
    1 BME280 Sensor (Temperature, Pressure, Humidity)
    1 DHT22 Sensor (Temperature, Humidity)
    1 RJ45 Adaptor so that the sensor board is connected to the main board

## Slide 21: ArdEnvino

## Slide 22: ArdEnvino

## Slide 26: WinCC_OA Panels (August 2016 Test Beam)

## Slide 27: WinCC_OA Panels (August 2016 Test Beam)

## Slide 28: WinCC_OA Panels (August 2016 Test Beam)

## Slide 29: WinCC_OA Panels (August 2016 Test Beam)

## Slide 30: WinCC_OA Panels (August 2016 Test Beam)

## Slide 31: Conclusions
A low cost system capable of monitoring the environmental parameters in several places using commercial sensors
Support of two Arduino Types (Mega and YUN)
Support of 2 sensors measuring pressure, temperature and humidity
Completely dynamic
The System has been fully integrated in the RD51 SLow Control SYstem and is available for any member of RD51
A RD51 note will be ready soon

## Slide 32: Future of ArdEnvino
The Arduino YUN although was ideal at the beginning because of the WiFi connectivity  memory problems  Arduino Mega only
Plans for ArdEnvino v 2.0 with Arduino Mega and WiFi Shield
  No cables (WiFi connection with OPC)
  Memory
Plans for similar system using Raspberry Pi