## Slide 1: CHARM FLUKA simulations
Rubén García Alía

## Slide 2: Simulation flow
Input Definition (geometry, scoring, physics, biasing…)
Running simulations (CPU intensive)
Process Output
Report Output (+ benchmark with measurements)
Long process, therefore it is essential to centralize the requirements at the right
moment (i.e. now!). Angelo is central contact point.

## Slide 3: FLUKA tabulated values
Used to provide the integrated dose and fluence values to the users
Referred to per proton on target and therefore independent of total number of protons on target (e.g. both SEC1 integral counts and calibration factor)
Concerned values: Dose [Gy/pot]; HEH, HEHeq and 1 MeV neq (/cm2/pot); R-factor
Tabulated for different configurations (three targets * two/three shielding layouts) and locations (1-13 + new “standard” locations)
To be benchmarked against measurements (Note: as referred to per pot, uncertainty in the number of pot is to be included in experimental value)

## Slide 4: FLUKA tabulated values (II)
Presently, the reference for the 2015 tabulated values are the online tables from Adam (+ step 2 correction for dose)
An ATS report has been submitted containing these values and will also serve as a document reference
When considering the step 2 dose corrections (details in Matteo’s presentation) the overall agreement with the measurements for TID, HEHeq and 1 MeV neq is within ±20%
Will be updated for 2016.1 run (however no dramatic changes are to be expected)

## Slide 5: Version 2016.1 – update overview (not complete!)
geometry:
  update of overall distances (already tackled by Joao, Iacopo and Angelo, and to be completed with 3D laser map)
  new table near target (+ typical large objects which might be placed on it, though this should be avoided not to alter the field)
  new permanent EPC test station
scoring:
  "standard" scoring in EPC test station
  scoring at table near target with fine resolution + LFcable and optical fibre
  location near patch panel, in line of sight of the target
  locations in corridor where control electronics might be placed during irradiations
  area in and around Montrac for position in beam line, both with and without target