## Slide 1: Beam loss monitor development at the ESRF Friederike EWALD ESRF
  ESRF – European Synchroton Light Source / Grenoble / France
  6 GeV electron energy
  200 mA stored current
  844 m circumference
  32 cells
  28 insertion device beamlines
  16 bending magnet beamlines

## Slide 2
~ 16 million 6 GeV electrons/s LOST
Reasons for beam loss:
Touschek scattering
Vacuum quality
(overal vacuum level, leaks, ...)
Limited apertures
(small undulator gaps, misaligned vacuum pipes,...)
Beam missteering
200mA stored
lifetime ~ 60hrs

## Slide 3: Loss monitors in one ESRF storage ring cell
Dipole magnets (bending magnets)
Quadrupoles
Sextupoles
Insertion devices (undulators, wigglers)
32 cells build the whole storage ring
==> 64 Perspex/PMT BLDs
64 ionisation chambers
---------------------------------------
128 beam loss measurements
Perspex rod + PMT
at beam height
shielded in 1 cm lead
~ 80 cm x 8 cm Ø
Ionisation chambers
placed on the floor
heavy lead shield
~ 30 x 50 x 20 cm

## Slide 4: Outline
What happens when a 6 GeV electron is lost?
How can we detect such losses?
The new generation of beam loss detectors chosen for the ESRF
Results obtained with prototypes installed in the storage ring
1

## Slide 5: Beam loss ? What happens when we loose a GeV electron?
ELECTRON
Photonuclear
reactions
etc.
e-
e-
e+
e-
g
n
MATTER (vacuum vessel, magnets,...)
e+
e-
g
g
g
e-
e-
n
g
Bremsstrahlung
Pair
production
g -/ PARTICLE – SHOWER

## Slide 6: Available particles and (some) detection methods
e.g. pure quartz
Converter shapes: ○ rod
○ fiber
Light  electrical output : ○ photomultiplier tube (PMT)
  ○ diodes, MPPC
(organic)
scintillators
e.g. EJ200
see
presentation of
J. Marroncle
conversion into
visible light
Cherenkov
radiation
Neutrons
g – photons
Electrons
Ionisation chambers :
gas or solid state
(pin diodes, CVD)
conversion into
electrical signal

## Slide 7: Scintillator versus Cherenkov radiation
Cherenkov-radiator versus Gamma-scintillator
Quartz-glass EJ-200 or BC-408
no need for Pb shielding - high light yield
since immune to X-rays (?) - cheap material
therefore : - less volume
- less weight
- compact
- low light yield needs Pb shielding
- more expensive - bulky & heavy (?)
PRO :
CONTRA:
We choose: BLD based on a small EJ-200 rod,
a small PMT (8mm window),
2mm of Pb shielding

## Slide 8: Test of sensitivity of different geometrical configurations
1
PMT
EJ-200
PMT
EJ-200
g – source : Cesium-137 (700 keV g )
Aluminium reflector around scintillator
Scintillator:
different sizes
Signal strength read out
Aluminium housing
Hamamatsu PMT

## Slide 9: Test of sensitivity of different geometrical configurations
Chart: 
| 21 | 83 | 100 | 100 | 115
without reflector | 22 | 52 | 41
with reflector | 33 | 100 | 146 | 25 | 69
Chart: 
| 21 | 83 | 100 | 100 | 115
without reflector | 22 | 52 | 41
with reflector | 33 | 100 | 146 | 25 | 69
PMT
EJ-200
PMT
EJ-200
PMT
EJ-200
PMT
EJ-200
PMT
EJ-200
L =130 mm
Ø = 22mm
tapered
L =100 mm
Ø = 22 mm
not polished
L =100 mm
Ø = 22 mm
L =100 mm
Ø = 20 mm
L =100 mm
Ø = 8 mm

## Slide 10: New ESRF beam loss monitors
1
Scintillator
PMT
Connectors SMA & RJ-25
Power-supply & gain-control
BLD-signal
BLD : aluminium housing 200 x 25 x 25 mm
BLM
(Libera-BLM)

## Slide 11: New ESRF beam loss monitors
1
Scintillator
PMT
Connectors SMA & RJ-25
Power-supply & gain-control
BLD-signal
Scintillator :
EJ-200, 100 x 22 mm rod wrapped in reflective Al-foil
PMT:
Hamamatsu H10721-110
8mm active photo-cathode
- powered (+5 V) & gain-controlled from BLM
- 3 orders of magnitude with 0-1V gain-control
- can drive 50 W load
BLM :
- 4 independent channels
- 14 bit ADCs, +/- 5 V to +/- 150 mV full-scale (adjustable)
- >10 MHz bandwidth
- 50 W or HiZ input
- PoE
- Embedded Tango-DS

## Slide 12: BLD “test bench” in the ESRF injection zone
Septum
Scraper
Dipole
Injected beam
4 (5) different BLDs
Crotch
absorber
Quadrupoles / Sextupoles
stored beam
Do the BLDs only see e- losses or also bending magnet radiation ?

## Slide 13: Do the BLDs only see e- losses or also bending magnet radiation ?
1
60 hours lifetime
 16 million 6 GeV electrons/sec lost
= ~ 2·10 -11 Watt/meter
(with 844 m of circumference)
Crotch absorber takes many kW from synchrotron light, ( Ecrit ~ 20 keV )
a tiny fraction of that power converted into
back-scattered photons can create a
dominant signal in the BLD
Pb-shielding necessary to suppress
up to 200 keV X-rays
Stored current = 200 mA :
Septum
Scraper
Dipole
Crotch
absorber
Quadrupoles / Sextupoles
stored beam

## Slide 14: 5 different BLDs tested for immunity against X-rays
10 mm Pb shielding = reference  no X-rays
EJ200 , 2 mm Pb, close to crotch
EJ200, 2mm Pb, middle of dipole
Cherenkov (ESRF)
Cherenkov (DESY)
0 mA
200 mA
BLD signals normalized [a.u.]
Time /a.u.
2 mm of Pb shielding is only enough when the
BLD location is chosen in a region with low
synchrotron radiation level !!

## Slide 15: BLD “test bench” in the ESRF injection zone
Septum
Scraper  closed internally
Dipole
Injected beam
4 (5) different BLDs
Crotch
absorber
Quadrupoles / Sextupoles
Turns
1, 2, 3 etc.
“ Strong & Fast ” losses at injection (top-up)
1) done at each top-up
2) obtain time-resolved loss-patterns, at ADC-rate or T-b-T-rate (or slower)
3) vary numerous injection parameters, and see the effects on these loss-patterns
4) purpose : asses the BLD system on coping with (extreme) strong levels of losses

## Slide 16: ADC buffer at injection of 5 bunches into the storage ring
Typical ADC data, 6 turns with 5 bunches injected:
Strongly varying loss level from turn to turn
Data-rate is ADC : 125 MHz = 352 samples/turn = 22 samples between bunches
ADC sample number
ADC signal mV
1 Turn

## Slide 17: Time-resolved losses of injected beam at different RF phases :
Data-rate is T-b-T ( 355 kHz, 2.8 us)
Orbit turn number
Loss signal [a.u.]
nominal phase phase +30deg
“betatron”-losses
“synchrotron”-losses : increase when out of phase

## Slide 18: Time-resolved losses of injected beam at different RF phases :
nominal phase phase +30deg
Data-rate is ADC ( 125 MHz, 8 ns )
80 ms
“betatron”-losses
“synchrotron”-losses
Loss signal [a.u.]

## Slide 19: Time-resolved losses of injected beam at different RF phases :
“synchrotron”-losses
nominal phase phase +30deg
Data-rate is ADC ( 125 MHz, 8 ns )
Loss signal [a.u.]
80 ms

## Slide 20: “ Single-electron ” losses by dumping injector’s dark current into scraper
profile of
shot #10
other extreme : high sensitivity
 Single electron detectivity
Any lost electron will create a different shower, and thus signal strength.

## Slide 21: Beam loss measurements in the vicinity of in-vacuum undulators
Magnet arrays of in-vacuum undulators are very close to the electron beam :
The ‘gap’ can be as small as 5mm
        Gain in flux
but: scattered electrons now get lost on these magnets
 Degradation of the magnets over less than a few years
This can be a real problem in rings with smaller beam-sizes (like ESRF-EBS …!)
more scattering = less lifetime = more losses . . .
less lifetime is compensated with more frequent refills  top-up
But any damage to In-Vacs is only felt after it is done
Solutions :
Add special & dedicated scrapers-collimators in that ring
the scattered electrons get lost there
Improved monitoring of losses to verify that these in-vacs are indeed protected.

## Slide 22: BLD installation at in-vacuum undulator
BLD #1
BLD #2
e-beam
In-Vacuum undulator

## Slide 23: ADC data from 2 BLDs near in-vacuum undulator, at 2 different injections
Red = up-stream detector
Blue = down-stream detector
one shot
another shot
1 Turn
Registered losses depend on detector position.
Losses are not the same at each injection shot.

## Slide 24: Beam loss at undulator with closed gap at injection
gap at 9 mm
gap at 7 mm
loss at injection turn
losses with
synchr. freq. signature
Turn number

## Slide 25: Plans at the ESRF for adding a new BLM system now
Presently we have already :
  64 old BLDs (scintillator + PMT) that are heavy & big
with slow read-out electronics (<1Hz)
  64 Ionization chambers : even heavier, very big
128 BLDs of the new type and 40 BLM electronics
will be installed at strictly regular positions (4/cell)
32 more units will be installed at points of interest like
some in-vacuum IDs, injection zone, close to scrapers etc.
Commissioning of the new BLD/BLM system will start in early 2017.
In 2019/20 all of these devices will be transferred to the new storage ring.
The experience acquired in the present ring will be valuable for judging data taken
at the start-up of ESRF-EBS.

## Slide 26: Acknowledgements and References
The BLD/BLM development as presented here is a collaboration between the ESRF (Kees Scheidt, Nicolas Benoist, Fouhed Taoutaou, Francis Epaud) and Instrumentation Technologies.
For a more detailed description of the BLD/BLM system:
K. Scheidt, F. Ewald, P. Leban et al. “Optimized beam loss monitor system for the ESRF”, IBIC2016 proceedings, MOPG20