## Slide 1
LA3NET Novel Accelerators Workshop, Paris 2016
Development of Diagnostics
for PW and multi-PW lasers
Jaroslav Moravec
FOTON, s.r.o.

## Slide 2
LA3NET Novel Accelerators Workshop, Paris 2016
Why ? What ? Who ?
FOTON, s.r.o.
ELI Beamlines
PW diagnostics + Challenges
Institute of Physics, Prague
Bedrich Rus

## Slide 3: FOTON, s.r.o.
founded 2000
Czech private company (LTD)
Development and manufacturing of special electronic devices
Studénka 1 509 01 Nová Paka Czech Republic www.fotons.cz

## Slide 4: „From system design to k delivery of final product …”
Founded 2000
SME
PIC (FP7) : 968991880
Special innovative firm
R&D + manufacturing
Design and development
Manufacturing
Testing
Installation
Service
Precision HV supplies
Micropositioning
Plasma diagnostics
Industrial control and measurement
Vacuum controllers
Complex services for R&D

## Slide 5: Company history
2000 FOTON founded, instrumentation for PALS
2001 X-ray laser instrumentation
2002 diagnostics for tokamaks
first high voltage supplies
Multidrive16
first exports
2007 Škoda Auto a.s.
2008 Joint Institute of Nuclear Research, Dubna, RF
2010 ELI – vacuum system
2011 LA3NET (Liverpool)

## Slide 6: Products overview
More than 140 prototypes during 15 years
High voltage supplies
Micropositioning
Optoelectronics
High temperature plasma diagnostics
Special systems
Current and voltage power supplies
Industrial control systems
Vacuum controllers
nA-100s A uV-10s kV
uW-kW UV-IR

## Slide 7: High voltage power supplies
Low – middle – high power, voltage up to 20kV (60kV)
HV 8002
HV 5000+
HVS 04
HVG 2000

## Slide 8: Micropositioning
System Multidrive 16+
Multidrive 16+

## Slide 9: High temperature plasma diagnostics
Signal processing, generators and controllers for experiments
HPD 4.1
DLS 08

## Slide 10: Vacuum control systems
High reliability control systems (HW, SW) for vacuum pumping
VCU 2000
ASU 2009

## Slide 11: Voltage and current power supplies
DC – AC – waveform – programmable, up to 500 A, peak power 40 kW
Galva 2001

## Slide 12: Automation and industrial process control
Industrial projects:
Large experiments:
Automatic pressure station
Particle accelerator

## Slide 13
Do you need a solution ?
…contact FOTON
You know, WHAT, but you don’t know HOW?
Have you not power / capacity?

## Slide 14
ELI-Beamlines: European laser research facility

## Slide 15
ELI-Beamlines aerial view – 2011 artist’s impression
Laser building
Offices and admin building
Laboratories
HiLASE

## Slide 16
July 2015: building opened for technology installation

## Slide 17
ELI-Beamlines master scheme: 4 laser systems

## Slide 18
ELI-Beamlines will use new concepts of heat extraction from the laser gain medium to achieve high repetition rates
Courtesy T. Metzger (MPQ Garching)
THIN DISK: active mirror
kHz rep. rates
~kW average power
MULTISLAB:
face cooling by He gas
10 Hz rep. rates
> kW average power
MULTISLAB:
face cooling by liquid
up to 10 Hz rep. rates
High energy (>kJ) lasers
Used in L1
Used in L2 and L3
Used in L4

## Slide 19
ELI-Beamlines laser systems: L1 / L2 / L3 / L4
L1
L2
L3
L4

## Slide 20
Beamline | L1 | L2 | L3 | L4
Peak power | >5 TW | PW | PW | 10 PW
Energy in pulse | 100 mJ | 15 J | 30 J | 1.5 kJ
Pulse duration | <20 fs | 15 fs | 30 fs | 150 fs
Rep rate | kHz | 10 Hz | 10 Hz | 1 per min
Supplier | Pump lasers from commercial suppliers | External supplier / developer | Major contractor | Major contractor
ELI-Beamlines development | Short pulse chain developed in house | Specific technology development | Cooperative development of subsystems | Cooperative development of subsystems
 | Development of diagnostics of short pulse (15 fs to ps) laser pulses |  |  | 
ELI-Beamlines lasers: in-house development + suppliers

## Slide 21
Example of ELI-Beamlines laser technology: L1 picosecond compressor

## Slide 22
L3-HAPLS laser: cooperation with Lawrence Livermore National Laboratory (USA)
HAPLS = High Repetition Rate Advanced Petawatt Laser System
developed for ELI-Beamlines by LLNL
PW compressor & diagnostics
developed by Inst. of Physics
Ti:sapphire gas-cooled power amplifier
Front end: Ti:sapphire oscillator, stretcher, pulse cleaner, pre-amplifiers
200 J / 10 Hz Nd:glass gas cooled DPSSL pump laser
Ti:sapphire pre-amp pumped by DPSSL
Pump laser front end
PW compressor
Short pulse diagnostics package (SPDP)

## Slide 23
Main challenges for development of PW laser diagnostics
High repetition rate - The diagnostics must operate at high repetition rates (1 kHz for the L1 laser, and 10 Hz for the L2 and L3 lasers) and data has to be retrieved & stored
On-line measurement capability - Laser pulse parameters have to be provided “on the shot”, i.e. without deviating entire laser output to the diagnostics (deviating of attenuated laser output to diagnostics is a widely used approach in current diagnostics) - Diagnostics of the output laser pulses has to provide machine safety functions, e.g. stopping the laser if any early signs of damage of optics are detected
Automation - The diagnostics package must be a “turnkey” system and must be integrated into control system of the laser
Reproducibility and reliability - The diagnostics must provide same data over extended period of time, without need for readjustments and/or for realignment

## Slide 24
2) Dark field
Real-time damage detection
3) Polarization
measurement
Spatially / spectrally resolved
polarization
1) Near & Far field
+ Wavefront
Intensity profile pointing, wavefront
Real-time
changes detection
detector:
25x25px
AOTF
λ/2
ND
CCD
Example: automated spatial diagnostics developed
3 intentional
damage spots

## Slide 25
Dark field image: automated beam spatial diagnostics

## Slide 26
Specifications
Pulse duration:
12-70 fs
Required energy:
>10 μJ
Resolution:
up to 1.7 fs (4.4 μm px)
Repetition rate:
up to 20 Hz
Attenuation:
fully variable (0-max)
Polarization:
linear
Delay line
CCD camera
Nonlinear crystal
Incoming beam
67 fs
raw data
Temporal diagnostic: single-shot autocorrelator pulse length
Development of system with LabView real-time (LVRT) drivers and SW

## Slide 27
THG
Incoming beam
SHG
Spher.
mirror
BS
Delay stage
PMT
Specifications
Dynamic range:
>1010 (100 dB)
goal 1011 (110 dB)
Scanning range:
up to 200ps
Required energy:
>100μJ
Repetition rate:
Slow - scanning
(depends on resolution)
Polarization:
linear
Third-order autocorrelator (contrast measurement)
Development of core functions on LabView real-time drivers
& SW & library for processing

## Slide 28
Spatial diagnostics
Near-field camera (beam profile, alignment)
Far-field (wavefront, alignment)
Wavefront sensor (wavefront )
Polarization module (spatially & spectrally resolved)
Dark-field (damage recognition)
Power/energy, spectrum
Full aperture power meter (absolute meas. & calibration)
Pulse shot-to-shot energy (diode + integrating sphere)
Pulse optical spectrum
Temporal diagnostics
SHG autocorrelator (pulse duration)
SPIDER / Wizzler (pulse duration, spectral phase)
3rd order correlator (contrast measurement)
Fully automated, 10 Hz real time operation
Signals for feedback and alignment
Pulse / beam diagnostics at the output of the final amplifier (before compression) and diagnostics of the compressed pulse
Example: Integrated short pulse diagnostic package

## Slide 29
Laser HMI
Facility interface
RT node
FPGA
I/O
I/O
Sequencer
Critical and/or fast feedback is local to node
Analogue and digital I/O
EPICS Integration layer
Machine protection
PLC
Failure signals
Facility interface
FPGA
State & configuration control
Status & monitoring
Serial devices
Camera-based diagnostics
Local post-mortem data buffer
Transition requests, operating mode
Trending, archiving, shot reports
Laser health monitoring
Interlock permissions
Device layer
Services layer
Modbus network
Diagnostics visualisation
Real-time
embedded controller
Diagnostics integration with laser control system